Y-MQ-320/420 Die Cutting Machine

1. Main Technical Parameter:

| Model | Y-MQ-320 | Y-MQ-420 |
| --- | --- | --- |
| Die cutting speed: | 20-220times/min | 20-180times/min |
| Max. Unwinding diameter | 450mm | 650mm |
| Max. Web width | 320mm | 420mm |
| Max. Die cutting width: | 300mm | 400mm |
| Max. Die cutting length | 290mm | 400mm |
| Precision of registration | ±0.01 | ±0.01 |
| Total power: | 2.5kw | 3.0kw |
| Power supply voltage: | 380v+/- 10% | 380v+/- 10% |
| Machine weight | About 2300kg | About 2500kg |
| Dimensions | 2600x950x1400mm | 2600x1050x1400mm |

2. Characteristics:

This is a kind of flat-bed die cutting machine with high precision. The paper-going is controlled by servo motor. The three photoelectric eyes do the web-guiding job. die cutting, laminating, waste rewinding, paper sheeting or rewwinding can be finished in the process, the machine is applicable to die cut self adhesive labels, dacron film labels and laser anti-false labels, it is an ideal auxiliary of flexo printing machine, screen printing machine, relief printing machine and so on.

3. Price list:

Standard configurations (Y-MQ-320): 11,500USD(FOB Ningbo)

Standard configurations (Y-MQ-420): 14,000USD (FOB Ningbo)

4. Optional devices for extra payment:

a). Hot stamping:

for Y-MQ-320-----800USD

for Y-MQ-420-----900USD

b). Punching: 900USD

5. Delivery time: 30 days

6. Payment terms: 30% deposit in advance, and 70% balance payment before shipment

7. Following photo for your reference