ICESTA QUOTES

FOR 2T BLOCK ICE MACHINE

- Customer’s Details

Comany name:

Contact Person:

Email:

tél:

- ICESTA Quote Reference Number: ICT-MDG -150812-01

- What is included in the quote

  - 1 No. of 1T/24H Block Ice Machine

- Detailed Spec Sheet

Parameters of 1T Block Ice Machine

| NO | Parameter | IB1T-R2W |
| --- | --- | --- |
| 01 | Ice Capacity | 1t/24h |
| 02 | Compressor | Bitzer |
| 03 | Refrigeration Capacity (KW) | 18 |
| 04 | Evaporating Temp (℃) | -15 |
| 05 | Condensing Temp (℃) | 40 |
| 06 | Total power (KW) | 6.77 |
| 07 | Compressor Input Power (KW) | 4.74 |
| 08 | Power of cooling tower motor (KW) | 0.18 |
| 09 | Power of cooling water pump (KW) | 0.75 |
| 10 | Pump for evaporator | 1.1 |
| 11 | Power Supply | 3P/ 380V/ 50Hz |
| 12 | Refrigerant | R22(or R404) |
| 13 | Freezing Cycle | 8 Hour |
| 14 | Freezing Times /day | 2 |
| 15 | Standard Ambient Temp (℃) | 30 |
| 16 | Max. Ambient temp (℃) | 40 |
| 17 | Standard Water Temp (℃) | 20 |
| 18 | Ice temp. (℃) | -10 |
| 19 | Ice Mould(unit) | 20 |
| 20 | Ice block weight (KG) | 25kg |
| 21 | Dimension of ice (mm) | 390*120*600 |

Note: The above data is for your reference and is subjected to final design.

- Main Component List

Details of 1T Block Ice Machine

| No. | Component | Qty(PC) | Brand | Remark |
| --- | --- | --- | --- | --- |
| 01 | Compressor | 1 | Bitzer/ (Or Bock) |  |
| 02 | Solenoid Valve | 1 | Danfoss |  |
| 03 | Brine water tank | 1 | ICESTA |  |
| 04 | Electric control panel with Simens PLC controller and touch screen monitoring | 1 | ICESTA |  |
| 05 | Ice Moulds | 20 | ICESTA |  |
| 06 | Expansion Valve | 1 | Danfoss |  |
| 07 | Pressure Control | 2 | Danfoss |  |
| 08 | Circuit Breaker | 1 | Schneider |  |
| 09 | Contactor | 3 | Schneider |  |
| 10 | Thermal Relay | 3 | Schneider |  |
| 11 | Oil Filter | 1 | Fasike |  |
| 12 | Condenser | 1 | YiLian (China) |  |
| 13 | Ball Valve | 1 | Danfoss |  |
| 14 | Filter Dryer | 1 | Danfoss |  |
| 15 | Cooling tower | 1 | Lingdian(China) |  |

- Photo-2T Block ice machine                           flake ice machines

Ice photo                                                                Block ice machine

The Block Ice Machine unit includes (main necessary parts):

- Bitzer Refrigeration unit and electric control system.

- Brine tank

- Ice moulds/Ice Can

- Cooling tower and water pump provided for water-cooling model.

Block Ice Machine workflow: 1, Feeding water in ice moulds inside of the brine tank.2, Salt water in brine tank cooled with refrigeration system running and salt water flow cycling, which makes the water in ice moulds frozen.3, Remove / harvest ice.

- CIF TAMATAVE,MADAGASCAR Price in US Dollar

| ITEM | Model Number | Capacity | UNIT PRICE | QTY | TOTAL |
| --- | --- | --- | --- | --- | --- |
| Block Ice Plant | IB1T-R2W | 1t/daily | US $ 5,900 | 1 | US $5,900 |
| Sea freight and insurance | US $1,800 |
| Total amount in USD | US $7,700 |
| Say FOB SHENZHEN US Dollars Seven Thousand and seven hundred Only. |

- Business Terms

    - 30% advance payment is made upon confirmation of order as deposit; 70% balance payment is paid before delivery of goods

    - Delivery Time: 25-30 days upon arrival of the advance deposit.

    - Warranty Period: 12 Month upon date of Bill of Lading

    - Documents required: Original signed Commercial Invoice and Packing List, Original Bill of Lading and Certificate of Origin.

    - Saing time: 23-25 days arrival by FCL shipment.

- Company showcase

Thanks for your reviewing and previous time.

Welcome to visit us at any time.

Best regards.