Quotation

| Our Ref No. | ICT-FR-20150827-01 | Date: August 27th, 2015 |
| --- | --- | --- |
| To: | BAMA | ICESTA Ice Systems |
| Attn: | Ms. Linda | From: Ms. Sharon |
| Email: | bama.linda@yahoo.fr | Email : sharon@icesta.com |
|  | Tel:+86- 0755-29914211 Fax: +86-0755-29914210 |
| Subject: | Quotation for 3ton block ice machine |

This program includes the following:

1) Quotation for the equipments

2) Technical parameter and components list

3) CE Certificate

4) Control system

5) Principles for Guarantee and technical support

6) Photos gallery for block ice machines

7) Working partners

1).Quotation for 3Ton block ice machines

| Item No. | Model | Capacity(T/24h) | Unit price (USD) |
| --- | --- | --- | --- |
| Block ice machine | IB3T-R2W | 3t/24h | 20,000.00 |
| Total Value in amount FOB Shenzhen |  |  | 20,000.00 |

IB3T-R2W: including refrigerating unit, cooling tower, water pump, connecting PVC pipes,connecting power line,pouring into brine to the scale mark after clean the brine tank, pouring into clean water to the scale mark after clean the ice rind (water pipes and wires not included, match one-time use solid salt)

COMMERCIAL ITEMS

| Remarks |  |
| --- | --- |
| Trade terms | FOB Shenzhen Port |
| Payment terms | Telegraphic Transfer. 30% deposit after PO confirmed. Balance paid before delivery. |
| Delivery | 25~30 days after deposit, depends on model and quantity |
| Package | Standard Wooden package |
| Validity | 30days |
| Warranty period | 1 year after B/L date. Any failure occurred within the period due to our responsibility, we'll supply you the spare parts for free, and permanent technical support & consultation all life long for the machines. |
| Note | CE approved certificate |

- . Block Ice Machine Technical Parameter

Block Ice Machine Technical Parameters IB3T-R2W

| Model Parameters | IB3T-R2W |
| --- | --- |
| Compressor Model | 4JE-15 |
| Design capacity | 3000kg/24h |
| Refrigeration capacity | 27.4kW |
| Evaporating temp. | -15℃ |
| Condensing temp. | 40℃ |
| Total input | 15.27 kW |
| Power of compressor | 11.9kW |
| Water pump of cooling tower | 1.5kW |
| Power of cooling fan | 0.37 kW |
| Water pump input | 1.1kW |
| Power of electric hoist | 0.4kW |
| Power supply | 380V/3P/50Hz |
| Water feeding pressure | 0.1Mpa－0.5Mpa |
| Refrigerant | R22 |
| Design ambient temp. | 30℃ |
| Design water inlet temp. | 20℃ |
| Ice temp. | -10℃ |
| Each weight of the block ice | 25kg |
| Dimension of ice (MM) | 390*120*600 |
| Each freezing time (H) | 11h |
| Each doff ice time (H) | 0.4h |
| Ice Machine Diameter (MM) | 1800*1000*1350 |
| Dimension of cooling tower (MM) | φ1165*1645 |
| Unit weight | 6t |
| Unit Operating Weight | 10t |

Spec. Sheet of Block ice Machine IB3T-R2W

| Item Specification | ICB3T-R2W |
| --- | --- |
| Name | Brand | Origin | QTY |
| Compressor | Bitzer | Germany | 1 |
| Anti-vibration Pipes | Hanlisi | Korea | 1 |
| Oil Separator | ALCO | USA | 1 |
| Condenser | Lianhe | China | 1 |
| Cooling Tower | Lingdian | China | 1 |
| Cooling Water Pump | Yuanli | China | 1 |
| Circulating Water Pump | South Pump | China | 1 |
| Filter Drier | Fasike | China | 1 |
| Solenoid Valve | Danfoss | Denmark | 1 |
| Expansion Valve | Danfoss | Denmark | 1 |
| Gas-Liquid Separator | Fasike | China | 1 |
| Pressure Controller | Danfoss | Denmark | 2 |
| Pressure Meter | Xianchuang | Taiwan | 3 |
| Hoisting Equipment | Icesta | China | 1 |
| Ice-pouring Equipment | Icesta | China | 1 |
| Water-supply Equipment | Icesta | China | 1 |
| PLC Controller | LS | Korea | 1 |
| Air Switch | Schneider | France | 1 |
| Contactor | Schneider | France | 7 |
| Thermal relay | Schneider | France | 7 |
| Touch Screen | Weinview | Taiwan | 1 |

3) ICESTA ICE SYSTEMS CERTIFICATION

4) ICESTA CONTROL SYSTEM (PATENT) UNIQUE INNOVATION

* Running status played live in touch-screen

* All failure record and relevant solution programmed in touch-screen for most convenience.

* Stop-time setting at will

ICESTA Control system

1). Picture one is the displaying screen of operation.

Characteristics：1. User-friendly display。

2. System failure will be indicated on screen。

2). Picture 2: Failure Display

Characteristics： The possible failures are all programmed

Into computer，operator could settle down the break-down

following systems instructions very easily.

3). Failure history record

Characteristics: The computer will record all history failure in

Its system, which will give greatly convenience to the services

man, for system checking and maintenance.

4). Picture 4: Operation hours setting

Characteristics：

A. User-friendly design，operator could set working hours,

system will stop automatically at setted time.

B. User could decide the working hours by himself, to avoid

Energy waste and save cost

5). Guarantee, technical support and failure claim procedures

- All Icesta ice systems delivered to customers are carefully examined and tested, with 72 hours trouble-free trial operation.

- All ICESTA ice systems delivered are plug-in ready and well piped.

- All ICESTA ice systems enjoy 1 year guarantee ever since B/L date.

Technical support

- ICESTA provide full technical support and training courses after equipment installation and commissioning.

- 7*24 hours phone assistance on technical support.

Failure Claim procedures

- Detailed written failure description is required by fax or by mail, indicating the relevant equipment information and detailed description of failure.

- Relevant pictures are required for failure confirmation.

- ICESTA engineering and after-sales service team will check and form a diagnosis report.

- Further trouble-shooting solutions will be offered to customers within 24 hours after receiving the written description and pictures.

- Photos gallery

7). Working partners worldwide in variety industries

Seafood Industry

Construction and concrete cooling industry

Meat processing Industry

Poultry Slaughtering

Super market and Chain stores