| Shot blasting machine |
| --- |
| equipment name and number |
| 1、device name | H type steel roller by Shot blast cleaning machine |
| 2、model | HPG2012-8 |
| equipment use and installation location |
| 1、use | Type rust steel surface treatment |
| 2、installation site |  |
| the main technical parameters |
| 1、the length of the whole | about 31m |
| 2、the height of the whole | < 6.8 meters (ground 0 above, the high is the equipment in the plant height) |
| Table height | ≤ 380mm above the ground |
| 3、load | ≤12T |
| 4、the maximum size (width * height) | 1400×2100㎜ |
| 5、maximum component size (length * width * height) | 15000×1200×2000mm |
| 6、shot blasting machine | Single linear blade, motor direct |
| Number | 8台 |
| Motor power | 11kW |
| Ejection velocity | ≥70m/s |
| 7、cleaning room |  |
| main cast chamber | 12mm steel plate, steel welding structure with the chamber body, throwing all indoor high chromium cast iron shield protection. Lining thickness is 14mm, stop splice way The arrangement of top and bottom, sides 2 shot blasting machine, shot blasting machine, side angle to 35 degrees, has good treatment effect on steel structure surface and the rib plate. |
| Throw room | Welding structure with 6mm steel plate, steel chamber body, interior to the main cast chamber 0.4 meters with NM500, δ12mm wear plate protection. The interior is provided with a rubber curtain and plates transverse curtain, prevent shot out of. |
| A sealed chamber | Welding structure with 6mm steel plate, steel chamber body, interior 4 rubber curtain and plates transverse curtain against flying out of shot |
| 8、high pressure air blowing device | The sealed chamber is provided with a high pressure wind pill device, used to purge the work-piece surface residual shot. |
| Power | 11kw |
| 9、screw conveyer |  |
| Helical gear reducer | Cycloid pin wheel reducer |
| Spiral power | Longitudinal spiral: 5.5kW Horizontal spiral: 3kW Scoop lifter spiral: 3kW |
| Recovery volume | More than 120t/h |
| 10、bucket elevator |  |
| Reducer | Cycloid pin wheel reducer |
| Power | 11kW |
| Annex | Tensioning device |
| Hopper materials | Material selection of wear-resistant material, the opening of the hopper to strengthen |
| Lifting capacity | 120t/h |
| 11、shot sand separator |  |
| Type | Fanning |
| Processing capacity | 120t/h |
| Annex | Manually adjust the setting sand curtain, curtain |
| 12、material control system | Cylinder control, manual screw plug flow setting, operation panel |
| 13、dust removal system |  |
| Form | Cartridge type automatic pulse blowback |
| Air volume | ≥11500～15500m3/hr |
| power of fan | 15kw 1set |
| Discharge mode | Outside the factory emission level |
| 14、the main cast chamber and a conveying roller | Table with all the high chromium cast iron wear-resistant sheath protection |
| The length of the main cast chamber body | 1800㎜ |
| length of the chamber body | 600㎜ |
| length of the chamber body | 2000㎜ |
| length of the Funnel length | 920㎜ |
| diameter of roller | 159㎜ |
| Conveyor speed | 0.4～4.5m/min(Frequency conversion speed regulation) |
| Roller spacing | 1040㎜ |
| 15、upper and lower conveying roller |  |
| Feeding roller length | 12000㎜ |
| Feeding roller length | 12000㎜ |
| Under the table height | Above the ground |
| diameter of roller | Φ159㎜ |
| Conveyor speed | 0.4～4.5m/min(Frequency conversion speed regulation) |
| Roller spacing | 1040㎜ |
| 16、use of abrasive | Abrasive diameter: diameter of 1.2 ~ 1.5mm, cast steel pill: steel cut wire shot ≥ 85:15 The first addition and normal operation: demand is greater than or equal to 5T |
| 17、derusting grade | Sa2.5 (GB8923-88, A, B grade steel plate in the state) |
| 18、surface roughness | Ra30~75μm（In accordance with GB1031-83） |
| 19、whole machine power | 140.9kw |
| 20、equipment noise | Wall 1 meters ≤ 75dB |
| 21、dust emissions | ≤80mg/m3 |
| Quotation: |  |
| 40’HQ *2 containers 20’GQ *1 containers |  |
| Total CIF price |  |

Production line in Party A's place after installation and commissioning, Party B shall provide the following documents:

Shot blasting machine layout                      2pcs

Shot blasting machine foundation drawing          2pcs

Wearing parts repair drawings                     2 pcs

Shot blasting machine operation, maintenance manual    2 pcs

Shot blasting machine manual                      2 pcs

Equipment electrical control principle diagram         2 pcs