Belt conveyor, position 35

Belt conveyor, position 36

Belt conveyor, position 37

Belt conveyor, position 38

No less than R100000

Belt conveyor, position 39

Working platform should be manufactured together with conveyor

| Technical characteristics / position of belt conveyor | 35 | 36 | 37 | 38 | 39 |
| --- | --- | --- | --- | --- | --- |
| Conveying capacity, t/h | 40 | 40 | 40 | 40 | 40 |
| Belt width, mm | 500 | 500 | 500 | 650 | 650 |
| Conveyor length, m | 2.5 | 6.4 | 23.7 | 16 | 11.4 |
| Belt angle, ° | 14 | 21 | 9 | 2 | 20 |
| Conveying speed, m/s | 1 | 1 | 1 | 1 | 1 |
| Bulk density, t/m3 | 1.6 | 1.6 | 1.6 | 1.5 | 1.5 |
| Loading point | From automatic cutter, position 25 | From belt conveyor, position 35 | From belt conveyor, position 36 | From automatic loader, position 29 | From belt conveyor, position 38 |
| Installed capacity (appr.), kW | 3 | 4 | 5.5 | 5.5 | 5.5 |

Dimensioning specifications are shown schematically

|  |  |  |  |  |  | 2013/03 – 1 – 1 –TX |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  | Obolsk ceramics factory CUPE. Reconstruction of workshop No. 2 with organization of production soft-mud molding ceramic bricks |
| Rev. | Qnty | Sheet | Doc No. | Sign. | Date |  |
| Deputy manager | Strashinskaya |  | 07.15 | Workshop No. 2 | Stage | Sheet | Sheets Qnty. |
| Chief project engineer | Mikulich |  | 07.15 |  | C | 1 |  |
| Principal Engineer | Suschenya |  | 07.15 |  |  |  |  |
| Executive | Chernous |  | 07.15 | Terms of reference of belt conveyor with positions 35, 36, 37, 38 and 39. | Ministry of Architecture and Construction of Belarus Orgtechstrom JSC, Minsk |
| Examined by | Kravchenko |  | 07.15 |  |  |

A1 sheet

|  | Agreed by | Agreed by |
| --- | --- | --- |
|  |  | Loginova |  | 07.15 |  |  | 07.15 |
| Orig. Inv. No. | Signature and date | Repl. Inv. No. |  | Bychkovskaya |  | 07.15 |  |  |  |
| 7197 |  |  |  | Strashinskaya |  | 07.15 |  |  |  |