YH Automatic Textile Screen Printing machine

Video Link: http://v.youku.com/v_show/id_XNDE3NzY2OTQw.html

The price for YH158/12: 53000USD,FOB,NINGBO.(8Colors,2 flash cure units and total 12Stations, max printing size: 500 x 700 mm,Max.pallet size:600*800mm)

The flash cure units can be inserted in the print station, price for extra flash unit is 830USD/SET.

Description:

YH series is our high-tech automatic textile printers. Aimed for higher production output and faster recovery of investments. Adopting automatic controller system with combination of mechanical, electrical and pneumatic control and together with screen printing principle, leading to the superior printer in any print workshop. YH series is available in 4, 6, 8, 10, 12, and 14-color models with 500×700mm maximum image area, all of which can print on T-shirts, garment materials, pant legs, paper boards, glassplates, PVC/PU boards and fabric sheets & bags etc. YH series feature servo-driven indexers, AC motor driving print heads and pneumatic lifting and lowering turntable.

Adjustable XY-coordination Pneumatic clamps hold screen frames tight and allow for quick frame loading/unloading. General benefits like independent squeegee & floodbar speed adjustments, availability for flock print, 40 degree wide range and calibrated pressure adjustments, tool-free print/flood stroke length and indexing speed control further simplify setup and reduce the unnecessary stoppage. The best aspect of YH printers include a multi-colored touch screen control center, in which all functions can be realized with easy finger-tip commands like onboard self-diagnostic and alarming system, real-time production data, job memory facility and an independent print start & print end setting that automatically stop working when reaching to the preset production data. The tool-free pop-up pneumatic pallet release and locator system means more of flexibility to the YH printers. Central off-contact adjustment on all station can be achieved synchronized through hand lever located on the control center.

Plus, the combination of safety cords and bars system eliminates risk of any trip-in accidents and the print head can be easily lift up and locked down as needed to load an flash cure or refill the ink. Two prominent skip-shirt smash buttons minimize the unnecessary print work on the empty pallet and the foot pedal switch speeds up the pallets changeover. All in all, choosing the YH series will let you achieve more unlimited opportunity.

STANDARD FEATURES

- Combined the advanced technology from home and abroad, high speed and nice looking.

- Automatic screen positioning system with precision turntables, placidly and steady running, excellent localizer.

- Every squeegee and flood blade can be operated separately by independent chopper, speed adjusted by frequency, slight air pressure.

- Imported servo motor drive system makes its running smooth, precise and quick rotation.

- Center computer controller system with multiple and interchange language.

- Three curing zones in each flash cure unit can be set independently.

- The flash cure unit can be installed in the print frame if necessary.

- Double-station indexing capability increases production output.

- Bounce switch is for skip over empty pallet or badness print to less waste.

- High-density printing is available.

TOUCH SCREEN CONTROL CENTER

1, Full colored display gives a vividly visual guide

2, an independent print start & print end setting that automatically stop working when reaching to the preset production data

3, In-line self-diagnostic and alarming system

4, Multiple (1-50) print stroke capability in each print head

5, Real-time production data

6, Zero position control

7, Test print setting turns individual print heads off/on during test print cycle

8, Loading time and flash curing dwell time control

9, Three curing zones in each in-line cure unit can be settled independently

10, Built-in UBS port for future software upgrades

12, Job memory features technical parameters restoration, making repeat production a breeze

TURNTBLE/INDEXER

1, Clockwise or counterclockwise rotation

2, Double-station indexing capability increases production output

3, Servo drive combines higher print speeds with superior smoothness, consistency, and longevity

4, Central off-contact adjustment can be adjusted precisely during production, minimizing press stoppage.

5, Precise four-point pallet leveling system

6, Pneumatic and tool-free pallet locator speeds up pallet changeover

SAFETY SYSTEM

1, Safety cords between print heads and four safety bars installed on load/unload stations ambient eliminate any trip-in accident

2, Skip-shirt smash button, located on both sides of the touch screen, allows operator to avoid printing on the empty pallets as they travel

3, Hundredth of a second indexer stop trigger time offers a strong safety guarantee

PRINT FRAME

1, Pneumatic clamps hold frames tight and allow for rapid frame loading

2, Visual reference marks every 1 degree (0-40 degree range) simplify squeegee/floodbar angle adjustment

3, Easy changeover for squeegee/floodbar

4, Availability for flock print

5, Calibrated front & rear stroke length with tool-free adjustment maximizes print flexibility.

6, Print and flood speed control, pneumatic screen frame clamping, left-and-right indexing, lifting and lowing action, print and flood holders displacement are incorporated into one membrane control panel in each print head, minimizing the setup time

Technical Parameters:

| Model | YH-158/12 |
| --- | --- |
| Print Color/Station | 4-8/12 |
| Max. Image Area | 500×700/mm |
| Pallet Size | 600×800/mm |
| Frame Size | 700×1000/mm |
| Max. Air Consumption | 8P30.44L/100mm (piston move) |
| Max. Output | 900pcs/h |
| Power | 4.4Kw |
| Each Dryer Power | 13.5Kw |
| Size | ∮5500×1850/mm |
| Weight | 3300Kg |

We also suggest you following accessary equipments:

SLZ-660 Laser Image setter

# Laser Image setter is especially designed for direct printing users. With RIP processing and multiple image setting choices inside, it can well meet users requirement of flexibility, safety, speed and low-cost.This series adopt semiconductor lasers, which has a 100,000 hours long life. And with image control technology, even if being amplified a hundred times, it can still guarantee a clear and sharp spot edge.

# Main Technical Parameters：

| Model | SLZ-660 |
| --- | --- |
| Media Size | 660mm x Unlimited (26inch x Unlimited) |
| Resolution | 1800DPI/3000DPI |
| Speed | 100m/min(1800DPI) |
| Repeatability | ±0.02mm |
| Power Supply | 220V±10%, 50/60HZ , 50W |
| Media Type | He-Ne Laser Film |
| Spot Size | 8μm |
| Operate System | PC Windows |
| Process Mode | Use roll film , Automatic Washing |
| Exposure Light | Semiconductor Laser |
| Dimention | 1800mm x 1050mm x 1000mm |
| Weight | 280 KG |

SQ Screen Stretcher:

14 Pneumatic Cylinder Clamps,

Max Stretching Size: 900*1200mm

Parameters

| Model | SQ |
| --- | --- |
| Air Pressure | 0.3-0.6Mpa |
| Max. Stretch Area | 1200×900/mm |
| Number of Screen Clamps | 14 |
| Cylinder Specification | ∮50×60/L |
| Weight | 280Kg |

SBW Series Exposure Machine

# STANDARD FEATUERS

1,  Automatic lights shutting off time can be pre-set by the operators

# 2,  Heavy-duty construction but easy to assemble/ dissemble

3,  High-powered halogen point light source offers faster but more excellent exposure result

4,  Built-in light reflector maximizes the image resolution

5,  The unique cabinet design and tabletop operation interface enable its unit to fit through a standard doorway

6,  Gas shock system let the blanket frame poping up/down being a pleasure

7,  LED timer and air pressure gauge outer display system allows for easy clear information readout

# 8,  All emulsion materials are available: direct, capillary and indirect

9,  Two safety yellow lamps features for viewing and setup indicator

10, Top vacuum environment delivers a pure intimate contact between blanket and screen.

# SPECIFICATION

| Model | SBW-1400 |
| --- | --- |
| Exposure area | 1300×1150mm |
| Frame | 1000×850mm |
| Power | 3.5kw |
| Size | 1400×1250×1080/mm |
| N.W/G.W | 140/175kg |
| Packing size | 1600* 1480* 1270MM |

SHB FILM POSITIONING & SCREEN FRAME DRYING MACHINE

Screen Frame Cleaner

SCD Tunnel IR Dryer

Suggestion size:800mm width 7000mm length of tunnel，total 8600mm

DESCRIPTION

SCD series infrared-red dryer is designed for the critical final step for screen printing system. SCD's wider belt widths and longer belt length let you accomplish a large production output, speeding up the steps to win the market. Modular infrared heat elements instead of gas & liquid heat sources is aimed to improve curing setup and provide more higher thermal power. Three built-in turbo fans operate independently as heat flow circulation, cool-down, exhaust. Plus high precision temperature controller system combining the multiple thermocouples ensure fast reach up to the stable operator-set temperature. In addition, HG features adjustable heating elements height knobs, Teflon coated fiberglass belts, heavy-duty anodized steel rollers, asbestos filled-in insulation construction and 3-phase AC belt tracking motor. The visible temperature digital display panel and automatic shut-down system when beyond the pre-set temperature led the HG to be the most affordable and efficient dryer over the current curing territory.

SPECIFICATION

| Model | SCD |
| --- | --- |
| Speed | 8m/min (Adjustable) |
| Belt Width | 800-1200/mm(Optional) |
| Max. Temperature | 200℃ |
| Tunnel Length | 4000-1200/mm(Optional) |
| Size | 5560×1320×1300/mm |
| Voltage/Frequency | 3Ph 380V/50Hz |
| Heat Power | 20-60Kw |