Quotation Sheet

| Our Ref No. | ICT-FR-20151010-01 | Date: Oct.10th, 2015 |
| --- | --- | --- |
| To: |  | ICESTA Ice Systems |
| Attn: | Peggy | From: Ms. Sharon |
| Email: | Peggy.ramet@orange.fr | Email : sharon@icesta.com |
|  | Tel:+86- 0755-29914211 Fax: +86-0755-29914210 |
| Subject: | Quotation for 2 ton seawater flake ice machine |

This program includes the following:

1) Quotation for the equipment

2) Technical parameter

3) CE Certificate

4) Principles for Guarantee and technical support

5) Photos gallery for seawater flake ice machines

6) Working partners

1).Quotation for 2 Ton seawater flake ice machines

| Item No. | Model | Capacity(T/24h) | Unit price (USD) |
| --- | --- | --- | --- |
| Flake ice machine(seawater) | IFS2T-R4W | 2t/24h | 12,535 |

- The flake ice machine includes ICESTA Unique design seawater evaporator, water-cooling condenser, electronic control system. Seawater evaporator includes ice-making can, stainless supporting frame, speed reducer, water pump.

COMMERCIAL ITEMS

| Remarks |  |
| --- | --- |
| Trade terms | FOB Shenzhen Port |
| Payment terms | Telegraphic Transfer. 30% deposit after PO confirmed. Balance paid before delivery. |
| Delivery | 25~30 days after deposit, depends on model and quantity |
| Package | Standard Wooden package |
| Validity | 30days |
| Warranty period | 1 year after B/L date. Any failure occurred within the period due to our responsibility, we'll supply you the spare parts for free, and permanent technical support & consultation all life long for the machines. |
| Note | CE approved certificate |

2). Seawater Flake Ice Machine Technical Parameter

| Model Parameter item | IFS2T-R4W bitzer |
| --- | --- |
| Compressor | 12HP |
| Daily Output | 2t/24h |
| Refrigeration Capacity(KW) | 12.67 |
| Evaporating Temp.(℃) | -25 |
| Condensing Temp.(℃) | 38 |
| Total Input Power (KW) | 8.01 |
| Compressor Power (KW) | 6.77 |
| Reducer Power (KW) | 0.37 |
| Ice Bin Water Pump Power(KW) | 0.12 |
| Condenser Water Pump Power(KW) | 0.75 |
| Power Supply | 3P/380V/50Hz |
| Feed in Water Pressure | 0.1Mp－0.5Mpa |
| Refrigerant | R404a |
| Flack ice Temp. | -5℃ |
| Thickness of Ice | 1.5mm-2.2mm |
| Standard Ambient Temp. | 25℃ |
| Standard water feed Temp. | 20℃ |
| Water Consumption (M3/h) | 0.235 |
| Feeding Tube | 1/2" |
| Net Weight of Unit | 650KG |
| Dimension of Unit (mm) | 1500*1200*1300 |