Safety Toys Testing

GT-MB01 Sharp Edge Tester

The Sharp Edge Tester is used to touch to examining a toy of position whether the existence endanger safe sharp-edged edge, belong to the test item of the toy safety.

Dimensions  290 x 190 x 100 mm ( L x D x H)

Weight      4 kg

Standards

ISO 8124-1,  EN-71-1,  ASTM F963,  16CFR 1500

GT-MB03 Small Part Cylinder

The Small Part Cylinder is the throat which uses to imitate a child under 3 years of age to test whether small article may pass or not. Belong to the test item of the toy safety. BE make into by the whole stainless steel material, the surface is turned a processing by bluntness.

Dimensions  41 x 41 x 66 mm ( L x D x H)

Weight      438 g

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-MB04 Sharp Point Tester

The Sharp Point Tester is use can touch to examining a toy of position whether the existence endanger safe of sharp-edged sharp point. Belong to the test item of the toy safety.

Dimensions   112 x 16 x 16mm( L x D x H)

Weight       800 g

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-MB06 ISO 8124-1 Accessibility Probe

Can touch A/B of stretch forward the cent two kinds of model numbers, the A model number applies the toy that the child under 3 years of age use and the B model number applies the toy that the child over 3 years of age use.

Dimensions   38.4 x 38.4 x 160 mm ( L x D x H)

Weight       450g

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-M02 EN-71-1 Toy Box Cover Durability Tester & Toy Chest Lids

Test times      0-999,999 times can be set

Test precision   0-10 time/min

Display mode   displayed by big digital liquid crystal screen

Control mode    controlled by Micro-computer automatically

Action mode    electromotion or Automatism

Test pieces      stop automatically

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-M03 ISO 8124-1, EN-71-1 Mouth Toy Endure Tester & Mouth-actuated

Box-type apparatus used in this design, through the cylinder of the reciprocating m otion of piston whistle toys, etc. move the required number of blowing, suction, observe whether the toy will blow, resulting from breathing or falling parts, resulting in infants or children the risk of testing the durability of toys.

Dimensions   700 x 380 x 550mm ( L x D x H)

Weight      40kg

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-M16 TTF Tensile Tester

The TTF Tensile Tester is use come in pull the dint test provide greatly and stability of pull dint. The most useds for the destructiveness of toy to pull a dint test; BE provided motive by the air cylinder; Clip to hold a pliers of try the kind whole adjustable to the arbitrarily suitable position.

Dimensions  1620 x 320 x 421 mm

Weight      48kg

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-M18 ISO 8124-1 Kinetic Energy Tester

To determine the size catapults kinetic energy of toys, the ejection of parts of the test apparatus through the tube or external testing of the components of the two sensors detect the ejection toy parts used away after a certain period of time, it has calculated the move Energy.

Dimensions   350 x 420 x 210mm ( L x D x H)

Weight       15kg

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-M19 2 m/s. Tester & Dynamic Strength Tester

This instrument is mainly used for test rides at the speed of toys 2m / s when the value of the barrier imposed by force. Toys will be under test placed on the conveyor belt, the drive wheel until the toy speed of 2m / s and remain stable, the display shows the pressure sensor to the force sensing value, according to ability to judge the value of toy safety.

Conveyor belt Speed: 2m/s (can be adjusting)

Dimensions  5920x650x770mm ( L x D x H)

Weight      900kg

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-M27-2 ISO 8124-1 Brake Performance Tester

Covered with a surface of abrasive paper (aluminium oxide P60) with its longitudinal axis parallel to the incline. Apply a force of (50+/-2) N in the direction in which the brake handle is normally operated. Apply the force to the brake handle at the point where it is normally applied in use.

Determine whether the toy moves more than 5 cm

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-M28 ISO 8124-1 Impact Tester

Determine whether the toy has produced hazardous sharp edges, hazardous sharp points or loose parts which

could enter the eye.

Standards

ASTM F963   16CFR 1500   ISO 8124-1

GT-M29 EN-71-1 Impact Test Table

Used to reduce the dangerous caused by damaged manufactural materials or simulated protective devices.

Impact hammer weight   1kg

Base plate size         300 x 300 x 16mm

Adjustable height       0-200mm

Impact hammer face diameter: 80mm

Standards

EN-71-1

GT-M33 Tension Carriage

For use with a pull test.

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-M34 Weights

50kg

25kg

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

IMADA Push-Pull Scale

●Plastic outer shell

●Enclosure: 6 accessorieses

●Peak value maintenance functions

●Accuracy: +/-0.3%F.S

●Zero adjust function

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

TOHNICHI Torque Guage

The torque tool of high nicety, can used for a computer to wait small spare parts assemble and special research to need of fine the torque measure.The degree dish of instrument corpus engraves a degree and measure tiny engrave a degree and measure tiny engrave one degree to row for cent can very expediently clip a tight work piece from any position firmness to carry on quickly with the diagraph of precision.

| Model | Capacity | Craduation |
| --- | --- | --- |
| 45ATG | 5-45 gf.cm | 1 gf.cm |
| 90ATG | 10-90 gf.cm | 2 gf.cm |
| 150ATG | 20-150 gf.cm | 2 gf.cm |
| 300ATG | 30-300 gf.cm | 5 gf.cm |
| 600ATG | 60-600 gf.cm | 10 gf.cm |
| 1200ATG | 100-1200 gf.cm | 20 gf.cm |
| 2400ATG | 300-2400 gf.cm | 50 gf.cm |
| 1.5BTG | 0.2-1.5 kgf.cm | 0.02 kgf.cm |
| 2.4BTG | 0.3-2.4 kgf.cm | 0.05 kgf.cm |
| 3.6BTG | 0.4-3.6 kgf.cm | 0.05 kgf.cm |
| 6BTG | 0.6-6 kgf.cm | 0.1 kgf.cm |
| 9BTG | 1-9 kgf.cm | 0.1 kgf.cm |
| 15BTG | 2-15 kgf.cm | 0.2 kgf.cm |

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-M35 EN-71-1 & ASTM F963 Drop Tester

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-M36 ISO 8124-1 & EN-71-1 Three Pronged Clamp

The stainless steel tests an eye, nose, button up etc. the accessories use fixture.

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-M37 ISO 8124-1 & EN-71-1 Two Pronged Clamp

The stainless steel tests an eye, nose, button up etc. the accessories use fixture

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-M38 ISO 8124-1 & EN-71-1 Compression Head

Steel(surface through electroplate a processing)

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-M39 ISO 8124-1 & EN-71-1Flat Clamp

Pull the dint test assistance fixture

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-M40 ISO 8124-1 & EN-71-1 Torque Fixture(Large)

It clips to hold to try kind in the torque test

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-M41 ISO 8124-1 & EN-71-1Torque Fixture(Middle)

It clips to hold to try kind in the torque test

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-M42 ISO 8124-1 & EN-71-1 Torque Fixture - Trumpet

It clips to hold to try kind in the torque test

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-M43 ISO 8124-1 & EN-71-1 Long - Mouth Clamp

In general use pull the dint test assistance fixture.

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-M44 ISO 8124-1 & EN-71-1 Flexure  Tester

Flexure Tester is metals silk or other metals materials which uses to test to rise to increase rigid or fixed features in the toy in curvedly fold the usage(or abuse) process, whether produces because of split dangerous sharp-edged sophisticated or sharp-edged edge outstanding thing.Belong to the test item of the toy abuse.

Dimensions    100 x 88 x 25mm

Weight       180g

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-M45 16CFR 1500 Bite Tester

Bite Tester is the toy surface of the tooth test which uses to imitate a child of the outstanding department(go together with) piece acceptance bite the ability of dint.Bite Tester belong to the test item of the toy safety.

Dimensions   89 x 42 x 47mm

Weight      756g

Standards

16CFR 1500

GT-M46 ISO 8124-1 & EN-71-1 Rattle Test Fixture ( Template A and B )

Rattle Test Fixture is the mouth cavity capacity which imitates a child, examine toy or toy up of the accessories may result in to suffocate or swallow the inferior danger.

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-M47 ISO 8124-1 & EN-71-1 Small Ball Test Fixture  ( Template C)

Small ball test fixture is use to examine a toy up of whether small ball accessories may result in the child swallow, stop breath way and esophagus to cause choking danger or not.

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-MB60 ISO 8124-1 & EN-71-1 Rattle Test Fixture

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-M48 ISO 8124-1 & EN-71-1 For a Round-gap Test (ABC) (Gap Test Round)

Diamater    5mm

Diamater    12mm

Diamater    6mm

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-M49 ISO 8124-1 & EN-71-1 Short - Mouth Clamp

In general use pull the dint test assistance fixture

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-M50 ISO 8124-1 & EN-71-1 Seam Clamp

Seam Clamp, Pull the cloth sews appropriation fixture.

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-M51 ISO 8124-1 & EN-71-1 Liquid Leak Test Needle

Diameter 1MM, the top radius 0.5MM steel needle, load 5N, for leakage testing

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-M52 ISO 8124-1 & EN-71-1 Hair Clamp

Test the hair pulls the dint appropriation assistance fixture.

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-M53 ISO 8124-1 & EN-71-1 Wide - Mouth Clamp

In general use pull the dint test assistance fixture.

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-M54 ISO 8124-1 & EN-71-1 Clamp for Wheel Tension

Pull cart the round uses fixture

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-M55 ISO 8124-1 & EN-71-1 Tension Clamp

Pull cart the round uses fixture.

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-M56 16CFR 1511, ASTM F963 Pacifier Tester

Dimensions (LxWxH): 102 x 76 x 6.35mm

Standards

16CFR 1511, ASTM F963

GT-M67 Screw Connector

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-M68  ISO 8124-1 Feeler gauge

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-MB14  ISO 8124-1 Plastic Sheeting

Thickness gauge

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-MB16  ISO 8124-1 Measurement of Temperature Rises

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-MB17  ISO 8124-1 Magnetic FluxIndex

PRECISION MILLI GAUSS METER

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-MB18  ISO 8124-1 Perimeter of Ropes and Chains

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-M19B  ISO 8124-1 Yo-yo Balls Measurement

Standards

ISO 8124-1  ASTM F963   EN-71 8.37

GT-M60  ISO 8124-1 Noise Testing Stand

Material: Aluminum alloy.

Noise meters layings aside jig:

Function: Can along X, Y, Z (X displacement: 0 - 1000mm;

Y displacement: 0 -1700mm; Z displacement: 0 - 1800mm)

tripartite to dynamic positioning

Dimensions       1650 x 1200 x 1560mm（LxWxH）

Weight           200kg

Standards

ISO 8124-1,  EN-71-1,  ASTM F963, 16CFR 1500

GT-M77 Simulation Head Tester

Simulation head C

Simulation Head E

Standards:

ASTM F 963, ISO -8124-4

GT-M65 Impact Hammer

Impact energies: 0.20J+/-0.020J,  0.35J+/-0.03J,  0.50J+/-0.04J,  0.70J+/-0.05J,  1.00J+/-0.05J

GT-M65A Single energy level spring hammer ( option one impact energie)

GT-M65B Universal Impact-test Hammer with 0.20 J, 0.35 J, 0.50 J, 0.70 J and 1.00 J, five selectable impact energies, for impact tests to demonstrate the level of robustness.

- Striking element with cocking knob and hammer head, polyamide face with a radius of 10 mm mass= 500 g+/- 1 g

- Hardness hammer Head = R 100 ( Rockwell Hardness )

- Release cone : 60 g+/- 1 g release pressure < 20 N

Standards

IEC60068-2-75, IEC60065, IEC60335-1, IEC60598-1, IEC60745-1, IEC 62115

GT-M11 Transportation Vibration Tester

- Have buffer start function, work medium noise very low.

- Frame structure through spray a powder processing, go together with noodles and the aluminum metal alloy slippery track combination of the stainless steel pedestal, beauty generous.

- Numerical type speed monitor. The simple operation control;Adjustable time has to output function after the electric appliances;Can the move type protect a column;The burly shape protect;The low noise operate.

Vibration frequency:100-300rpm

Load Capacity:100kg

Standard Table Size:1000x1000mm

GT-C76 Formaldehyde Content Tester

Used for rapid testing formaldehyde contents in all kinds of textiles.
Transmittance: 0% -100%

Absorbance :0-2 .0

Formaldehyde content: 5.00-500.00mg/kg  (sample dilution of up to 5000mg/kg)

Wavelength range: 325-1000nm

Wavelength accuracy: +/- 2nm

Standards

ISO 14184-1/2  AATCC 112

Flammability Tester

GT-M17 EN71-2, ISO 8124-2 Toy Inflammability Tester

To test flammability resistance of finery or toy and its decorations of children, to evaluate the burning speed and time of the following kinds of toy. It is including following test.

- Testing for Toys to be worn on the head.

- Testing for Toy disguise costurnes & tyos intended to be entered by a child.

- Testing for Soft-filled toys.

Dimensions   1030 x 680 x 470mm (LxWxH)

Weight       40kg

Standards

EN71-2,  ISO 8124-2

GT-MB17-2 Nailed Flammability Tester

This annex establishes the protocol and general criteria for flammability testing of solids, and soft toys in conformance with the requirements of 16 CFR1500.3.

Hold a burning paraffin candle whose diameter is at least 1 in. (25 mm) so that the flame is a minimum of 5/8 in. (16 mm) high, with the tip of the inner cone of the flame in contact with the surface of the sample at the end of the major axis for 5 s. Maintain contact of the candle with the sample for 5 s or until ignition occurs.

Standards

ASTM F963

GT-M20 Surface Flash Tester

The rapid spread of flame over the surface of the material without ignition of its basic structure, usually applied to pile or fur fabrics. Surface Flash Tester, Swivelling butane burner is traversed across the face of the fabric to determine whether surface flash occurs and to record any damage to the base fabric.

Standards

BS4569

GT-C32 45Degree Automatic Flammability Tester

To determine the burning characteristics of textiles under controlled conditions. Stainless steel test cabinet with glass observation panel provided with automatic timing of flame spread in 0.1-second increments from ignition. Brushing Device including Spare Nylon Brush.

Dimensions   370 x 230 x 540mm(LxWxH)

Weight      30kg

Standards

ASTM 1230  CRF 16-1610  CALIF TB 117

GT-C34 Horizontal Flammability Tester

Flammability Tester (Horizontal method) is applicable to access the flammability performance of textiles by determining the flame spreading speed in the horizontal direction.

Dimension   80 x 33 x 57cm (LxWxH)

Weight      30kg

Standards

ASTM D5132, ISO 3795,FMVSS 302 , DIN 75200 SAE J369

GT-C35 Vertical Flammability Chamber

To determine the vertical flame spread for children’s sleepwear, fabrics, other textile materials or resilient filling materials used in upholstered furniture of textiles in a vertical direction.

Dimensions   65 x 50 x 102cm (LxWxH)

Weight        68Kg

Standards

CATB 117   CFR1615 CFR1616   ASTM6413

GT-C35B ISO 6940 6941 Vertical Combustibility Tester

To detect the flammability resistance of vertical oriented fabrics or wool of weft and toy. Requires operator to ignite. Flame self-extinguish.

ISO6940 Sample size  70 x 190 mm

ISO6941 Sample size  150 x 560 mm

ISO 15025           150 x 190 mm.

Dimension          620 x 730 x 1220mm ( L x W x H )

Weight             80kg

Standards

EN ISO 6940 6941  ISO 15025

GT-C35F UL 94  Horizontal and Vertical Flame Chamber

For the flammability testing of plastic materials used in consumer electric devices and appliances. Stainless steel construction with black interior and large sliding window for easy viewing. Includes a fully adjustable specimen support and precision gas flow controls.

Dimensions     1100 x 700 x 1300mm

Weight        180kg

Standards

UL 94-2006 IEC 60695-11-3  IEC 60695-11-4

GB/T5169.15 16 17 22-2008

GT-C35G IEC 60695 Needle Flame Tester

Needle flame tester is the latest release of the flaming test equipment, with imports of touch-screen controller and instrument.

New test circuit, stable performance, reliable, simple and easy to operate. wide range of parameter adjustment. Apply to the test standards IEC60695,GB5169, etc.

Dimensions    1120x600x1020mm

Weight        180kg

Standards

IEC60695 . GB5169

GT-C35H Glow Wire Tester

Glow wire tester is the latest release of the flaming test equipment, with imports of touch-screen controller and instrument.

New test circuit, stable performance, reliable, simple and easy to operate. wide range of parameter adjustment. Apply to the latest test standards IEC60695,GB5169, etc.

Dimensions    1120x600x1020mm

Weight        180kg

Standards

IEC60695 . GB5169

Swings & Slide Testing

GT-M72 ISO 8124-4 Horizontal Thrust Tester

Water thrust locator: consist of Tension bar and steel structure

Pertinency: The action toy of freely-falling body that bigger than600mm. The swing of above ground more than 1200mm and other action toy with beam.

The tester is used to test the children cilmbing toys, exert water power to the toy top, and observe whether it tip-over or not.

- Loading device: 4 Group

- Loading point distance: ≤ 600mm

- Load range: 0 - 2500N

- Accuracy: +/-0.5%of reading down to 1/100of sensor capacity

- Resolution: 5N

- Units: kgf, Lbf, N, KN. ( can be change)

Standards

ISO 8124-4 6.1.2 and  6.1.4, EN71-8

GT-M74 ISO 8124-4 Sway Tester

Consist of dumbbell steel tube.

Pertinency: aimed at the condition that children swing forward and back, check whether the swing turn-over or not.

Size: 210 x 464mm

Size tolerances: +/-1mm

Standards

ISO -8124-4,6.1.5, EN71-8

GT-M76 ISO 8124-4 Dynamic Strength of Barriers and Handrails

Guardrail dynamic strength tester: consist of steel frame and pulley structure.

Children guardrail is for handgurad. Check whether there is functional damage or not at the horizontal impact.

Gasket: Length: 200mm, Height: 50mm

Instrument: 500x500x2500mm

Weight: 25 kg +/ 1 kg

Standards

ISO 8124-4 ,6.3, EN71-8

GT-M77 ISO 8124-4 Simulation Head Tester Simulation head C,D, E

This is used to test guardrial or fence

Standards

ISO 8124-4, 6.5.1, EN71-8

GT-M81 ISO 8124-4 Swing Suspension Connector Durability Tester

Used to test durability of swing suspension

connector and suspension tool.

Key Specification

Operation: swing to left and right method (90°, 60°, 45° degree)

Load: 37KG, 60KG, 27KG, 54KG

Angle accuracy: +/-1 degree

Standards

ISO8124-4 6.8, EN71-8

GESTER INTERNATIONAL CO.,LTD

7/F, No.15 Chifeng Road, Licheng Region, Quanzhou City of Fujian PR. 362000. China

TEL: 86 0595-22515230                FAX: 86 0595 22515221

E-mail: gester@gester-instruments.com    Web: www.gester-instruments.com