| TO |  | DATE |  |
| --- | --- | --- | --- |
| website | www.bjfth.com |
| TEL | 86-10-81760978 | FAX | 86-10-81769546 | EMAIL | business@bjfth.com |

Technical specification of ZLP

| Name | Technical parameter |
| --- | --- |
| Model | ZLP800 | ZLP630 |
| Rated load | 800Kg | 630Kg |
| Lifting speed | 8-10m/min | 8-10m/min |
| Platform Dimension L×W×H(mm) Spray plastics corrosion-resistant | 7500(2.5m*3)×720×1300 | 6000(1+2+3m)×720×1300 |
| Lifting Height | 100 m | 100 m |
| Cable | 100 m | 100 m |
| Steel rope (specially-made) | Ф9.1mm | Ф8.3mm |
| Hoist | Pulling power | 7.84KN | 6.17KN |
|  | electric motor | model | YEJ100L-4 | YEJ90L-4 |
|  |  | Power | 1.8KW*2 | 1.5KW*2 |
|  |  | Voltage | 380V/220 3phase | 380V/220v 3phase |
|  |  | Rotational speed | 1420rpm | 1420rpm |
|  |  | Braking moment | 15Nm | 15Nm |
| Safety lock | Permission force of impact | 30KN | 30KN |
|  | Locking Cable Angle | 3°~8° | 3°~8° |
| Suspension mechanism (galvanized ) | Front beam overhang | 1.3~1.5m | 1.3~1.5m |
|  | Support adjustable height | 1.44~2.14m | 1.44~2.14m |
| Counterweight | 1000kg | 800kg |
| 20’ft container | 8sets | 9sets |
| FOB Tianjin | A-alloy platform | USD 2810 | USD 2610 |
|  | Hot Dipping Platform | USD 2590 | USD 2420 |
|  | Steel platform | USD 2520 | USD 2350 |
| Note: 1.The quotation efficient duration: 1 month 2.Payment term:T/T Delivery time:7-15days 3. The Voltage and Frequency could up to different countries' standard. 4.Counterweight is made of cement(25KG/piece) |