QUOTATION

| To: Meycagesal Quotation No.: 20151022 |
| --- |
| Phone: Date: 22th,Oct,2015 |
| 1.Port of Loading: Shanghai Port. 2.Way of transport: by sea FCL. 3.Terms of payment: 30% in advance T/T , Balance 70% T/T before shipment. 4.Partial Shipment: Not allowed 5.Delivery Time: 30 days after receiving deposit. 6.installation,training:included |
| Assembly-welding-straightening machine |
| Model: | PHJ-15 |
| Applicable height of web（mm） | 200-1500 |
| Applicable thickness of web（mm） | 4-20 |
| Applicable height of flange（mm） | 100-500 |
| Applicable thickness of flange（mm） | 5-25 |
| Applicable length of H-beam（mm） | 3000-12000 |
| Working Speed: (m/min) | 0.15-1.5 |
| Approach table: | 2600mm*3sets, mechanical arm and draw bar system |
| Runout table: | 2600mm*3sets |
| Welding machine | Not include |
| Welding way | SAW,MIG |
| Way of Straightening: | Hydraulic pushing mechanical compelling straightening |
| Size of machine(after installation) | 28000mm*3800mm*4500mm |
| weight | 13500KG |
| Power of total machine | 21KW(without welding machine) |
| Capacity | Normal 1m/min-1.3m/min(depend on the thickness of plate) |
| Quotation: | USD/set, CIF Cadiz |

We can produce according to your requestment.

Pics for reference only.

Supply range

- Main body of 3-in-1 auto welding machine is including: Main frame and gantry frames, flange and web clamping, centering and straightening system, driving motor and reducer and so on.

- Approach table is including: 3 sets of Driving and driven table roller 2600mm each., 3 groups of mechanical arms, and draw bar system etc

- Runout table is including: 3 sets of Driving and driven table roller 2600mm each.

- Hydraulic system is including: Oil pump station, high pressure oil pipes, hydraulic cylinders etc

- Electrical control system is including: Electric cabinet, AC frequency converter etc

- Soldering flux recycling system is including: 2 sets of soldering flux recycling machine