|  | Model | PRICE(USD)20’CONTAINER FOB(per set) | PRICE(USD)40’CONTAINER FOB(per set) | Features | Advantages |
| --- | --- | --- | --- | --- | --- |
|  | BZB-FB-1200 Diesel heating spray booth |  | USD26,400 40’HQ and 20’GP | Two rows of pits with galvanized duty-bearing grids for air sucking. Wall panel is 70mm EPS, heat preservation, steel plate thickness 0.426mm, wall panel equipped structural steel upright and composite beam. All light are Philips lamp, Ballasts Professional and durable, more steadily than electronic headlamp. Inlet use 4 sets 4kw Centrifugal Outer-rotor F-category Insulated Ventilator, exhaust fan use 2 sets 7.5kw fan blade belt drive fan, increase the air speed, the positive internal air-pressure effectively prevents the dust without from going into the area so that the quality of paint spraying is thus guaranteed. 2 sets Italy Riello G20 diesel burner. Optional: 3D platform lift system. Optional: side exhaust instead of 2 rows of pits. | This model is suitable for 10 meters long minibus, van etc. transportation maintenance and manufactured. |
|  | BZB-FB-1500H Diesel heating spray booth |  | USD35,100 40’HQ and 20’GP | Two rows of pits with galvanized duty-bearing grids for air sucking. Wall panel is 75mm EPS, heat preservation, steel plate thickness 0.476mm, wall panel equipped structural steel upright and composite beam. All light are Philips lamp, Ballasts Professional and durable, more steadily than electronic headlamp. Inlet use 4 sets 7.5kw Centrifugal Outer-rotor F-category Insulated Ventilator, exhaust fan use 2 sets 15kw fan blade belt drive fan, increase the air speed, the positive internal air-pressure effectively prevents the dust without from going into the area so that the quality of paint spraying is thus guaranteed. 2 sets Italy Riello RG5S diesel burner. Optional: 3D platform lift system. Optional: side exhaust instead of 2 rows of pits. | This model is suitable for high level customer requirements, can meet the demand of 12 meters long coach, heavy-duty goods vehicle etc. transportation maintenance and manufactured. |
|  | BZB-FB-1500M Diesel heating spray booth |  | USD31,800 40’HQ and 20’GP | Two rows of pits with galvanized duty-bearing grids for air sucking. Wall panel is 75mm EPS, heat preservation, steel plate thickness 0.426mm, wall panel equipped structural steel upright and composite beam. All light are Philips lamp, Ballasts Professional and durable, more steadily than electronic headlamp. Inlet use 4 sets 5.5kw Centrifugal Outer-rotor F-category Insulated Ventilator, exhaust fan use 2 sets 11kw fan blade belt drive fan, increase the air speed, the positive internal air-pressure effectively prevents the dust without from going into the area so that the quality of paint spraying is thus guaranteed. 2 sets Italy Riello G20 diesel burner. Optional: 3D platform lift system. Optional: side exhaust instead of 2 rows of pits. | This model is suitable for normal level customer requirements, can meet the demand of 12 meters long coach, van etc. transportation maintenance and manufactured. |
|  | BZB-FB-1500L Diesel heating spray booth |  | USD22,700 40’HQ | Semi-downdraft construction, the whole cabin front ceiling part with ceiling air supply system, the rest part just have ceiling board; Two rows of pits with galvanized duty-bearing grids for air sucking. Wall panel is 75mm EPS, heat preservation, steel plate thickness 0.426mm, wall panel equipped structural steel upright and composite beam. All light are Philips lamp, Ballasts Professional and durable, more steadily than electronic headlamp. Inlet use 2 sets 7.5kw Centrifugal Ventilator, exhaust fan use 2 sets 7.5kw fan blade belt drive fan. 2 sets Italy Riello G20 diesel burner. Optional: 3D platform lift system. | This model is considering the economic (economically affordable type), can meet the demand of 12 meters long coach, van etc. transportation maintenance and manufactured. |
|  | BZB-FB-1800 Diesel heating spray booth |  | USD46,800 2*40’HQ | Two rows of pits with galvanized duty-bearing grids for air sucking. Wall panel is 75mm EPS, heat preservation, steel plate thickness 0.476mm, wall panel equipped structural steel upright and composite beam. All light are Philips lamp, Ballasts Professional and durable, more steadily than electronic headlamp. Inlet use 6 sets 7.5kw Centrifugal Outer-rotor F-category Insulated Ventilator, exhaust fan use 3 sets 15kw fan blade belt drive fan, increase the air speed, the positive internal air-pressure effectively prevents the dust without from going into the area so that the quality of paint spraying is thus guaranteed. 3 sets Italy Riello RG5S diesel burner. Optional: 3D platform lift system. Optional: side exhaust instead of 2 rows of pits. | This model is suitable for high level customer requirements, can meet the demand of 15 meters long coach, non-standard large-sized workpiece, heavy-duty goods vehicle, train etc. transportation maintenance and manufactured. |
|  | BZB-FB-2000 Diesel heating spray booth |  | USD51,800 2*40’HQ | Two rows of pits with galvanized duty-bearing grids for air sucking. Wall panel is 75mm EPS, heat preservation, steel plate thickness 0.476mm, wall panel equipped structural steel upright and composite beam. All light are Philips lamp, Ballasts Professional and durable, more steadily than electronic headlamp. Inlet use 6 sets 7.5kw Centrifugal Outer-rotor F-category Insulated Ventilator, exhaust fan use 3 sets 15kw fan blade belt drive fan, increase the air speed, the positive internal air-pressure effectively prevents the dust without from going into the area so that the quality of paint spraying is thus guaranteed. 3 sets Italy Riello RG5S diesel burner. Optional: 3D platform lift system. Optional: side exhaust instead of 2 rows of pits. | This model is suitable for high level customer requirements, can meet the demand of 18 meters long coach, non-standard large-sized workpiece, heavy-duty goods vehicle, train etc. transportation maintenance and manufactured. |