DUCT MANUFACTURE AUTO-LINE II

Line II consists of a feeding metal frame unit, leveler grooving roller, notch and punch square machine, shearing machine. The electrical control system uses a computer combined with a closed-loop servo-system to increase the precision and stabilization of the line.

MACHINE DETAIL

A:The maximum working speed is 10m/min.

B:The length tolerance is ±0.5mm/m.

C:The diagonal line tolerance is ±0.8mm/m.

D:The feeding frame can be set to the customer's requirements.

FLOW CHART

BASIC EQUIPMENT

A: Two power metal feeding frames 
B: One leveler grooving roller machine 
C: Four hydraulic notch and die 
D: Hydraulic shearing machine 
E: Industrial computer and specific software

Price:

Price basis: FOB Tianjin, China.

Payment: 40% down payment by T/T in advance, the balance by T/T before shipment.

Lead-time: within 30 days after receiving down payment

Unit price: USD18,990 for 1300mm width

USD20,960 for 1600mm width

Guarantee: one year since the date of B/L