QUOTATION

| To: Cristian Quotation No.: 20151130 |
| --- |
| Phone: Date: 30th,Nov,2015 |
| 1.Port of Loading: Shanghai Port. 2.Way of transport: by sea FCL. 3.Terms of payment: 30% in advance T/T , Balance 70% T/T before shipment. 4.Partial Shipment: Not allowed 5.Delivery Time: 30 days after receiving deposit. |
| Assembling-welding-straightening machine |
| Model: | PHJ-18 |
| Applicable height of web | 200-1800mm |
| Applicable thickness of web | 5-20mm |
| Applicable height of flange | 200-800mm |
| Applicable thickness of flange | 6-25mm |
| Applicable length of H-beam | 4000-15000mm |
| Working Speed | 0.15-1.5m/min |
| Approach table | 2600mm*4, mechanical arm and draw bar system |
| Runout table | 2600mm*4 |
| Welding machine Model | 2 sets of zhenzhong DC welder MZ-1250,2 sets of zhenzhong AC welder MZ-1600 |
| Welding way | Twin arc-twin wire welding type |
| Wire dia. | 3.2mm,4mm,5mm |
| Power of drive motor | 21KW |
| Way of Straightening | Hydraulic straightening |
| Power supply | Designed by requirement |
| Quotation: | USD/set, FOB Shanghai |

We can produce according to your requestment.

Pics for reference only.

Supply range

- Main body of 3-in-1 auto welding machine is including: Main frame and gantry frames, flange and web clamping, centering and straightening system, driving motor and reducer and so on.

- Approach table is including: 4 sets of Driving and driven table roller 2600mm each., 3 groups of mechanical arms, and draw bar system etc

- Runout table is including: 4 sets of Driving and driven table roller 2600mm each.

- Hydraulic system is including: Oil pump station, high pressure oil pipes, hydraulic cylinders etc

- Electrical control system is including: Electric cabinet, control  box, AC frequency converter etc

- Automatic welding system is including: 2 sets of zhenzhong DC welder MZ-1250,2 sets of zhenzhong AC welder MZ-1600,4 sets of wire feeding system,2 sets of MZ-1250 control box, 2 sets of MZ-1600 control box.

- Soldering flux recycling system is including: 2 sets of soldering flux recycling machine