RY320-5B/480-5B Flexo printing machine

Station for 5-color flexo printing machine:

1.One mounting device.

2.One anilox roller for each group (Specification is optional)

3.Three sets printing rollers (3*5=15)

4.Printing both sides at the same time (with turn bar)

5.With the lamination station

6.One unwinding tension controller (Mitsubishi Japan)

7.One rewinding tension controller

8.One rotary die cutting station

9.Each station with IR drier

Main technical parameter:

| Model | RY320-5B | RY480-5B |
| --- | --- | --- |
| Printing speed | 60m/min | 60m/min |
| Printing color | 5colors | 5colors |
| Max. Web width | 320mm | 480mm |
| Max. Printing width | 310mm | 460mm |
| Max. Unwinding diameter | 600mm | 650mm |
| Max. Rewinding diameter | 550mm | 600mm |
| Printing girth | 175-380mm | 250-580mm |
| Precision of registration | ±0.10mm | ±0.10mm |
| Dimensions | 2100*1100*2700(mm) | 2100*1300*2700(mm) |
| Machine weight | About 2200kg | About 2600kg |

Characteristics:

- Adopt the anilox roller to spread ink.

- Unwinding and rewinding are controlled by magnetism power brake, clutch. (or by automatic tension controller of mitsubishi , made in Japan).

- Printing unit adopt 360º for registration.

- Printing unit have one infrared to dry the device group each.

- The rubber roller can break away from automatically while parking, and running at a low speed, in order to avoid water being black to be dry.

- The main motor is adopted the import stepless regulation of frequency conversion.

- Unwinding, printing, varnishing, IR drying, laminating and rewinding can be finished in one process, this kind of printing machine is best for each printing companies to print on adhesive-paper labels and other commercial label.

Price list

- RY320-5B Flexo printer(standard configuration): 27000USD

Extra color unit: 3500$

- RY480-5B Flexo printer (standard configuration): 30000USD

Extra color unit: 4000$

- Optional devices for extra payment:

1). Web guiding:

a. Chinese web guiding: 2500USD

b. American Accuweb: 5000USD

2). UV (for 320 model): 2700USD/PC （4.8KW）---made in China

4500USD/PC--- Taiwan UV light

UV (for 480 model):  2900USD/PC （4.8KW）---made in China

5500USD/PC--- Taiwan UV light

3). Video monitor: 5000USD

4). Corona treator: 3500USD

5). Extra 1 rotary die cutting station: 2,500USD

Power supply: 380V, 50HZ, 3 Phases

Note: above are FOB price, and valid for 2 months.

Delivery time: 45 days

Payment terms: 30% deposit in advance, and 70% balance payment before shipment

Installation and testing the machines

If the buyer need engineer from the seller's side, the seller should dispatch an engineer to buyer's side. The buyer pays all the expenses including the payment to get visa, round air ticket, food and accommodation, and also pays 80$/day for engineer during the installtion and testing machine period of first 7 days. After 7 days, the buyer shold pay 100$/day for engineer.

Guarantee:

Within one year guarantee from installation date. If the machine need repair during this period, the seller shall dispatch technician to buyer's side. The buyer pays all the expenses including the payment to get visa, round air ticket, food and accommodation during the repairing period, and pays 80$/day for engineer during the repairation period of first 7 days. After 7 days, the buyer should pay 100$/day for engineer.During the gurantee period, the seller will bear the cost for defective parts arisen by quality and mail the parts. but the freight for the defective parts should be paid by the buyer’s side. Additionally, if the defective parts are arisen by improper use of buyer’s side, the seller will not supply them for free.

Following photo for your reference