DCSWS-300  Automatic  Triangle  Tea  Bag  Packing  Machine

Features:

- This packing line including multi-heads weigher and triangle tea bag packing machine, can have inner bag with tag and thread with outer bag automatically.

- Packing process: Separate multi-heads weigher can weigh different rawmaterial like tea, dry fruit pcs according to weight set, fill rawmaterial into inner bag together, inner bag slip into outer bag.

- Inner tea bag packing machine use ultrasonic can get triangle tea bag and flat three side sealing tea bag.

- Whole packing line use PLC controller and touch screen operation, driving system simple and reliable.

Machine picture as below

Automatic tea bag packing machine           multi-heads weigher and sample tea bag

Technical Specification

| Item | Description of Item | Unit Price in USD | Qty. | Total Price in USD |
| --- | --- | --- | --- | --- |
| 01 | Nylon triangle tea sachet packing machine with five heads weigher Model:DCSWS-300 Range of Measurement: ≤3±0.5g Packing Speed:30 - 40bag/min （Depend on Products） Request of rawmaterial: Tabular tea and length ≤15mm Packing material: Nylon and printed with line and tag already Sealing type: Ultrasonic sealing Air requested: ≥0.6Mpa Inner film width: 140mm Outer film width: 180mm, outer bag size: W90*L100mm Total Power: 380V/1.6KW Machine Weight:950Kg Mainframe Dimensions(L x W x H): (1500x1200x2400)mm | 30,000 | 01 | 30,000 |

Remark: All the price is FOB Port Shanghai.

Guarantee	: One year from the date of shipment against any manufacturing defects

Shipment	: Within 40-45 working days from receiving 30% deposit

Payment	:T/T, 30% deposit in advance and full payment before delivery

# Text boxes

Price of wrapping:

US$0.04/bag with thread and tag

6000bag/roll

6 roll/box

MOQ: 5 boxes   (STD tag as below)

Delivery time: 10 working days

OEM tag: MOQ: 17 boxes and edit fee US$350/color

If your order reach 1000,000 bags, do not need pay for edit fee.

Delivery time: 80 working days.

About outer bag material like PET/AL/PE, US$7/kg, MOQ:500kg, edit fee: each color:US$160