3 type install for weighbridge introduce

Type 1 setting weighbridge with steel ramps on ground directly(Mobile weighbridge)

- Please refer to follow design drawing 01.

- The ground is without need extra concrete and dig ground,

- But you need make sure your ground condition is same or better than follow 2 side condition:

1>Ground concrete thickness should more than 30CM

2>Soil is rigid and not soft under Ground concrete

3>Plan to move weighbridge to other place in future

Design drawing 01

Type 2 is set weighbridge with 2 concrete ramps above ground

This type is input more steel and concrete in construct ground concrete,

if scale capacity is 70ton to 150ton and have large ground space,this type is advice to choose,please refer to attached photo 01 to photo 03

Photo 01 is fix steel reinforcement bars in ground as per drawing.

Photo 02 is Pour mixed concrete after formwork.

Photo 03 is maintain concrete dry and build 2 concrete ramps

Photo 03-01 is setting weighbridge on ground

Type 3 is setting weighbridge in ground

(Without concrete ramps or steel ramps)

This type is also required input more steel and concrete in building.

If your ground is small and narrow,it can consider this type to reduce occupy.

Detail please refer to attached photo 10 to photo 11

Photo 10 is Weighbridge in ground type concrete

Photo 11 is setting Weighbridge in ground

Please confirm WHICH type you prefer?

Type 01 OR type 02 OR type 03?