群峰PL60型混凝土砌块劈离机

PL60 CONCRETE BLOCK SPLITTER

PL60型砌块劈离机用于劈离混凝土建筑砌块、挡土墙砌块等。该劈裂机属四刀式劈裂机，液压系统独立，电控系统方便，操作设定简单，安全可靠，可实现自动化生产。

The PL60 can split retaining wall, architectural and standard units in heights ranging from 40 mm to 300mm and configured 600mm wide. It is built with a self-contained hydraulic unit that makes it simple to be set up and operate. It has four-way blades and controls with panel. It can realize in automatic.

技术参数 Technical Data

| 劈离高度 | 40~300mm | Splitting Height | 40~300mm |
| --- | --- | --- | --- |
| 最大劈离宽度 | 600 | max.Splitting Width | 600 |
| 生产效率 | 300~600块/小时 | Production Rate | 300~600pcs./hour |
| 电机功率 | 7.5kW | Power | 7.5kW |
| 整机重量 | 2398kg | Weight | 2398kg |
| 外形尺寸 | 2700×2200×2000mm | Dimension | 2700×2200×2000mm |
| 价格Price (FOB Xiamen Port, China) | PRICE USD18,000.00 |

This price is valid until 31st December 2015.