Technical parameters

Of

BH-1000-840 roll forming machine

Ⅰ.Profile drawing

Ⅱ.Main parameters:

- Frame of machine: welding with 350H beam steel

- Forming of guide feeding:  side roller type

4.  Diameter of shaft:  ￠70mm

5.  Thickness of wallboard: 14mm

6.  Motor power of forming machine:  4.0 KW

7.  Line speed of forming machine: 5-8 m/min

8.  Steps of forming machine: 11 steps

9.  Roller material:  superior 45# steel forging

10.  Thickness of roller Chromium coating: 0.05mm

11.  Hydraulic station motor: 3.0 KW, pressure: 8-12Mpa

12.  Hydraulic station Oil pump:  gear pump

14.  Cutting blade:  Cr12 with heat treatment,  HRC58º-60

15.  Thickness of the coil: 0.4-0.8 mm

16.  Feeding width: 1000mm

17.  Precision to length:  ±2mm

18. Computer system: industry PLC controlling

19. Voltage: 380V, 50Hz, 3 Phases(can be as your required)

Ⅲ.  Technological process figure:

Ⅳ.  Equipment configuration

| Item | Number |
| --- | --- |
| Roll forming machine | 1 set |
| Hydraulic station | 1 set |
| Counter | 1 set |
| Computer control cabinet | 1 set |
| Decoiler | 1 set |

- Ⅴ.Machine

Ⅶ.Price terms:

Price :USD7,500 FOB( Dalian port).

Payment terms: T/T. 30% deposit,70% before delivery.

Delivery time: Within 30 days after receiving your 30% deposit.

Guarantee period: 13 months after B/L date