ALUMINUM FLEXIBLE DUCT FORMING MACHINE

This machine is specially for producing aluminum flexible ducts with pure aluminum foil without steel wire reinforcement for various purpose. Our advantage is our omnipotent mould which will save investment cost.

I Main technical data

1.1 Diameter range: 60mm~300mm

1.2 Length of aluminum tube: 100-8000mm

1.3 Suitable material: 42-55mm wide

Pure aluminum foil: 0.05-0.15 (code 8011, hardness H22)

1.4 Working speed: 1-5m/min

1.5 Weight: about 250kg

1.6 Main motor power: 0.75kW

1.8 Dimension: 1200mm x 550mm x 1200mm (main machine, excluding unloading rack)

1.9 Duct concentrating device: 3000mm x 480mm x 1500mm

II Buildup of the line:

2.1 Simple decoiler

2.2 Feeding speed adjuster

2.3 Material of roller: GCr15 steel, quenched HRC58-62.

2.4 Manual cutting type (automatic cutting can be optional)

Automatic cutting details:

a)Cutting way: Saw cutting online without stop

b)Cutting saw speed: 2800rpm, ID32mm, OD200mm

c)Cutting motor power: 0.18KW

d)Cutting length is adjustable

2.5 Automatic compressing system can be optional

Automatic compressing details:

Compressing speed: 6-8m/min

Max. duct lenth: 4500-5500mm

Motor power: 0.75KW

Air pressure: 4MPa

Automatic loading and unloading device.

Automatic adjustment for different diameter

III Accessories:

3.1 Omnipotent mould, diameter range from 60 to 250mm, free adjusting.

3.2 Special steel strip as mould, 20 meters

3.3 Special tool, one set

3.4 Lubricant oil, one bottle

3.5 Duct contracting device is optional

IV Price

Price basis: FOB Shanghai

Payment: 30% down payment by T/T, the balance down before shipment

Lead-time: within 30 days after receiving down payment

Unit price: PAD-300-1   USD 7,780

PAD-300-2   USD9,950

PAD-300-3   USD23,680

Note: For double layer duct forming, the machine cost should be USD3000 extra.

V Guarantee: One year since the date of B/L