东莞志成机械有限公司

DONGGUAN CHI SHING MACHINERY CO., LTD.

Website: www.quiltingmachine.cn                        www.quilt-machines.com

E-mail: sales1@quiltingmachine.cn                       Post code: 523406

Add: Fu Zhushan, Liao Bu Town, Dong Guan City, Guang Dong Province, China

TEL: 0086-769-83322330                               FAX:0086-769-83326330

1. Digital Control Multi-needle Quilting Machine

Technical Specification:

| Model | CS64-2 | CS64-3 | CS94-2 | CS94-3 | CS110-2 | CS110-3 | CS128-2 | CS128-3 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| L Dimensions W H | 3600mm | 3600mm | 4600mm | 4700mm | 5200mm | 5300mm | 5500mm | 5600mm |
|  | 1100mm | 1200mm | 1100mm | 1200mm | 1100mm | 1200mm | 1100mm | 1200mm |
|  | 1600mm | 1650mm | 1650mm | 1650mm | 1600mm | 1650mm | 1600mm | 1650mm |
| Quilting Width | 64inch | 64inch | 94inch | 94inch | 110inch | 110inch | 128inch | 128inch |
| Max. Needles’ Quantity | 128 pcs | 192 pcs | 188 pcs | 282 pcs | 220 pcs | 330 pcs | 256 pcs | 384 pcs |
| Pattern size | 1-6inch | 1-12inch | 1-6inch | 1-12inch | 1-6inch | 1-12inch | 1-6inch | 1-12inch |
| Needle Distance | 1 inch | 1 inch | 1 inch | 1 inch | 1 inch | 1 inch | 1 inch | 1 inch |
| X-driver | 8 inch | 12 inch | 8 inch | 12 inch | 8inch | 12inch | 8inch | 12inch |
| Quilting Thickness | ≤30mm ≤400g/m2 | ≤30mm ≤400g/m2 | ≤30mm ≤400g/m2 | ≤30mm ≤400g/m2 | ≤30mm ≤400g/m2 | ≤30mm ≤400g/m2 | ≤30mm ≤400g/m2 | ≤30mm ≤400g/m2 |
| Needle Stitch | 2-6mm | 2-6mm | 2-6mm | 2-6mm | 2-6mm | 2-6mm | 2-6mm | 2-6mm |
| Needle Model | #16,#19 | #16,#19 | #16,#19 | #16,#19 | #16,#19 | #16,#19 | #16,#19 | #16,#19 |
| Running Rate | 200-500r/m | 200-500r/m | 200-500r/m | 200-500r/m | 200-500r/m | 200-500r/m | 200-500r/m | 200-500r/m |
| Production Capacity | 2-120m/h | 2-120m/h | 2-120m/h | 2-120m/h | 2-120m/h | 2-120m/h | 2-120m/h | 2-120m/h |
| Voltage | 3.5kw | 3.5kw | 3.5kw | 3.5kw | 6.2kw | 6.2kw | 6.2kw | 6.2kw |
| Weight | 2300kg | 2600kg | 3000kg | 3400kg | 3500kg | 3800kg | 4000kg | 4500kg |

Applications:

This kind of quilting machinery adopt digital control program. It is widely used for quilting high-quality bedding covers ,quilt covers, garments, handbags, sofa and mattress protectors, seat-covers, kitchen sets(aprons, oven glovers, potholders) and household ornaments. Different patterns are available.

Main Feature and Function:

1. Saddles and rollers driven by Panasonic servo devices. 
2. The revolution of the spindle controlled by Panasonic frequency conversion control devices. 
3. Stitches length 2mm-6mm adjustable.
4. Easy pattern drawing system enables you finish the pattern design in a few minutes. 
5. 360 degrees quilting and machines come with 300 quilting patterns for your choices.
6. Tack and jump function included (independent patterns can be quilt).
7. Function of pattern compensation, and effective solution to the distortion of patterns when quilting thick materials. 
8. Adjustable pressing plate lifting mechanism enables you quilt a broad range of material thickness.

9. Simulation display of quilting. 	
10. Automatic needle raising and location brake system. 
11. Function of automatic stop on breaking of thread.(thread break detectors)
12. Infrared sensors to guarantee the safety of the operator.

13. Function of setting bottom thread length.

14. Error problem detection system.

15. Emergency sensors safety device.

16.Improved quilting software control system allows more precise and stable quilting operations.

17. Improved fabric loading system: The fabric-loading motor provides tension control and ensure the quilting effect.

2-1. CSHX233 Series High Speed Multi-head Quilting And Embroidery Machine

Technical Specification:

2-2. CSHX2-34 Separate Multi-head Quilting and Embroidery Machine(B Type)

Technical Specification:

Applications:

Because of using the large rotating hook, (KHS20-R) the bottom thread capacity can be up to 120 meters, independent needle bar and presser foot. The stitch is very smooth, clear, beautiful with strong three-dimension effect which is particularly applicable to high-grade fabric processing. Such as, clothing, beddings, bags, shoes, wardrobe doors and background walls, etc.

Main Feature and Function:

1. This quilting and embroidery machine adopting digital control program. 
2. The revolution of the Spindle, Saddles and Rollers controlled by Panasonic servo motors and drivers. 
3. Stitches length 2mm-12mm adjustable.
4. WILCOME pattern design system or other embroidery machine design software.
5. 360 degrees quilting and embroidery. The PC comes with 300 quilting and embroidery patterns for your choices.
6. Tack and jump function included (independent patterns can be quilt).
7. Function of pattern compensation and effective solution to the distortion of patterns when quilting thick materials. 
8. Adjustable pressing plate lifting mechanism enables you quilt a broad range of material thickness.

9. Thread break detectors (top thread and bottom thread)
10. Automatic needle raising and location brake system. 
11. Error problem detection system.
12. Emergency sensors safety device. Infrared sensors to guarantee the safety of the operator.

13.Improved quilting software control system allows more precise and stable quilting and embroidery operations.

14. Improved fabric loading system: The fabric-loading motor two way running makes the fabric loading more easier and faster and provides tension control and ensure good quilting and embroidery effect.

# Text boxes

| Model | CSHX-233 | CSHX67.5”-25 | CSHX-322 |
| --- | --- | --- | --- |
| L Dimensions W H | 5300mm | 5300mm | 5300mm |
|  | 1503mm | 1503mm | 1503mm |
|  | 1943mm | 1943mm | 1943mm |
| Embroidery Width | 3353mm | 3375mm | 3350mm |
| Needles’ Quantity | 66 pcs | 54 pcs | 44 pcs |
| Heads | 33 | 25 | 22 |
| Needle Distance | 2 inch | 2.6 inch | 3 inch |
| Running Rate | 200-800RPM | 200-800RPM | 200-800RPM |
| Quilting Thickness | ≤400g/m2 | ≤400g/m2 | ≤400g/m2 |
| Needle Stitch | 2-12mm | 2-12mm | 2-12mm |
| Needle Model | #11-18 | #11-18 | #11-18 |
| Saddle Distance | 12” | 12” | 12” |
| Production Capacity | 2-140m/h | 2-140m/h | 2-140m/h |
| Rating Power | 5.5kw 380v | 5.5kw 380v | 5.5kw 380v |
| Weight | 3500kg | 3500kg | 3500kg |

| Model | CSHX2”-34B | CSHX67.5”-26B | CSHX3”-22B |
| --- | --- | --- | --- |
| L Dimensions W H | 6000mm | 6000mm | 6000mm |
|  | 1503mm | 1503mm | 1503mm |
|  | 1943mm | 1943mm | 1943mm |
| Embroidery Width | 1727mm*2 | 1755mm*2 | 1676mm*2 |
| Needles’ Quantity | 68 pcs | 52 pcs | 44 pcs |
| Heads | 34 | 26 | 22 |
| Needle Distance | 2 inch | 2.6 inch | 3 inch |
| Running Rate | 200-800RPM | 200-800RPM | 200-800RPM |
| Quilting Thickness | ≤400g/m2 | ≤400g/m2 | ≤400g/m2 |
| Needle Stitch | 2-12mm | 2-12mm | 2-12mm |
| Needle Model | #11-18 | #11-18 | #11-18 |
| Saddle Distance | 12” | 12” | 12” |
| Production Capacity | 2-140m/h | 2-140m/h | 2-140m/h |
| Rating Power | 5.5kw 380v | 5.5kw 380v | 5.5kw 380v |
| Weight | 3800kg | 3800kg | 3800kg |