###### CHINA JIANGSU INTERNATIONAL ECONOMIC-TECHNICAL COOPERATION

GROUP LTD.  (ZJMECH TECHNOLOGY CO LTD.)

Add: Haian Development Zone, Jiangsu, China

Http: www.zjmec.com  Attn: Mr Song

### Facture Pro-forma

Date: le décembre 30, 2015

N°: 14ALG32ZJ55A1004

A: M/S S.A.R.L OUEST Equipment

Email: Ouestequipement@ymail.com

Kind Atten: Mr Mezouar Mohammed; Mr Bouchakour Ali Amar Nasreedine

Nous sommes ravis de offrir les marchandises suivantes au sujet des conditions et les modalités ci-dessous.

| Emballage Prix Expédition Valitité Alimentation | : Emballage d’exportation standard : FOB Shanghai, Chine : Sous les 90 jours : Sous les 21 jours : 380V/50HZ/3PH |
| --- | --- |

I : Liste de détails

|  | Article | Modèle | U/prix FOB China | Qté | TTL (USD) |
| --- | --- | --- | --- | --- | --- |
| 1 | Presse à ailettes type C ∮12.7mm | ZCPC-65 | USD30100 | 2 | 60200 |
| 2 | Moule d’ailettes (1): ∮9.52mm*25*21.65*12Rows*2P | USD20000 | 1 | 20000 |
|  | Pièces de rechange pour∮9.52mm | USD3260 | 1 | 3260 |
|  | Moude d’ailettes (2) ∮12.7mm*41*35*8Rows*1P | USD20000 | 1 | 20000 |
|  | Pèces de rechange pour ∮9.52mm | USD3260 | 1 | 3260 |
| 3 | Cintreuse d’épingles semi-automatique | ZJBU-9.52*4 /1600mm | USD18000 | 1 | 18000 |
|  |  | ZJBU-12.7*4 /2500mm | USD24000 | 1 | 24000 |
| 4 | Découpeuse de coiled tube automatique | ZJQX-9.52*2 + 12.7*2 | USD19000 | 1 | 19000 |
| 5 | Pistolet pneumatique | M6, M8, M10 | USD220 | 3 | 660 |
| 6 | Expandeur portable | ZSZ -12.7/2500 | USD7500 | 2 | 15000 |
| 7 | Exbandeur de tube vertical | Model: AFPZ-1500 | USD51000 | 1 | 51000 |
| 8 | Cintreuse de coude U | Model: ZXU-9.52 | USD20000 | 1 | 20000 |
|  |  | Moule: 12.7 | USD8000 | 1 | 8000 |
| 9 | Machine d’insertion de bague | ZTH9.52 | USD22000 | 1 | 22000 |
| 10 | Machine de soudage automatique | ZSH-1500 | USD52000 | 1 | 52000 |
| 11 | Machine de nettoyage pour coude U | ZXU | USD29000 | 1 | 29000 |
| 12 | Cintreuse de tube manuelle | 5/8”, 3/4”, 7/8” | USD1500 | 3 | 4500 |
| 13 | Poinçonneuse CNC à tourelle | HPM-300 (8station) | USD62800 | 1 | 62800 |
|  | Moule de poinçonnage de trou |  | free | 8 | 0.00 |
|  | Alésoir |  | USD250.00 | 6 | 1500 |
| 14 | Presse plieuse CNC avec CNC Delem DA-41, vis à billes, onduleur, verrouillage rapide | PB-100/3200 | USD16570 | 1 | 16570 |
|  |  | 121# (30 degree) | USD480.00 | 1 | 480.00 |
|  |  | 141# | USD550.00 | 1 | 550.00 |
|  |  | 132# (R12) | USD590.00 | 1 | 590.00 |
|  |  | PB-80/2500 | USD16000 | 1 | 16000 |
|  |  | 121# (30 degree) | USD380.00 | 1 | 380.00 |
|  |  | PB-40/1500 | USD11940 | 1 | 16000 |
|  |  | 121# (30 degree) | USD380.00 | 1 | 380.00 |
| 15 | Cisaille-guillotine avec NC E21, vis à billes, onduleur, lame 6CrW2Si | SBSH-4*3200 | USD10300 | 1 | 10300 |
|  |  | SBSH-4*2500 | USD9100 | 1 | 9100 |
| 16 | Encocheuse hydraulique avec angle ajustable | HN4/200 | USD6200 | 1 | 6200 |
| 17 | Presse hydraulique ( simple action 200-Ton, w/ operation à bouton classique) | YAN32-200 (table de travail 1500 L-R x 1200 F-B) | USD26000 | 1 | 26000 |
|  | Moule combiné poinçonnage + alésage 15mm (5 tailles, 1.2mm) (220, 265, 320, 365, 420mm) | Cadre moulé | USD9600 | 1 | 960 0 |
|  |  | 5 tailles | USD8460 | 5 | 42300 |
| 18 | Compresseur à air à vis | SMAC-22KW | USD4890 | 2 | 9780 |
|  | Réservoir d’air | 2m3, 1MPa | USD1500 | 2 | 3000 |
|  | Sécheur à air | SMLG-5GF | USD1000 | 2 | 2000 |
|  | D’autres accessoires | Comme notre liste | USD3025 | 2 | 6050 |
| 19 | Cisaille manuelle | GS1000 | USD1500 | 1 | 0.00 |
|  |  |  | Réduction |  | -30750 |
|  | Total FOB Shanghai USD | 578710.00 |

C’est-à-dire, cinq-cent-quatre-vingt-un-milles deux-cent-dix dollars américains au total.

D’autres:

Délai de livraison:  90 jours après la réception de l’acompte.

Modalité de paiement: 15% T/T à l’avance, 85% avant l’expédition après l’inspection dans l’usine du vendeur.

Garantie :     14 mois à compter de la date de B/L ou 12 mois à compter de la mise en service.

Installation:      Excluant .   Formation gratuite.

Validité de devis:  30 jours

Informations Bancaires:

BÉNÉFICIAIRE: CHINA JIANGSU INTERNATIONAL ECONOMIC-

TECHNICAL COOPERATION GROUP LTD

Banque de notification: BANK OF CHINA, JIANGSU BRANCH

Adresse    : 148 ZHONGSHAN NANLU, NANJING, 210005, P.R.CHINA

SWIFT:   BKCHCNBJ940; A/C NO.:  532658191164

Vendeur: CHINA JIANGSU INTERNATIONAL ECONOMIC-

TECHNICAL COOPERATION GROUP LTD

-----------------------------------------------------------------

II Details quotation

- FIN PRESS  ZCPC-65

RE: C type FIN PRESS  Stroke: 120~200spm

Main performance features of ZCPC series:

● Composition: Aluminum foil uncoiled mechanism, oil tank, initial feeding equipment (option), closed high- speed precision

press, sucker collector, electric control system, pneumatic control system, hydraulic control,quick change die device, High and

reliable technology with Patent 1P/2P changing system;

● The slide has hydro-lifting function which will be convenient for dies installation/commissioning;

● Power press speed & vacuum sucker is controlled by inverter;

● Collector has protecting system for fault operation, material shortage warming, oil shortage warming;

● Hydraulic overload protection for main machine;

● Equipped with hydraulic rapid-dies changing device, making dies change more quickly and convenient;

● Touch screen and PLC electrical control system ensuring the reliable operation of the automatic stamping .

Main characters & function:

Technical Specs: ZCPC-65 Capacity 650KN Nominal pressure stroke 1.5mm Slide-strokes 40mm/ dia 9.52 fin die; 50mm/dia 12.7mm Fin die Stroke per minute 120~200spm; 120~180spm Die height Max 290mm Die height adjustment 75mm Table size 850*580*80mm Bottom size of slide 500×360mm Width of material 270mm / dia 9.52mm; 290mm / dia 12.7mm Stack length Max 1000mm Collecting height of material 600~800mm Coil ID x Coil OD Φ75mm/150mm×Φ850mm Main motor 5.5KW Weight 6000kgs Overall size 7200X2580X2950mm

Part chose:

  - Air valve—TACO (Japan)

  - PLC --- OMRON Japan

  - Converter: TECO Taiwan or DELTA Taiwan

  - Pneumatic Solenoid valves: Airtec ( Taiwan)

  - Electric components: TE (France) or LG ( Korea)

  - Pneumatic cylinder: Allgreat or SMC (Japan)

  - Induction switch & sensors & inductor: Autonics (Korea)

Optional  : USD5500 included

Industrial Touch-Screen controller

Photo-electric protecting device (not included)

Hydraulic overloading system:

- Re:Fin Die

2.1 FIN Die (1) : Conical collar base, Wave flat surface, Rippled fin edge

- Drawing to be issued for your confirmation

- SPECIFICATIONS:

(1) fins: ∮9.52mm*25*21.65*12R*2P

Tube diameter: ∮9.52

Fin hole: ∮9.83mm+/-0.03mm (ID)

Row Distance:21.65mm

Hole distance: 25mm

Collar height: 3~6 mm (according to fin drawings confirmed)

Fin thickness:0.15 to 0.20mm

FPI: 3 to 6

Fin Surface: plain flat surface

Fin edge: ripple fin edge

Numbers of rows: 12

Progress: 2P

With heating hole (no flaring)

- Die consists of draws, pierce extrudes, reflare, Edge trim, pilot, slit, feed and cut-off station

2.2 FIN Die (2) : Conical collar base, Wave flat surface, Rippled fin edge

- Drawing to be issued for your confirmation

- SPECIFICATIONS:

(2) fins: ∮12.7mm*41*35*8R*1P

Tube diameter: ∮12.7

Fin hole: ∮13.00mm+/-0.03mm (ID)

Row Distance:35mm

Hole distance: 41mm

Collar height: 6~9mm(according to fin drawings confirmed)

Fin thickness:0.32mm

FPI: 2 to 3

Fin Surface: plain flat surface

Fin edge: ripple fin edge

Numbers of rows: 8

Progress: 1P

- Spare tooling recommended as optional order (not covered in price)

|  | Items | U/price (USD) | Q’ty | TTL amount (USD) |
| --- | --- | --- | --- | --- |
| 1 | Pierce punch and die | 65.00 | 12 | 780.00 |
| 2 | Slitting blade | 100.00 | 4 | 400.00 |
| 3 | Edge-trim blade | 340.00 | 2 | 680.00 |
| 4 | Cut-off blade | 1100.00 | 1 | 1100.00 |
| 5 | Spring | 25.00 | 12 | 300.00 |
|  |  | TTL Amount USD USD | 3260.00 |

- Die consists of draws, pierce extrudes, reflare, Edge trim, pilot, slit, feed and cut-off station

- Re: Semi-Automatic Hairpin Bender

3.1 Model: ZJ-BU-9.52*4/1600

Main specs:

- It is suitable for T2M or TP2M Copper tube (straight)

- Tube specs: 9.52*4pcs     tube thickness: each 0.35mm

- Center distance of tube: ∮9.52mm*25mm

- It is max 04 pcs one specs  (number of tubes at a time: 4nos)

- Bending length: L200~1600 (stepless adjustable)  After bending size

- Bending angle = 180°

- Accuracy:

6.1 Bending ellipse degree: <0.5mm

6.2 Bending length accuracy in two end: 1mm

6.3 Bending area is without obvious deform, crack, wrinkles etc defects

6.4 Tube mouth should be even，max length error ≤ 1mm，cut tube is smooth, flat and without crack

- Bending speed: L=1000mm, 20s/cycle

- Power: 380V/50HZ/3PH

- Hydraulic pressure: 0-6Mpa

- Hydraulic oil: YA-46#, 150L

- Air pressure: >0.5Mpa, 1m3/h

- Oil pump: PV2R2-33-F-EAL,

- Oil pump motor: 3KW

- Water cooling system equipped

Main components:

- Hydraulic system: YUKEN (Japan)

- Pneumatic components:  SMC

- PLC: mustubish (Japan)

- Electric components: Fuji or Schneider

Standard accessories:

|  | Name | Unit | Qty | Note |
| --- | --- | --- | --- | --- |
| 1 | Fixing mandrel | pc | 20 |  |
| 2 | Swivel ball mandrel | pc | 20 |  |
| 3 | Stripper tube | pc | 15 |  |
| 4 | Special tools | pc | 1 |  |
| 5 | Wrench | pc | 1 |  |

Optional accessories :

|  | Name | Unit | Qty | U/price | T/Price |
| --- | --- | --- | --- | --- | --- |
| 1 | Swivel ball mandrel | pc | 20 | 35 | 700.00 |
| 2 | Stripper tube | pc | 15 | 18 | 270.00 |
| 3 | E_Magnitic vlave | unit | 2 | 40.00 | 80.00 |
|  | Total FOB Shanghai USD | 1050.00 |

3.2 Model: ZJ-BU-12.7*4/2500

Main specs:

- It is suitable for T2M or TP2M Copper tube (straight)

- Tube specs: 12.7*4pcs     tube thickness: each 0.40mm

- Center distance of tube: ∮12.7mm*41

- It is max 04 pcs one specs  (number of tubes at a time: 4nos)

- Bending length: L200~2500 (stepless adjustable)  After bending size

- Bending angle = 180°

- Accuracy:

6.1 Bending ellipse degree: <0.5mm

6.2 Bending length accuracy in two end: 1mm

6.3 Bending area is without obvious deform, crack, wrinkles etc defects

6.4 Tube mouth should be even，max length error ≤ 1mm，cut tube is smooth, flat and without crack

- Bending speed: L=1000mm, 20s/cycle

- Power: 380V/50HZ/3PH

- Hydraulic pressure: 0-6Mpa

- Hydraulic oil: YA-46#, 150L

- Air pressure: >0.5Mpa, 1m3/h

- Oil pump: PV2R2-33-F-EAL,

- Oil pump motor: 3KW

- Water cooling system equipped

Main components:

- Hydraulic system: YUKEN (Japan)

- Pneumatic components:  SMC

- PLC: mustubish (Japan)

- Electric components: Fuji or Schneider

Standard accessories:

|  | Name | Unit | Qty | Note |
| --- | --- | --- | --- | --- |
| 1 | Fixing mandrel | pc | 20 |  |
| 2 | Swivel ball mandrel | pc | 20 |  |
| 3 | Stripper tube | pc | 15 |  |
| 4 | Special tools | pc | 1 |  |
| 5 | Wrench | pc | 1 |  |

Optional accessories :

|  | Name | Unit | Qty | U/price | T/Price |
| --- | --- | --- | --- | --- | --- |
| 1 | Swivel ball mandrel | pc | 20 | 35 | 700.00 |
| 2 | Stripper tube | pc | 15 | 18 | 270.00 |
| 3 | E_Magnitic vlave | unit | 2 | 40.00 | 80.00 |
|  | Total FOB Shanghai USD | 1050.00 |

- Re: Automatic Coiled Tube Cutting Machine

Model: ZJ-QX-9.52*2 + 12.7*2

Copper size: 9.52mm*2pcs+ 12.7*2pcs

Tube length cut: 30mm, length: 3000mm

Hydraulic feeding with water cooling system

Feeding size: 1000mm max

Cutting method: Free scrap cutting

Servo motor feeding + ballscrew feeding

Adjustable manual-decoiler, ID: 134mm

4~5pcs/min (1000mm length)

Main motor: 5.5KW

Cutting motor: 1.5kw

PLC control: Mitsubishi

Accuracy: cutting ≤+/-0.5mm (1000mm length)

Straightening: ≤+/-3mm (1000mm length)

Manual adjustment of straightening wheels, 8pcs/set

Cutting blades: 12pcs + tool box + english manuals

1. This is burr free type, cutting blade size: 31x8x12mm

2. Spares: Blade – USD15.00/pc

- Portable Expander Model:ZSZ-9.52

|  | Maunal Expander: 1. Expanding specifications of copper tube: 12.7mm 2. Length of copper tube: 3000mm. (Tube after bending l ength:1500mm) 3. Center distance: 41mm * 0.32mm thickness 4. Max q’ty one time expander:02 pcs 5. Expanding method: 1 time expanding 6. Manual operation/adjustment 1. Pressure of hydraulic system: 70kgf/cm2 2. Motor: 3KW 3. Oil tank: about 45L 4. Emergancy stop 5. Overall size: 550x200x300 6. Expanding head: 4pcs, 7. Including 1set hydraulic station, 1 set frame, 1 set trolley, 2sets balancer, 2 sets expanding gear and flaring devices |
| --- | --- |

Extra head for dia 9.52* 25mm * 0.35mm

- Vertical Tube Expander  Model: AFPZ-1500

Main specs

Valid stroke of expanding pipe: 200-1500mm

Capacity: 42 holes/rows X 6 rows, Number: 252 holes ( to be cnfirmed by customer)

Smooth tube size:φ9.52mm x 0.35mm WT flat

Control way:manual-automatic shift

Speed of expanding pipe:5M/min(fast speed)or less

Motor power:15KW, 380V, 50Hz

Work pressure of hydraulic station:5-10MPa

Cooling water for hydraulic oil-pressure:0.2MPa

PLC control: Control: Mitsubishi

Emergency stop button

EL setting: small motor driving & micro-adjustment

2,3 time expanding mouth adjusting: small motor driving & micro-adjustment

1,2,3 time expanding: at same time

Max expand force: about 35 tons

Mechanic cycle time: about 25 sec

Overall size: about 2200x2200x4800mm

Expanding Way: 3 steps

Standard Accessories: Mandrel commissioning/releasing device Middle base plate & accessories Expanding accessories Pattern drawing plate accessories Base plate to Hair-pin receiver Expanding adjusting device

Stand tools including:

|  |  | Q’ty |
| --- | --- | --- |
| 1 | Expand rod | 144 |
| 2 | Expand head ( called bullet also) | 144 |
| 3 | Expand sleeve | 144 |
| 4 | Flaring sleeve receiving rod | 144 |
| 5 | Knock-out sleeve | 48 |
| 6 | Level insert acceptor | 72 |
| 7 | Slanting insert | 24 |

- RE: SHORT-U-BENDER MACHINE  Model: ZXU-9.52 (to make Elbow)

Main specs:

- Oval tube size: 9.52 * 25mm*3pcS, wall thickness: 0.32mm

12.7*41mm*3pcs, wall thickness 0.45mm

- Bending 3pieces at the same time.

- Speed :15s/time.

- PLC Controller

- Oil pressure: 60kgs/cm2 (for oil cooler)

- Air pressure: 4.5~6bar/cm2

- Mechanic/automatic operation,

- Tube-shortage showing

Two die:   1 die  9.52 * 25mm, wall thickness: 0.35mm

1 die  12.7*41mm, wall thickness 0.40mm

- RE: RING INSERTING MACHINE FOR WELDING MODEL: ZTH9.52

This machine is unfit to change die.

The machine is specially designed to insert the small ring to the small elbow, the welding ring and elbow were feeder separately by feeding and guider to the set position

Main specs:

Diameter of elbow: 9.52mm

Inserting position: 5mm or more from the end of elbow

Capacity: about 3000~3600pc/hour

Cycle time for inserting: 1s

Power: 380V/50HZ/3PH, Control power: DC 24V

Accuracy: 0.25mm

Pressure used: 5kg/cm2, 50NL/m

Environment temperature: 0—40 C degree, Humidity: 20—95%, Dust: little

Overall size: 1400x700x1200mm

- Re:Automatic welding machine Model:ZSH-1500

Main specs:

- Max coil height: max 1500mm ~ min 300mm

- Transmission belt: 26meter Length X 190mm Width

- Transmission speed: 0-3m/min

- Blow air pressure: 4kg/cm2

- Oil content rate inside furnace: <= 300PIM

- Air input pressure: 6-10kg/cm2

- Cold air blow pressure: 4kgs/cm3, 300m3/h

- Air working pressure: <=15kgs/cm2

- LPG gas: 7kg/cm2

- LPG working Capacity: 15m3/h, 0.5-1kg/cm2

- N2: 4-16L/min

- Motor: 3.5KW

- Max, height of solder: 1500mm machines type can be selected.

- The burners of special design: 4~6 pieces. Per burner carry angles: 20

- Special gas control cabinet, flow adjustable and with auto fire extinguishing. Strong fire   and feeble fire can be changed.

- The angle of welder muzzle can be adjusted, as you like.

- Welding gas: Liquefied petroleum gas and  Compress air

- It employs converter, welding speed is adjustable from 300 to 3000mm/min.

- Equipped with the independent welding protective system of Nitrogen with flux, and the independent system of Air cool fines.

- Suggestion:above 2000mm,pls welding by man-made, workpiece is too big,improve station may be more difficult

- Re: Chip-cleaning machine for Small U

|  | This machine is used to deal with kinds of small elbows at φ9.52 in heat exchanger. It can remove burring of massive elbows and clean them and make them dry at one time. 1. Feeder, which can convey the small elbows from storage hopper to vibrating grinding machine. The time and frequency can be set. 2. Cleaner, in which both elbows and grinding steel balls vibrate and they rub each other. In the meantime, cleaning agent (about 20min washing) at a certain dilution ratio is added continuously to wash the elbows and the wastewater is discharged. Thus the burring is removed. 3. Dryer, in which elbows automatically is aligned with openings downwards, so as to completely empty the grinding balls in the elbows and to dry them up by electrical heat-blower |
| --- | --- |
| II Main technical parameters Power supply elbow Size * height (mm) Water consuming Center Distance (mm) Air Pressure (Mpa) Quantity of elbows for one clean Clean speed (pc/min) Dimensions (cm) Weight 7.5kW Dia 9.52 mm 0.3Mpa, 80L/h 1~30mm 0.5~0.7 1800 about 70 382*122*192 1500kg |

Stainless steel ball: 1Cr18Ni9Ti required

PLC control: Omran (Japan)

Pnematic parts: SMC (Japan)

Main electric parts: Chneider, Omron, fuji etc

- Re: Manual Hairpin Bender Model: ZJMB- 5/8”, 3/4”, 7/8”

|  | Main specs: It is suitable for T2M or TP2M Copper tube (straight) Tube specs:5/8”, 3/4”, 7/8” Air cylinder feeding It is max 01 pcs one specs Bending length: L100~1000 Bending angle = 180° |
| --- | --- |

CNC Punching Machine from Qingdao AMADA

Press brake, shear from Nantong New Atlantic

Air compressors as per separate File

More specs:

Fin: H22, 8011

Tube: TP2M, Soft

- FIN  DIE  ONE  Φ12.7x41+35x8Rx1P

FIN =0.32mm

Collar height=6~9mm

Width of coil=290mm, ID of coil=Φ75mm

Stroke of press=50mm

- Long U tube Φ12.7x0.4mm thickness

Φ9.52x0.35mm thickness

- Small U Φ12.7x0.65mm

Φ9.52*0.5mm

- Other tube

Φ5/8”x0.6mm

Φ3/4”x1mm

Φ7/8”x1mm

5. Fin die two  Φ9.52x25x21.65x12Rx2P

Fin =0.15-0.2mm

Collar height=3~6mm

Width of coil=270mm, ID of coil=Φ75mm

Stroke of press=40mm

With heating hole (no flaring)

- Vertical expander

4Rx14 hole x 2pcs/expanding

>14 hole x 1pcs/expanding

Fin die Φ9.52; fin thickness: 0.13~0.20mm

| Fin thickness (mm) | Collar height (mm) | FPI |
| --- | --- | --- |
| ~0.13 | 3 | 8 |
| ~0.15 | 4 | 6 |
| ~0.2 | 8 | 3 |
| ~0.18 | 6 | 4 |

Rules of fin

Collar height=25.4/number of FPE - FIN thickness

Fin die Φ12.7; fin thickess: 0.32mm

| Fin thickness | Collar height | FPI |
| --- | --- | --- |
| 0.32 | 6~9mm | 3~4 |
| 0.25 |  |  |

------- the end -------------