ICESTA QUOTE

FOR 10T/24H CUBE ICE MACHINE

- Customer’s Details

Company name:

Address: Cote D'Ivoire

Contact Person: Olivier KOUKOUA

Email: koukoua@yahoo.com

Tel: (225) 07 69 85 35

- ICESTA Quote Reference Number: ICT-CIV-20160509

- What is included in the quote

  - 1 No. of 10T/24H Cube Ice Machine

- Detailed Spec Sheet

Parameters of 1T Block Ice Machine

| NO. | Parameter | IC-10T |
| --- | --- | --- |
| 01 | Ice Capacity | 10t/24h |
| 02 | Compressor | Bitzer |
| 03 | Refrigeration Capacity (KW) | 100 |
| 04 | Evaporating Temp (℃) | -12 |
| 05 | Condensing Temp (℃) | 40 |
| 06 | Total power (KW) | 53.15 |
| 07 | Compressor Input Power (KW) | 45.8 |
| 08 | Power of cooling tower motor fan (KW) | 1.5 |
| 09 | Power of cooling water pump (KW) | 4 |
| 10 | Pump for evaporator | 1.1 |
|  | Ice outlet power | 0.75kw |
|  | Cooling water consumption | 0.05 m3/h |
| 11 | Power Supply | 3P/ 380V/ 50Hz |
| 12 | Refrigerant | R404a |
| 15 | Standard Ambient Temp (℃) | 30 |
| 16 | Max. Ambient temp (℃) | 45 |
| 17 | Standard Water Temp (℃) | 23 |
| 18 | Ice temp. (℃) | -10 |
| 19 | Dimension of machine | 5750*1780*2000mm |
| 20 | Freezing time | 16-18 minutes |
| 21 | Ice density | 500~550kg/m3 |
| 22 | Ice storage bin capacity | 800kg |

Note: The above data is for your reference and is subjected to final design.

- Main Component List

| No. | Component | Brand | Remark |
| --- | --- | --- | --- |
| 01 | Compressor | Germany BITZER |  |
| 02 | PLC | Germany Siemens |  |
| 02 | Solenoid Valve | Denmark DANFOSS |  |
| 03 | Expansion Valve | Denmark DANFOSS |  |
| 04 | Oil filter | America Emerson |  |
| 06 | High and low pressure meter | Switzerland REFCO |  |
| 07 | Electrical components | South Korea LG (LS) |  |
| 08 | Circuit Breaker | SCHNEIDER |  |
| 09 | Contactor | SCHNEIDER |  |
| 10 | Thermal Relay | SCHNEIDER |  |
| 12 | Condenser | UAR/CHINA |  |
| 14 | Filter Dryer | FASIKE |  |
| 15 | Recycling pump | MINAMOTO |  |
| 16 | Water Pump | CNP(CHINA) |  |
| 16 | Cooling tower | LINGDIAN(CHINA) |  |

Note: The above data is for your reference and is subjected to final design.

- Photos-10T Cube ice machine and cube ice

- CFR Abidjan, Côte d'Ivoire Price in US Dollar

| ITEM | Model Number | Capacity | UNIT PRICE (USD) | QTY | TOTAL(USD) |
| --- | --- | --- | --- | --- | --- |
| Cube ice machine | IC-10T | 1t/daily | $ 63,495 | 1 | $63,495 |
| Sea freight | 1 | $1800 |
| CFR Abidjan, Côte d'Ivoire Total amount in USD | US $65,295 |
| CFR Abidjan, Côte d'Ivoire US Dollars sixty five Thousand and two hundred and ninety five Only. |

- Business Terms

    - 30% advance payment is made upon confirmation of order as deposit; 70% balance payment is paid before delivery of goods

    - Delivery Time: 40-45 days upon arrival of the advance deposit.

    - Warranty Period: 12 Month upon date of Bill of Lading

    - Documents required: Original signed Commercial Invoice and Packing List, Original Bill of Lading and Certificate of Origin.

- Company showcase

Office

warehouse

Factory#1

Factory#2

Thanks for your reviewing and precious time. Welcome to visit us at any time.

We are the Best ice plants manufacturer for you!

ICESTA Ice Systems

(the reliable and Creditworthy enterprise)

dated on May 9,2016

Vivian