报 价 单   (共9页）

Quotation  （total 9 pages)

JDCPE 90/60-1000 两层共挤缠绕膜生产线

JDCPE 90/60-1000 High Speed Stretch Film Co-extrusion Line

日期（Date）：May 13，2016

SUPPLIER:

浙江建达机械有限公司

Zhejiang Jianda Machinery Co., Ltd.

电话(Tel):0086-577-65159968

传真(Fax):0086-577-65599887

Http://www.jiandajx.com

E-mail:jd@jiandajx.com,  msn messenger: jiandajxa@hotmail.com

TO:

编    号:

Quotation No.

客户名称: 
Name of customer: :
客户电话:

Tel of Customer:

Machine reference picture: :

Short video link:  http://en1.jiandajx.com/about7shows_7.html

设 备 规 格

Equipment specifications

| 序号 no | 品名 name | 数量 quantity | 说明 Description |
| --- | --- | --- | --- |
| 1 | SJ90挤出机（A） SJ90 extruder( A ) Screw L/D ratio: 34:1 | 1台 1 set | 采用铸铝加热，高精度温控仪控制温度。 配55KW变频电机和松下变频器控制。 Using aluminium casted heater, temperature control by high precision temperature controller Equipped with 55KW frequency conversion motor and control by Panasonic inverter. |
| 2 | SJ60挤出机（B） SJ60 extruder (B) Screw L/D ratio: 34:1 | 1台 1 set | 采用铸铝加热，高精度温控仪控制温度。 配22KW变频电机和松下变频器控制。具有节能省电，控制精度高等特点。 Using aluminium casted heater, temperature control by high precision temperature controller Equipped with 22KW frequency conversion motor and control by Panasonic inverter. |
| 3 | 自动上料机 Automatic feeding loader | 2台 2 sets | 上料能力100--200Kg/h. feeding capacity100--- 200Kg/h 打胶设备：1套 Glue feeding motor & pump: 1 set |
| 4 | 换网装置 Screen changing device | 2套 2 sets | 液压换网站 Non-stop hydraulic net changer station; |
| 5 | A/B分配器 A/B distributor | 1套 1 set | Distributor heating power: 6kw |
| 6 | 负压定型装置 Minus pressure shaping device | 1套 1 set | 负压风机功率： 1.5KW, 数量：2个 Minus pressure air blower power: 1.5kw * 2 pcs |
| 7 | 1250mm流延模头 1250mm cast die head (cloth hanger design) | 1套 1 set | Finished film thickness: 0.015-0.03mm Die material: Sm3Cr2Mo Heating power: 22.4kw Size: 1292*160*244 mm |
| 8 | 牵引冷却装置 traction & cooling part | 1套 1 set | Traction driving motor power: 4kw Cooling roller：Ф600mm, length:1300mm traction roller：Ф268MM, length:1300mm Traction small roller: Ф80mm, 2pcs, length: 1300mm |
| 9 | 摆动装置 Oscillating device | 1套 1 set | oscillating motor: 0.18kw Gearbox ratio: 1:1200 |
| 10 | 自动卷取装置 automatic winding part | 1套 1 set | 自动裁切&自动换卷 With automatic cutting & winding system Winding roller：Ф345MM, length: 1150mm Smooth roller: Ф119MM, length: 1150mm Rubber roller: Ф118MM, length: 1150mm Winding motor：2.2KW Edge trimmed film recycling & directly feeding into hopper Air expanding roller：Ф74mm, 2pcs, length: 1150mm Automatic meter counting system |
| 11 | 电器配置 Electronics |  | 变频器: 欧瑞/台达/松下 Inverter: Eura/Delta/Panasonic 电机： 西门子 Motor: Siemense PLC: 松下 PLC: Panasonic 触摸屏： 台湾海泰克 Touch screen: Taiwan, Hi-tech 温控仪表: 汇邦（江苏） Temperature controller: WINPACK(JIANGSU) |
| 12 | Accessories for your option: | 1) 2) 3) | 20p water chiller: 7,000usd/set fob 1.1cube meter air compressor: 2,500usd/set fob JDARW-500B automatic stretch film rewinder: 10,000usd/set |

# 1) JDQL-20P WATER CHILLER

- technical parameters:

Cooling capacity: 56678 w

48800kcal/hour

193638Btu/hour

Input power:16.8 kw

II. Machine picture:

2) 1.1 cube meter air compressor:

1.technical parameters

flux capacity: 1.1m3/min

Motor power:7.5kw

2. Picture for reference

3) JDARW-500B全自动复卷机

JDARW-500B automatic stretch film rewinder

MAIN TECHNICAL PARAMETERS:

| Model 型号 | JDARW-500B |
| --- | --- |
| Main motor power 主电机功率 | 4kw |
| Unloading motor power 卸卷电机 | 0.55kw |
| Mother roll diameter 母卷直径 | ＜400mm |
| Mother roll width 母卷宽度 | Not more than 500mm |
| Mother roll paper core dia. 母卷卷芯规格 | 3” |
| Finished roll diameter子卷直径 | ＜150mm |
| Finished roll width子卷宽度 | 300-500mm |
| Finished roll paper core dia. 子卷卷芯规 | 1.5” 2” 3” |
| Cutting way 切断方式 | Cutting by resistance wire heating |
| Error corrcetion way 纠偏方式 | JOG |
| Rewinding type 复卷形式 | Friction winding |
| Working speed 工作速度 | Max.1000m/min |
| Machine Size 机器尺寸 | 2400*1450*1550mm |
| Machine weight 机器重量 | 750kg |
| Power supply 电源电压 | 380v/3/4/50 |
| Note: the machine is now updated with discharge/unloading table |
| Short video link: http://v.youku.com/v_show/id_XODIyMTE3Nzcy.html |

- Machine photo for reference:

商务条款

Business clause

- Price: JDCPE-90/60--1000 stretch film coextrusion machine: 92,000usd/set fob

20p water chiller: 7,000usd/set fob  (for your option)

1.1cube meter air compressor: 2,500usd/set fob (for your option)

- Term of payment: 30% of the total amount should be prepaid as deposit by T/T, balance payment 70% of

the total amount shall be paid up by T/T after inspection and qualified in seller's factory before delivery.

- Delivery date: 30 days since the receipt of deposit in seller’s factory.

- Packaging: sea worthy packaging with air bubble film or stretch film.

- Guarantee: 1 year

- The seller shall send the technicians to buyer’s factory cover installation, commissioning, guide and train the buyer’s workers for 7 days; visa, round way tickets, hotel & food are borne by Buyer, over 7 days, Buyer shall pay the technician 100usd/day as salary.

- Valid period of offer: 30 days.