AFD-600 ALUMINUM FLEXIBLE

DUCT FORMING MACHINE

This machine is specially for producing aluminum flexible ducts with aluminum foil or metalized PET film with steel wire reinforced for ventilation purpose.

I Main technical data

1.1 Diameter range: 80mm~600mm

1.2 Length of aluminum tube: 1-10m

1.3 Raw material: metalized PET film, 0.012mm, width 35-50mm (or pure aluminum foil 0.025~0.035mm); Steel wire 0.8-1.4mm dia

1.4 Dimension (L x W x H): 2200 x 820 x 1550mm

1.5 Weight: 500kg

1.6 Main motor power: 1.5kW

1.7 Temperaute: 40~120 centigrade

1.8 Electric heating power: 2.4kW

1.9 Working speed: 1-35 m/min, adjutable

1.10 Features of finished ducts:

Temperature resistance: -30°C-140°C

Max. air flux: 30m/s

Max. working pressure: 2500Pa

Pitch between corrugations: 20mm

II Working flow:

2.1 Brewaging glue: Mix activator, glue and thinner in the ratio 1:10:20. And then put the mixture into the glue tank, till reaching the needed level

2.2 Before starting work, first heat the oven, after the temperature reach 40 degree in the temperature meter, adjust the meter to 35 degree, then start work.

2.3 Select suitable mould and mount on the machine head, install the transmission belt, adjust the mould.

2.4 Lead aluminum foil through glue-applying roller, heating oven and then to the machine head.

2.5 Put steel wire between the aluminum foil, press the heating device, start the machine and adjust the speed.

2.6 Inspect whether the foil is even and whether the wire is exposed.

III Price

Price basis: FOB Shanghai

Payment: 30% down payment by T/T, the balance down before shipment

Lead-time: within 20 days after receiving down payment

Unit price: USD 6,950 (with one dia 300mm)

Note: Extra cost for dies：

- 100mm, USD 198

- 150mm, USD 295

- 200mm, USD 390

- 250mm, USD 480

- 300mm, USD 580

- 350mm, USD 675

- 400mm, USD 770

- 450mm, USD 875

- 500mm, USD 960

IV Guarantee: one year since the date of B/L

V After-sale service: Should need mounting & adjusting service abroad, all the relative charges such as visa, safety insurance, round flight tickets, boarding & lodging, labor charges USD 200 per day, will be borne by buyer.