YQ SERIES 2-POINTED TOOTHPICK MACHINE LINE

Quotation: 11800 USD (EX-WORK)

Video Link: http://v.youku.com/v_show/id_XMjIwMzYzMzMy.html

The quotation above contains each set of following ten machines. The daily production comes to 500000PCS/8 hours(about 80kg). However adding one more YQ-642 (2000USD) will double the daily production. Such as: if you have 6sets YQ-642, the output will be 3,000,000pcs/8hours.

Generally, each 100kg fresh (wet) bamboo can bring you 120000 to 150000 toothpicks in size of φ2.0mm-diameter,65mm-long.(about 18kg toothpicks)

| ITEM | QUANTITY | PARAMETERS FOR EACH ITEMS | PICTURE (FOR YOUR REFERENCE) |
| --- | --- | --- | --- |
| 1, YQ-791 Raw Bamboo Sawer | 1 | Parameter: Electrical Requirement: 380V, 50Hz, 3Phases, 1.5Kw Weight: 58Kg Dimension: 1000*600*1150mm |  |
| 2, YQ-388 Bamboo Slitter | 1 | Parameter: Feeding Speed: 1.5m/s Electrical Requirement: 380V, 50Hz, 3Phases, 4Kw Weight: 650Kg Dimension: 3100*700*1250mm |  |
| 3, YQ-275 Fixed Thickness and Width Slicer | 1 | Parameter: Feeding Speed: 85m/min Electrical Requirement: 380V, 50Hz, 3Phases, 3.3Kw Weight: 310Kg Dimension: 1300*650*1030mm |  |
| 4, YQ-144 Bamboo-wool Shaper Former | 1 | Parameter: Feeding Speed: 80m/min Electrical Requirement: 380V, 50Hz, 3Phases, 8.2-10.2Kw Weight: 400Kg Dimension: 1000*650*1100mm |  |
| 5, YQ-741 Bamboo Wool Block Ruler Fixer | 1 | Parameter: Saw Specification: 300*25*2*150T Electrical Requirement: 380V, 50Hz, 3Phases, 0.75 Kw Weight: 80Kg Dimension: 1400*660*900mm |  |
| 6, YQ-746 Toothpick Ruler Fixer | 1 | Parameter: Saw Specification: 180*25.4*1.5*80T Electrical Requirement: 380V, 50Hz, 3Phases, 3.37 Kw Weight: 125Kg Dimension: 850*650*900mm |  |
| 7, YQ-516 Toothpick Polisher | 1 | Parameters: Volumn: 0.56m2 Electrical Requirement: 380V, 50Hz, 3Phases, 1.5 Kw Weight: 130Kg Dimension: 1300*1100*1300mm |  |
| 8, YQ-948 Toothpick Orgnizer | 1 | Parameters: Speed: 20000PCS/Min Electrical Requirement: 380V, 50Hz, 3Phases, 0.55 Kw Weight: 80Kg Dimension: 1000*1000*750mm |  |
| 9, YQ-642 Toothpick Points Sharpener | 1 | Parameters: Speed: 1700PCS/Min Electrical Requirement: 380V, 50Hz, 3Phases, 1.99 Kw Weight: 210Kg Dimension: 1050*650*950mm |  |
| 10,YQ-803 Multifunctional Blade Sharpener | 1 | Parameters: Electrical Requirement: 380V, 50Hz, 3Phases, 0.37Kw Weight: 65Kg Dimension: 700*500*950mm |  |