Quotation

| Our Ref No. |  | Date:July 1st, 2016 |
| --- | --- | --- |
| To: |  | ICESTA Ice Systems |
| Attn: |  | From: Ms. Sharon |
| Email: |  | Email : sharon@icesta.com |
|  | Tel:+86- 0755-29914211 Fax: +86-0755-29914210 |
| Subject: | Quotation for 1ton block ice machine |

This program includes the following:

1) Quotation for the equipment

2) Technical parameter and components list

3) Principles for Guarantee and technical support

4) Photos gallery for block ice machines

5) Working partners

1).Quotation for 1Ton block ice machine

| Item No. | Model | Capacity(T/24h) | Unit price (USD) |
| --- | --- | --- | --- |
| Block ice machine | IB1T-R2W | 1t/24h | 5,850.00 |

IB1T-R2W: including refrigerating unit, cooling tower, water pump, connecting PVC pipes,connecting power line,pouring into brine to the scale mark after clean the brine tank, pouring into clean water to the scale mark after clean the ice rind (water pipes and wires not included, match one-time use solid salt)

COMMERCIAL ITEMS

| Remarks |  |
| --- | --- |
| Trade terms | FOB Shenzhen Port |
| Payment terms | Telegraphic Transfer. 30% deposit after PO confirmed. Balance paid before delivery. |
| Delivery | 25~30 days after deposit, depends on model and quantity |
| Package | Standard Wooden package |
| Validity | 30days |
| Warranty period | 1 year after B/L date. Any failure occurred within the period due to our responsibility, we'll supply you the spare parts for free, and permanent technical support & consultation all life long for the machines. |
| Note |  |

- . Block Ice Machine Technical Parameter

Block Ice Machine Technical Parameters IB1T-R2W

| Model Parameters | IB1T-R2W |
| --- | --- |
| Compressor Model | 4TES-9 |
| Design capacity | 1000kg/24h |
| Refrigeration capacity | 17.9 kw |
| Evaporating temp. | -15℃ |
| Condensing temp. | 40℃ |
| Total input | 6.77 kw |
| Power of compressor | 4.74 kw |
| Water pump of cooling tower | 0.75 kw |
| Power of cooling fan | 0.18 kw |
| Water pump input | 1.1 kw |
| Power of electric hoist | 0.4 kw |
| Power supply | 380V/3P/50HZ 220V/3P/50HZ |
| Water feeding pressure | 0.1Mpa－0.5Mpa |
| Refrigerant | R22 |
| Design ambient temp. | 30℃ |
| Design water inlet temp. | 20℃ |
| Ice temp. | -10℃ |
| Each weight of the block ice | 25kg |
| Dimension of ice (MM) | 390*120*600 |
| Each freezing time (H) | 11h |
| Each doff ice time (H) | 0.4h |
| Ice Machine Diameter (MM) | 1800*1000*1350 |
| Dimension of cooling tower (MM) | φ920*1830 |
| Unit weight | 5.5t |
| Unit Operating Weight | 9t |

3). Guarantee, technical support and failure claim procedures

- All Icesta ice systems delivered to customers are carefully examined and tested, with 72 hours trouble-free trial operation.

- All ICESTA ice systems delivered are plug-in ready and well piped.

- All ICESTA ice systems enjoy 1 year guarantee ever since B/L date.

Technical support

- ICESTA provide full technical support and training courses after equipment installation and commissioning.

- 7*24 hours phone assistance on technical support.

Failure Claim procedures

- Detailed written failure description is required by fax or by mail, indicating the relevant equipment information and detailed description of failure.

- Relevant pictures are required for failure confirmation.

- ICESTA engineering and after-sales service team will check and form a diagnosis report.

- Further trouble-shooting solutions will be offered to customers within 24 hours after receiving the written description and pictures.

4) Photos gallery

5). Working partners worldwide in variety industries

Seafood Industry

Construction and concrete cooling industry

Meat processing Industry

Poultry Slaughtering

Super market and Chain stores