SPIRAL TUBEFORMER BTF-2000

This machine line is for producing round air duct for various uses, such as for HVAC round ducts, oval ducts, chimney flue, etc.

I Advantages

1.1 Special casting steel mould, light & long life.

(Aluminum alloy one is optional)

1.2 Two cutting way include automatically saw cutting and plasma cutting.

1.3 Large diameter range

1.4 PLC control, convenient operation

1.5 Auto unloading rack, low labor cost

II Main technical data

2.1 Diameter of round tubes: 100mm ~ 2000mm.

2.2 Max. Tube length: 8000mm.

2.3 Thickness of strip: 1.2mm-2.0mm

2.4 Width of strip: 155mm

2.5 Strip speed: 1~30m/min, adjustable

2.6 Suitable strip material: aluminum, stainless steel, galvanized steel, color coated steel, etc.

2.7 Weight: 2500kg

2.8 Power of main motor: 22kw

2.9 Power of hydraulic motor: 0.75kw

2.10 Power of cooling water pump motor: 125W

2.11 Power of material feeding motor: 125W

III Main configuration

3.1 Uncoiler: mechanical expanding type, capacity 1200kg, inner diameter range 480-610mm, outer diameter 1000mm.

3.2 Control system: Mitsubishi inverter, PLC control

3.3 Driving system: Spiral subulate gear type decelerator (low noise, large moment)

3.4 Material of forming rollers: GCr15 bearing steel, quenched, HRC58-62

IV Accessories accompanied with the machine

4.1 Unloading rack: one set, 3000mm each

4.2 Four press-adjusting rollers (changed to suit different thickness)

4.3 One set of special tools.

V Mounting way

VI Best Offer:

Price basis: FOB China.

Payment: 30% down payment by T/T in advance, the balance by irrevocable L/C at sight

Lead-time: within 45 days after receiving down payment

Unit price: USD 46,800 (include one die less than 300mm)

Cost of dies: USD 450 for Diameter from 100~500mm

USD 580 for Diameter from 500~1000mm

USD 680 for diameter above 1000mm

Note: 1. Above price is net price excluding mounting and adjusting service abroad. Should needed, relative charges and costs, such as visa, round flight tickets, boarding & lodging, labor cost USD 200 per day, etc., will be borne by buyer. This service period will be no longer than 15 days.

2. Whether buyer needs service abroad or not, we request buyer to send one or two technicians to our factory to be trained here. We can supply free boarding & lodging.

VII Guarantee: One year since the date of B/L.