Automatic Chicken Nuggets Production Line (LTNP-600) (totally 2 pages)

No matter meat, seafood, poultry or vegetable, the production line can fulfill the processing procedure of forming, preduster (flavor), battering, breading etc. The equipment can be connected to the fryer, cooking apparatuses, instant freezer and packing machine to match a full automatic processing line to produce several of popular foodstuffs. The raw materials that it can use include pork, beef, chicken, fish, onion, potato and so on. This production line includes the following machines: (Capacity: 500-1000kg/h)

| No. | Item | Function | Parameter | Quantity (Set) | Price (USD) |
| --- | --- | --- | --- | --- | --- |
| 1 | Automatic Forming Machine LTHF-600 | Forming the meat paste or granular into various shapes | Belt Width: 600mm, Power: 15.12kw, Burger thickness: 6-40mm Maximum diameter: 150mm (round burger) Overall dimension: 3170×1170×2430mm | 1 |  |
| 2 | Battering Machine Model 600 | Covering Batter(flour paste) on nuggets | Belt Width: 600mm; Power: 2.6kw, Belt Speed: 3~15m/min Input height: 1050±50mm, Output height: 1050±50mm Dimension: 2100×1035×1450mm | 1 |  |
| 3 | Preduster with Air Flow System Model 600 | Covering flour&flavor on nuggets | Belt Width: 600mm; Power: 2.93kw, Belt Speed: 3~15m/min Input height: 870~970mm, Output height: 1000±50mm Dimension: 2650×1035×2150mm Air Flow System collecting the dust of flour and keep the room clean (power: 1.5kw) | 1 |  |
| 4 | Battering Machine Model 600 | Covering Batter(Tempura) on nuggets | Belt Width: 600mm; Power: 2kw, Belt Speed: 3~15m/min Input height: 1050±50mm, Output height: 1050±50mm Dimension: 2100×800×1450mm | 1 |  |
| Total Price | FOBQingdaoUSD |

Flow chart: Forming(Battering(Predusting(Battering (Tempura)

Factory Picture: