HD-400 High Speed Automatic Paper Food Bag Machine

Quotation:45000USD,FOB,Shanghai( including 4 sets of bag forming moulds)

Picture for reference

This machine is built to make paper rolls or printed-paper rolls into bags for packing fast food like bread, loaf, KFC. Paper Baguette bags. It is equipped with HMI for easy operation; with photocell for make the same printed paper bags. The bags can be many different dimensions.

| Paper Gram Weight (g/㎡) | 40-80 |
| --- | --- |
| Bag length (mm) | 160-440 |
| Bag Width （mm） | 80-250 |
| Bag Side Width （mm） | 20-100 |
| Paper Roll Width (mm) | 230-720 |
| Maximum Paper Roll Width (mm) | 1200 |
| Speed | 100-400bags/min. |
| Total Power (kw) | 10 |
| Machine Weight (Ton) | 3.5 |
| Machine Dimension (L*W*H) | 4500*1500*2100mm |

| Main Components of HD-400 High Speed Paper Food Bag Machine |
| --- |
| No. | Name | Model | Specification | Quantity | Brand | Country |
| 1 | Servo Drive | SGDM-50ADA | 5.0KW | 2 | Yasakawa | Japan |
| 2 | PLC | DVP | 32EH | 1 | Delta | Taiwan |
| 3 | Servo Motor | SGDV-330A01A | 4.4KW | 2 | Yasakawa | Japan |
| 4 | Human-interface screen | DOP | B10S411 | 1 | Delta | Taiwan |
| 5 | Switching power supply | DVP-PS02 | 2.1A | 1 | Delta | Taiwan |
| 6 | Optoelectronic switch | LTK-1180 |  | 1 | Omron | Japan |
| 7 | AC contactor | CJX2-5011 | 50A/220V | 1 | Schneider | Franch |
| 8 | Solid-state relay | SSR-10DA | 10A | 2 | Schneider | Franch |
| 9 | Intermediate relay | JZX-22FD/3Z | DV24V | 1 | Schneider | Franch |
| 10 | Circuit Breaker | DZ47-60 | C32/C5/C1 | 5 | Schneider | Franch |
| 11 | Position switches | YBLX-K1/411 | 5A | 3 | Schneider | Franch |
| 12 | Ultrasonic sensors for glue system | QS | 18UNA | 1 | Bonner | America |
| 13 | Proximity switch | NPN |  | 2 | Omron | Japan |
| 14 | Buttons | LA39B3-11x/k | Rotary | 4 | Schneider | Franch |
| 15 | Relay | JZX-22FD/3Z | DV24V | 2 | Schneider | Franch |
| 16 | Button | NP3-1 | Inching | 1 | Schneider | Franch |
| 17 | Filter pressure regulating valve | AFR20 |  | 1 | Airtac | Taiwan |
| 18 | Magnet Braker | EPCB-K | 2.5kg | 1 | YAN-CLUTCH | TAIWAN |

Machine Photo / Parts & Samples

Cold Glue System

Samples of bag:

After sale services and component replacement

During the period of quality guarantee, we supply the spare part in free for replacement.

Packaging

Adopts moisture-proof and shock-proof packaging which is suitable for long-distance road transportation and various types of weather conditions. A full set of maintenance and operation manuals is included.

Delivery Date

Within 35 days after payment of deposit.

Terms of Transportation

Seller shall deliver equipment at its factory and may arrange transportation for Buyer but freight shall be for Buyer’s account.

Terms of Payment

30% deposit by T/T upon final confirmation; balance by T/T or L/C before shipment.

Quality Assurance

Seller provides a 2 years guarantee period. All spare parts free of charge in one year time.

Training, Installation and Test Run

Installation and training are done by our technician at buyer’s factory(normally 20 days). The flight tickets, accommodation & traffic expenses and service fees at USD50/day shall be borne by the buyer.

# Text boxes

Air shaft with Hydraulic System

Photo-cell for printed paper