Fax:(+86)10-81769546   Email:manufacturer@bjfth.com     Web:www.bjfth.com

| 参数Parameter 车库种类Model | 垂直循环式立体停车设备 Vertical Rotary Car Parking System |
| --- | --- |
| 产品型号Type | PCX |
| 停车数量Car no. | 8P/10P/12P/14P/16P |
| 适停车辆Car size | Z:5000*1800*1550 D: 5300*1850*1550（SUV）5300*2100*2000（Customized） |
| 车辆重量Car weight | ≤1800kg |
| 设备占地面积Land aera | 6500*5500 |
| 设备层数及高度 Layer&height | 高度Height 规格 Model | 5层8车 8cars for 5 layers | 6层10车 10cars for 6 layers | 7层12车 12cars for 7 layers | 8层14车 14cars for 8 layers | 9层16车 16cars for 9 layers |
|  | 普通车型(Sedan) (n-3) 1.84+6.3m | 10m | 11.8m | 13.7m | 15.5m | 17.3m |
|  | SUV车型 （n-3）*2.3+7.2米 | 11.8m | 14.1m | 16.4m | 18.7m | 21m |
| Max in-out time | 90~150s |
| 整机功率Power | 7.5KW/9.2KW/18.5KW |
| 控制方式 Control type | PLC自动控制 PLC full-automatic |
| 操作方式Operate type | 按键/IC刷卡(或ID)刷卡 Button/IC(ID) card |
| 电源 Power supply | 380v/AC 50hz |
| 噪音Noise | ≤65db |
| 进出口方式 In and Out type | 前进入库 Forward parking |
| 使用寿命 Lifetime | 30年 30years |
| 出厂价 EXW price | 8cars for 5 layers USD5500/parking space |
|  | 10cars for 6 layers USD6200/parking space |
|  | 12cars for 7 layers USD6500/parking space |
|  | 14cars for 8 layers USD6800/parking space |
|  | 16cars for 9 layers USD7200/parking space |
| NOTE | SUV price should be pay extral USD300 per unit on the basis of above price |