Quotation

| Our Ref No. |  | Date:September 19th, 2016 |
| --- | --- | --- |
| To: | Abu-saleh | ICESTA Ice Systems |
| Attn: |  | From: Ms. Sharon |
| Email: | benhumaeed.ms@gmail.com | Email : sharon@icesta.com |
|  | Tel:+86- 0755-29914211 Fax: +86-0755-29914210 |
| Subject: | Quotation for 1ton tube ice machine |

This program includes the following:

1) Quotation for the equipment

2) Technical parameter

3) Photos gallery

4). Working partners

1).Quotation for 1Ton tube ice machine

| Item No. | Model | Capacity(T/24h) | Unit price (USD) |
| --- | --- | --- | --- |
| Tube ice machine (air cooling) | IT1T-R2A | 1t/24h | 10,420 |

COMMERCIAL ITEMS

| Remarks |  |
| --- | --- |
| Trade terms | FOB SHENZHEN Port |
| Payment terms | Telegraphic Transfer. 30% deposit after PO confirmed. Balance paid before delivery. |
| Delivery | 30days after deposit, depends on model and quantity |
| Package | Standard Wooden package |
| Validity | 30days |
| Warranty period | 1 year after B/L date. Any failure occurred within the period due to our responsibility, we'll supply you the spare parts for free, and permanent technical support & consultation all life long for the machines. |
| Note |  |

2) Tube Ice Machine Technical Parameter

Tube Ice Machine Technical Parameters IT1T-R2A

| Model Specification Parameters | IT1T-R2A Bitzer |
| --- | --- |
| Compressor Model | 5HP |
| Ice output | 1t/24h |
| Ice tube diameter | φ29 |
| Cooling Capacity | 11.3 |
| Evaporating temperature | -15 |
| Condensing temperature | 40 |
| input power | 6.26 |
| Compressor input power | 4.74 |
| Ice cut reducer input power | 0.37 |
| Water pump input | 0.55 |
| Condenser Fan input power | 0.6 |
| Power supply | 3P/380V/50Hz |
| Water Pressure | 0.1Mpa－0.5Mpa |
| Refrigerant | R22 |
| Standard ambient temp. | 30℃ |
| Standard Water Temp. | 20℃ |
| Water Consumption(M3/h) | 0.042 |
| Water supply tube Diameter | 1-1/4" |
| Overflow pipe | 1" |
| Drain pipe | 1" |
| Ice machine Weight | 950 |
| Ice Machine Diameter (mm) | 1400*1300*2000 |

3) Photos gallery

4). Working partners worldwide in variety industries

Seafood Industry

Construction and concrete cooling industry

Meat processing Industry

Poultry Slaughtering

Super market and Chain stores