Quotation  Sheet

Quotation No.: SN20161009-BV-10                                        Dated: 9th October, 2016

Submitted to : 玻利维亚华商总会

Subject: Supply 5T/day Tube Ice Machine With Complete Refrigeration System.

Price & Commercial Term

| Item | Commodity&Specification | Quantity | Unit price （USD） | Amount （USD） |
| --- | --- | --- | --- | --- |
| 1 | Tube Ice Machine – 5T/24hrs | 1 Unit | 25,376.00 | 25,376.00 |
| TOTAL(FOB FUZHOU): USD 25,376.00 |
| TOTAL SAY US DOLLAR TWENTY FIVE THOUSAND THREE HUNDRED AND SEVENTY-SIX ONLY |

*The price valid for one month, Quote given is on basis of exchange rate: usd=6.50rmb. it is subject to change if the exchange rate varies.

# Terms and Conditions :

  - Packing: export worthy package suitable for container transportation.

(2) Terms of payment: 30% downpayment by T/T , 70% balance before shipment by T/T.

(3) Delivery time: ready for shipment within 45days after downpayment.

(4) Pre-shipment inspection :Supplier’s pre-shipment inspection is Final ;pre-shipment inspection by third Party on buyers cost.

(5) Installation and commissioning :the related fee such as visa, round-trip air tickets, boarding and lodging, traffic of seller’s engineers should be paid by the buyer.

(6) Warranty: One year after commissioning or 18 months from the date of shipment,subject to the early expiry.

Technical Specification

Tube ice machine (TIM50A)

1.1 Main parameter

| a) Design drawing | See attachment |
| --- | --- |
| b) Capacity of ice making | 5T/day |
| c) Installation power | 22.73kw |
| d) Water consumption | 0.23T/h |
| e) Refrigeration capacity | 30kw |
| f) Cooling way | air-cooling |
| g) Out-diameter of tube ice | 22mm/29mm |
| h) Refrigerant | R22/R404A/R507A |
| i) Power supply | 3P/400V/60HZ (±5%) |

1.2. Main part list

| 1. | 1 Set | Semi-hermetic piston compressor unit |
| --- | --- | --- |
|  |  | Compressor Refrigerant capacity Evaporating temperature Condensing temperature | Refcomp 28.9 -15 43 | SP-4H250E kw ℃ ℃ |
| 2. | 1 Set | Tube ice maker (filtered fresh water) | TIM50SF Snowkey |
|  |  | Direct evaporation with high efficiency. Special water line design to gurantee ice quality(even thickenss,,beautiful tint,clean and sanitary) and water saving. Special refrigeration loop design to improve refrigeration and ice doffing efficiency. The only moving part is durable ice cutting system to keep run performance. Effcient heat conducting pipe to ensure meet the sanitary requirement of the whole refrigeration process and greatly improve the system refrigeration capacity. |
|  |  | Evaporator Drum : Carbon steel, with anti-corrosive painting around outter surface. Material of ice making tube : Stainless steel SUS304 Ice cutting device : SUS304, composed of two semi-circle parts Top & bottom cover : SUS304 Insulation : Polyurethane board around the drum Gear box : Good quality, stable and reliable Motor : Industrial-purpose motor Water pump : With stainless steel shell Water tank : SUS304, with float valve, etc. |
| 3. | 1 Set | Air cooled condensor | Greenhalgh (Australia) |
|  |  | Rated heat exchange load :65kw ( including needful accessories) |
| 4. | 1 Set | Oil seperator | ALCO (USA) |
| 5. | 1 Lot | Refrigeration valves |
|  |  | included all necessary refrigeration parts, including check valve, pressure gauge, pressure controller(high pressure, low pressure, double pressure), liquid sight glass, filter, electromagnetic valve solenoid valve and so on. |
| 6. | 1 Lot | Refrigeration pipe connecting |
|  |  | included all necessary refrigeration pipes, including gas exhaust pipe, gas return pipe, oil pipe, insulated pipe, water pipe and capillary with regulated paint. |
| 7. | 1 Lot | Compressor oil and refrigerant |
|  |  | All compressor oil and system refrigerant will be filled in the system after it is tested and accepted. (Refrigerant gas is provided by the client) |
| 8. | 1 Set | Electrical box and control system |
|  |  | Included Schneider breaker ,contactor ,hot relay and sequence protector , Omron time relay,ect. |
| 9. | 1 Set | Outer frame |
|  |  | Carbon Steel, Painted with three layers, anti-corrosive and finish painting |

1.3 Main part list

| Item | Name | Model. | Technical data | Qty. | Unit | Brand | Origin |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Compressor | SP-4H250E | -15/43℃,28.9/14.9kw | 1 | Set | Refcomp | Italy |
| 2 | Gas exhaus pipe |  | Including valves & acessories | 1 | Set | Snowkey | China |
| 3 | Air cooled condensor |  | Rated heat exchange load 65kw, including needufl acessories | 1 | Set | Greenhalgh | Australia |
| 4 | Liquid feed pipe |  | Including valves & acessories | 1 | Set | Snowkey | China |
| 5 | Tube ice maker | TIM50SF | Including needful acesories | 1 | Set | Snoweky | China |
| 6 | Gas return pipe |  | Including valves & acessories | 1 | Set | Snowkey | China |
| 7 | Reservior |  | Including needful acesories | 1 | Set | Snowkey | China |
| 8 | Oil seperator |  | Including needful acesories | 1 | Set | Snowkey | China |
| 9 | Refrigerating oil |  |  | 5 | L | / | / |
| 10 | Refrigerant gas |  |  | 170 | Kg | / | / |
| 11 | Electrical control system |  | Including electrical box,cable,ect | 1 | Set | Snowkey | China |
| 11.1 | PLC |  |  | 1 | Set | OMRON | Japan |
| 11.2 | Breaker |  |  | 1 | Set | Schneider | France |
| 11.3 | Contactor |  |  | 1 | Set | Schneider | France |
| 11.4 | Intermediate relay |  |  | 1 | Set | OMRON | Japan |
| 12 | Outer frame |  |  | 1 | Set | Snowkey | China |