عرض السعر لـ BTB-300A

FOB Shanghai port

ميناء FOB Shanghai

| الموديل | اسم المنتج | العدد | سعر الوحدة (USD) | السعر الكامل (USD) |
| --- | --- | --- | --- | --- |
| BTB-300A | ماكينة تغليف سلوفان | 1 set | 9,200 | 9,200 |

الشروط

- تفاصيل التسليم: المنتج سيكون جاهزا في ورشة العمل.
2. تفاصيل التغليف: الصناديق الخشبية المعيارية الخاصة للتصدير
3. شروط الدفع: الدفعة المسبقة 30% بـ TT، المبلغ الباقي 70% بـ TT بعد الفحص وقبل الشحن.
4. شروط التجارة: مصنع FOB Shanghai
5. طريقة الشحن: عبر البحر
6. مدة الضمان: الشركة المزودة ستقدم أجزاء المكونات مجانا خلال 12 شهرا.
7. خدمة ما بعد البيع: المهندسون متوفرون لتقديم الخدمات عن الآلات في مصنع المشتري
8. صلاحية: صلاحية عرض السعر بـ 1 شهر.

BTB-300A Cellophane Wrapping Machine

1. Production Instruction:

This machine is widely applicable to the automatic film packaging (with gold tear tape) of various single boxed articles. With new-type of double safeguard, no need to stop the machine, other spare parts will not be damaged when the machine runs out of step.. Original unilateral hand swing device to prevent adverse shaking of the machine, and the non-rotation of the hand wheel when the machine keeps running to secure the security of the operator. No need to adjust the height of worktops on both sides of the machine when you need to replace mould, no need to assemble or dismantle the material discharge chains and discharge hopper.

Automatic Grade: Automatic   Driven Type: Electric

Application: food, cosmetics, stationary, hardware, daily used products, pharmaceutical etc.

- mainly single box

- Technical Data:

| Packing Material | BOPP film and gold tear tape |
| --- | --- |
| Packing Speed | 40-80 packs/Min |
| Max Packing Size | (L)240×(W)120×(H)60mm |
| Electric Supply & Power | 220V 50Hz 5kw |
| Weight | 500kg |
| Overall Dimensions | (L)2000×(W)700×(H)1400mm |

3. Features:

1. No need to regulate the height of two work tops of the machine when the mould is replaced, no need to assemble or dismantle the material discharge chains and discharge hopper. Reduce the replacement time of the mould four hours to the present 30 minutes.

2. New-type double safeguard mechanisms are used, hence other spare parts will not be

damaged when the machine runs out of step without the stop of the machine.

3. Original unilateral hand swing device to prevent from shaking the machine adversely, and the non-rotation of the hand wheel during the running of the machine can secure the security of the operator.

4. New-type double-rotary film cutting cutter can ensure no need to mill the blade during many-year use of the machine, which overcomes the defect that the traditional stationary single-rotary film cutting cutter was easily worn.

| 4. Component list |
| --- |
| No. | Item | Qty | Brand |
| 1 | Breaker | 6 | Zhengtai (Shanghai) |
| 2 | Auxiliary relay | 4 | Omron (Japan) |
| 3 | Temperature controller | 6 | Yatai (Shanghai) |
| 4 | Solid State Relay | 6 | Xinling (Shanghai) |
| 5 | Inverter | 1 | Yatai (Shanghai) |
| 6 | Counter | 1 | Yatai (Shanghai) |

5. Parts

6. Photos for our factory:

7. Certificate: