LT-420 Film Forming Packaging Machine

(Automatic Bag Forming, Weighing & Sealing System)

SPECIFICATION

| Model | LT-420 |
| --- | --- |
| Packing Speed | 15-60bag/min |
| Available Bag Size | Length: 60-300mm (adjustable freely) Width: 60-200mm (one width of bag needs on pipe) |
| Weighing Range | 10-1000g (per time) |
| Max outer diameter of film | 420mm |
| Power | 220V/50Hz, 2.2Kw |
| Outside Dimension | L. 3200 x W. 1800 x H. 3200mm |
| Air Flushing Function | Yes |
| Date Printing Function | Yes, color ribbon printer |
| Materials | Full Stainless Steel for all the parts that touches products; other parts are painted Mild Steel. |

Remark

- You can check the information that I painted in blue which is the most important information. For the length, we can freely adjust in this range. But for the width of bag, it is one pipe to shape one (width size) of bag. For example, 100mm and 150mm wide bag, it needs 2 shaping pipes. 1 pipe is already there with the machine. For more, it costs USD 700.00/PC.

II. The specification of machine

① Packaging speed: max 70bag/min (fix on the quality of the packaging film)

② The total power: 4.2KW

③ Combined with air compressor: not less than 0.4-0.6 cubic metre

III. Introduction of every device

1. LT-420

Large vertical automatic packaging machine

- Features

*Imported PLC computer control system with human-machine interface; touch screen is simple and direct-viewing in operation;

*precise positioning with servo film transporting system; excellent complete machine performance and nice packing;

* minimize the loss with complete automatic warn protection function;

* supported with metric device, the machine will automatically complete all packaging processes from measuring, feeding, filling, bag ma

* the way of bag making: the machine can make pillow-type bag and standing bag according to customer’s requirements.

- Technical parameter

| Items | Content |
| --- | --- |
| Packing speed | 5-70 bag/min |
| Bag size | (L)60-300mm (W)60-200mm |
| Bag making mode | Pillow-type bag, standing bag, punch |
| Range of measuring | 150-1300ml |
| Max packaging film width | 420mm |
| Thickness of film | 0.04-0.09mm |
| Air consumption | 500L/min 0.8×105Pa |
| Main power/voltage | 2.2KW/220V 50-60Hz |
| Dimension | 1530×970×1600mm |
| The weight of switchboard | 450kg |

2. Features of ten-hopper computer combination scale

- Features

* Suitable range: dosing and weighing of grain, chip, bar or irregular shaped material such as candy, sunflower seed, potato chip, happy fruit, peanut, jelly, freezing rice dumpling, biscuit, chocolate, nut, pet food, puffed food, small metal parts and plastic parts, etc.

* Select the best combination immediately from diversified weight combinations through computer with perfect combination of high precision and high speed.

* High precision data-type weighing sensor realizes precise weighing.

* Liquid crystal screen operating system in multiple languages such as Chinese and English, etc.

* IP65 grade water-proof and dust-proof design. It's clean and sanitary with all stainless steel parts. Full sealed design prevents accumulation of material and facilitates cleaning.

* It can fine the opening and closing speed of hopper door according to the features of items to be weighed, and prevent crushing and blocking of material.

* With powerful digital automatic counting function, it can record the index for each batch of product such as total bag number, pass rate and difference of single bag, etc.

* Optional devices: triglyph balance ball, suction hopper, printing device, tolerance sorting device.

* Strong compatibility and more compact structure with it directly installed on the upper part of packing machine.

* Fast return for investment by largely saving large quantity of raw material and labor cost.

* Net weight: 300kg; Gross weight: 370kg

* Voltage: 220V; Power: 1500W; Frequency: 50/60HZ; Rated current: 9A.

* Out package dimension(mm)：1400(L)×1130(W)×1120(H):

- Technical parameter

| Range of single weighing | 14-1000g |
| --- | --- |
| Maximum weighing quality | 3000g |
| Average tolerance for single bag | 0.2-0.5g |
| Range of weighing precision | 0.1-1.5g |
| Maximum weighing speed | 70 bags /minute |
| Hopper capacity | 1300ml |
| Hopper type | Bi-row hopper without memory |
| Driving | Step motor |
| Preset number for product | 99 kinds |
| Size of machine body(mm) | 1150(L)X950(W)X1129(H) |

3、LT-Z type conveyer

- Features

The conveyer is applicable for vertical lifting of grain material in departments such as corn, food, fodder and chemical industry, etc. For the lifting machine, the hopper is driven by the chains to lift. It’s used for vertical feeding of grain or small block material. It has advantages of large lifting quantity and highness.

- Specification

The highness of lifting   2.6m

speed of lifting：  0-17m/minute;   lifting quantity： 5.5cubic meter/hour

power           550w

voltage          220v

specification customized; material: carbon steel plastic-spray or stainless steel; the part contacting with food is food grade plastic.

4、LT-A2 Vibration type feeder

- Features

The parts contacting with food is made of 304 stainless steel; supported with non-grade adjuster to regulate the feeding quantity. It sends the material from the storage to the material conveyer through vibration.

- Specification

The max. feeding capacity: 2㎡/hour;

the storage is used to store the material to be packed with capacity of 0.5 cubic meter

5、LT-A3 Finished products conveyer

- Features

The machine can send the packed finished bag to after-package detecting device or packing platform.

- Specification

Feeding speed: 30m\minute

Dimension: 2110×340×500mm

Voltage: 220V/45W

# Text boxes

You see, it is this bag shaping pipe that curls the film and shape it into the bag.