SCY-400 Automatic high speed “V” shape bottom food paper bag making machine

Price: 31000 USD/SET ,FOB NINGBO,CHINA

If the bag width change ,you need to buy extra mould :400 USD/SET

The bag’s length can be adjusted by machine (160-400mm)

Video: https://youtu.be/PDrnzxc-QRo

It is an ideal machine for producing food bags like bread bags, KFC bags and Mcdonald's bags.

Features:

1. Suited for 30-80gsm paper.

2. Controls bag length through the human-machine interface.

3. PLC system for calculating parameters.

4. Equipped with an accurate photocell system.

Technical parameter:

| Model | SCY-400 |
| --- | --- |
| Paper thickness | 30-80g/m2 |
| Bag length | 160-400mm |
| Bag width | 60-250mm |
| Side width（insert side） | 20-100mm |
| Speed | 70-400pcs/min |
| Power | 10Kw |
| Total weight | 2500kg |
| Machine dimension | 3550 x 1530 x 1950mm |

Delivery time：30 workday after receive the 30% deposit

Payment term：30% T/T as deposit,The balance is 70% before shipment

Gurantee : 1 year