FORWOOD

PROJECT  REPORT

Reporter: ANHUI FORWOOD Drying Equipment Co., Ltd.

Project:  50M3 Aluminum Panel Timber Drying Kiln（ electricity）

Date:  2017/05/10

秘鲁客户

Technical Specifications

Type: FW-50

Kiln Cavity Dimensions:

Depth: 6600mm

Width: 6000mm

Height:5600mm

Number of Fans: 4

Working Air Volume of a Single Fan: 30000M3/h

Electric Power of a Single Fan: 12kw

Heat-Transfer Material:  electricity

# Quotation for the Equipment(FOB shanghai)

All Components for a Single Kiln:

Total price for one unit of kiln  （electricity heated):   24,000USD/set ,

The seller will send persons to install the kiln on site at the requirement of the Buyer. The freight and the boarding of the persons seller send will be afford by buyer, and $60 will paid to each person one day.

# Payment Terms

The Buyer should pay to Seller 30% of the total price as the deposit when this contract comes into effect.

The Buyer should pay to Seller 70 % of the total price with in three days after shipment against BL.

# Date of Shipment

Shipment shall be effected within 40days from the date of the Seller’s receipt of the Buyer’s deposit.

Detailed List of the Equipment (for one unit)

#### Control System

1-1. Wood Drying Controller      1 set

Type:  DELPHI             HOLZMEISTER Delphi

Place of Production:    Italy

Technical Specifications:

Measurement and Control Range of Temperature:  0-100℃

Measurement and Control Range of Humidity:     0-100%

Measurement Range of Moisture Content of Wood:  4-60%

Power:  30W

Environmental Specifications:

Input Voltage: 220+10%AC

Working Temperature: 5-50℃

Working Humidity: 35-75%

Auxiliary Parts:

Temperature and humidity transducer and wire    1 set

Measurement probe of moisture content of wood  12 pieces

Measurement plug of moisture content of wood   12 pieces

EMC sets transducer and wire                    6 sets

1-2. Control Panel

Type:               FW-50

###### Air Circulating System

2-1. Fan                  4 sets

Type:                ￠800

Place of Production:    CHINA-FUJIAN

Technical Specifications:

Working Air Volume: 30,000 m3/h

2-2. Motor                3sets

Type:  100 Series

Technical Specifications:

Rated Voltage: 380±10%AC

electromagnetic frequency 50HZ

Rated Current: 6A

Rated Power: 3.0kw

Insulation Grade: H

Protection Grade: IP55

Place of Production:    CHINA-FUJIAN

Environmental Specifications:

Maximum Working Temperature: 120℃

Maximum Working Humidity: 100%

The Way of Working: Continuous

2-3. Fan Rack             1 set

Place of Production:    FORWOOD

Material: Shaped aluminum alloy

2-4. Ceiling                1 set

Place of Production:    FORWOOD

Material: 1.0mm corrugated aluminum alloy plate

###### Heating System

3-1.  electricity Heat- Exchanger Coils       120KW

Place of Production:    FORWOOD

Technical Specifications:

Fin Type: Rolled

Fin Material: Aluminum Alloy

Tube: Stainless steel tube

Heat-Exchanging Area:

## Spray System

4-1. Electromagnetic Spray Valve          1 piece

Type: D-20

Place of Production:    Taiwan

Technical Specifications:

Standard: 20

Working Voltage: 220V/AC

Maximum Allowed Working Temperature: 200℃

Working Pressure: 0.3-10Kg/cm2

4--2  atomizing spray head               5sets

4--3， atomizing spray pump             1set

## Venting System

5-1. Venting Motor                      2set

Type: SIEMENS

- Place of Production:   Germany

Technical Specifications:

Input Voltage: 220V±10%/AC

Power: 4W

Output Torque: 15NW

Maximum Load Area: 4m2

5-2. Venting Duct           6sets

Place of Production:    FORWOOD

Material: Aluminum Alloy

Standard:  D300

5-3. Driving Mechanism     2sets

Place of Production:    LIYANG

Material: Seamless and stainless steel tube

## Door System

6-1. Door                1leave

Type: FW-50

Place of Production:    FORWOOD

Standard: 6500×4450mm

Material:

Rim: Shaped aluminum

Frame: Shaped Aluminum

Insulation Material: insulation layers

Sealing Material: custom-tailored special-shaped rubber tube

Auxiliary Parts:

Door Case: Shaped aluminum alloy

6-2. Inspection Door                    1 set

Place of Production:    FORWOOD

Standard: 1600×600mm

Auxiliary Parts:

Door Case: Shaped aluminum alloy

6-3. Door Carrier:                          1set

Type: Sliding and supported with floor rail

Place of Production:   FORWOOD

## Housing

7-1. Post, Beam, Truss

Material: Shaped aluminum or Shaped steel

Place of Production:         FORWOOD

7-2. Wall

Internal Wall Panel: Aluminum plate

Type: 1.2mm

Place of Production:  FORWOOD

External Wall Panel: corrugated Aluminum plate

Type: 1.0mm

Place of Production:   FORWOOD

Insulating marterial: Fiber glass

Thickness: 100mm

7-3. Control Room

Material: Polystyrene panel 50mm

##### After-Sales Service

## Installation and Trial Run

Our engineers and technicians coordinating with the User’s personnel shall complete all installation and shall be responsible for the trial run until all equipment run well.

## Technical Training

We shall train the kiln drying operators for Users free of charge on site or in our company. The experts from the Institute of Drying Technology shall give lessons in drying mechanism and operating rules to make the operators have a real grasp of the wood drying technology and be skilled in wood drying.

## Maintenance and Technical Service

- We shall give prompt maintenance service to our Users by email and phone.

2.  We shall provide spare parts at the best price.

3.  We shall provide free latest wood drying technology for our Users and can provide particular technical service according to User’s individual requirements.