Forwood Wood Drying Equipment Co., Ltd

Heating Treatment Equipment

Project Report

FWH-15(electricity)

Features of our Thermally Modified wood kiln

1, our thermally modified wood kiln is a newly developed product by our company. It adopts the PLC control system researched and developed by our company, which ensures precise and reliable control.

2, the efficient fan used in our thermally modified wood kiln provides uniform thermal conduction.

3, the kiln housing adopts stainless steel-steel-aluminum alloy, with ultra-thick insulation and good ability of preventing penetration.

4, our thermally modified wood kilns are highly efficient and suitable for mass production.

5, we adopt the unique security system.

Confifuration scheme

Model：              FWH-15

Capacity：            15m3

Loading：             Trolley

Kiln structure：        Stainless steel-steel-aluminum alloy structure

Power：              4×3KW（4 sets of fan，outlay motor）

Heating demand for 1sets of kiln：     120KW /h（Electrical Power Heating）

# Quotation for the Equipment (FOB SHANGHAI)

All Components for a Single Kiln:

Total price for one unit of kiln :           50,000USD

Freight to Shanghai port

Container：                           1×40GP

The seller will send persons to install the kiln on site at the requirement of the Buyer. The freight and the boarding of the persons seller send will be afford by buyer, and $60 will be paid to each person each day when working on site.

# Payment Terms

The Buyer should pay to Seller 30% of the total price as the deposit when this contract comes into effect.

The Buyer should pay to Seller 70% of the total price with in three days after shipment against BL.

# Date of Shipment

Shipment shall be effected within 45 days from the date of the Seller’s receipt of the Buyer’s deposit.

# Civil Engineering system

Provided by FORWOOD:

- A complete set of working drawings for the foundation

- Technical guidance during the period of construction

User’s Responsibility:

- Complete all foundation construction according to working drawings

- Complete laying of all embedded parts according to working drawings

# Electric Power System

Provided by FORWOOD

- General control panel and cables connected to the panel

- Sub-panels for each kiln and cables and other facilities connected to them

Provided by User:

- Cables from the mains to the general control panel

- Earthling system for each panel

## Technical parameters:

Model：  FWH-15

Kiln inner size：

depth：6300mm

width：3000mm

height：4800mm

stack size：

degth：6000mm

width：1600mm

height：3000mm

Theoretical Timber Capacity: 15m3

Fan：4

Maximum Air Volume of a Single Fan: 3000m3/h

Electric Power of a Single Fan: 3kw

Heat-Transfer Material：Electrical Power

## Intelligence control system

PLC-Automatic control system                          1 set

Producing area：                                    Forwood

Technical parameters：

Measurement and Control Range of Temperature             0~250℃

Measurement and Control Range of Humidity               10~100%

Power                     30W

## Environmental Specifications:

Input Voltage: 220+10%AC

Working Temperature: 5-50℃

Working Humidity: 35-75%

Auxiliary Parts:

Temperature and humidity transducer and wire     2 set

## Main accessories：

1—1.  PLC Full-automatic Control system

Place of Production: FORWOOD

1—2.  Control Panel

Type:   FW-EC              1set

Technical parameters：

Input voltage                 380V±10%AC

Rated operational current       24A

Output power                12Kw

Place of Production: FORWOOD

## Airflow cyclic system

2—1. Fan                  4 sets

Type:                   8#

Place of Production:       SUZHOU

Technical Specifications:

Maximum Air Volume:  30000M3/h

2—2. Motor and drive system  4sets

Type:

Technical Specifications:

Rated Voltage: 380±10%AC

Rated Current: 6A

Rated Power: 3Kw

Place of Production:    Wuxi

Motor rack：     1 set

2—3 Bearings machine seal up and cooling system

2—4   Fan Rack             1 set

Place of Production:        FORWOOD

Material: Shaped aluminum alloy

2—5.    Ceiling                1 set

Place of Production:        FORWOOD

Material: 1.0mm corrugated Stainless steel plate

## Heating System

3-1.  Heat- Exchanger                                  120KW

Place of Production:    FORWOOD

## Steaming system

4—1. Kiln inner stainless steel water channel               1set

4—2. kiln outside vaporization water pipe road and valves    1set

## Spray-cooling system                                    1 set

5—1 Spray system

Origin：China

Pump:  Germany

Pressure：50b

Spray volume：500L/h

Water tank: 100L，

atomizing spray head                                    20sets

.cooling system

5---2 cooling finned tube                             1set

5—2 cooling water circulatory system                  1set

## Fire protection system

5—5.  Atomizing pressure pump                   1set

5—6.  Atomizing                               2 set

5—7.  Stainless steel piping                       1 set

5—8.  Atomizing magnetic valve                  1set

## Door System

7-1. Door                    1 leave

Place of Production:        FORWOOD

Standard: 1700×3050mm

Material:

Rim: Shaped aluminum

Frame: Shaped Aluminum

Insulation Material: insulation layers

Sealing Material: custom-tailored special-shaped rubber tube

Auxiliary Parts:

Door Case: Shaped aluminum alloy

Inner door board: 1.0mm stainless steel board

Outside board: 0.8mm aluminum alloy plate

7-2. Wall

Internal Wall Panel: Stainless steel plate

Type: 1.0mm

Place of Production:  FORWOOD

External Wall Panel: corrugated Aluminum plate

Type: 1.0mm

Place of Production:  FORWOOD

Insulating material: rock wool board

Thickness: 200mm

Framework:   carbon steel

7-4. Control Room

Material: Polystyrene panel,  polyphenyl grease plate

8-1  Loading trolley                           1 set

Standard:                                6000×1600mm

8- 2  Rail                                    26m

## Installation and Trial Run

Our engineers and technicians coordinating with the User’s personnel shall complete all installation and shall be responsible for the trial run until all equipment run well.

## Technical Training

We shall train the kiln drying operators for Users free of charge on site or in our company. The experts from the Institute of Drying Technology shall give lessons in drying mechanism and operating rules to make the operators have a real grasp of the wood drying technology and be skilled in wood drying.

## Maintenance and Technical Service

- We shall provide free maintenance service by email and phone.

- We shall provide spare parts at the best price.

- We shall provide free latest wood drying technology for our Users and can provide particular technical service according to User’s individual requirements.