Quotation

| Our Ref No. |  | Date: July 24th,2017 |
| --- | --- | --- |
| To: |  | ICESTA Ice Systems |
| Attn: |  | From: Ms. Sharon |
| Email: |  | Email : sharon@icesta.com |
|  | Tel:+86- 0755-29914211 Fax: +86-0755-29914210 |
| Subject: | Quotation for 5/8/10ton flake ice machine |

This program includes the following:

1) Quotation for the equipment

2) Technical parameter and components list

3) CE Certificate

4) Control system

5) Principles for Guarantee and technical support

6) Photos gallery for flake ice machines

7) Working partners

1).Quotation for 5/8/10Ton flake ice machines(air-cooling)

| Item No. | Model | Capacity(T/24h) | Unit price (USD) |
| --- | --- | --- | --- |
| Flake ice machine | IF5T-R4A | 5t/24h | 20,475 |
| Flake ice machine | IF8T-R4A | 8t/24h | 30,550 |
| Flake ice machine | IF10T-R4A | 10t/24h | 35,532 |

- The flake ice machine includes ICESTA Unique design flake ice machine, water pump, ice shovel, ice amount detector and supporting frame, screen-touch computerized electrical controller.Ice storage bin is not included.

COMMERCIAL ITEMS

| Remarks |  |
| --- | --- |
| Trade terms | FOB Shenzhen Port |
| Payment terms | Telegraphic Transfer. 30% deposit after PO confirmed. Balance paid before delivery. |
| Delivery | 40 working days after deposit |
| Package | Standard Wooden package |
| Validity | 30days |
| Warranty period | 1 year after B/L date. Any failure occurred within the period due to our responsibility, we'll supply you the spare parts for free, and permanent technical support & consultation all life long for the machines. |
| Note | CE approved certificate |

2). Flake Ice Machine Technical Parameter

Flake Ice Machine Technical Parameters

| Model Technical parameters | IF5T-R4A BOCK 25HP | IF8T-R4A BOCK 40HP | IF10T-R4A BOCK |
| --- | --- | --- | --- |
| Compressor Model | HG6/1240-4 | HG7/1860-4 | 2* HG6/1240-4 |
| Ice production | 5t/24h | 8t/24h | 10t/24h |
| Refrigeration Capacity (KW) | 35 | 48.8 | 69.9 |
| Evaporating Temp (℃) | -20 | -20 | -20 |
| Condensing Temp (℃) | 40 | 40 | 40 |
| Total power (KW) | 22.55 | 30.46 | 44.36 |
| Compressor Input Power (KW) | 20.7 | 27.5 | 41.4 |
| Reducer Power (KW) | 0.37 | 0.55 | 0.55 |
| Evaporator Pump Power (KW) | 0.12 | 0.37 | 0.37 |
| Condensing Fan Power (KW) | 1.36 | 2.04 | 2.04 |
| Power Supply | 3P/380V/50Hz | 3P/380V/50Hz | 3P/380V/50Hz |
| Feed in water pressure | 0.1Mp－0.5Mpa | 0.1Mp－0.5Mpa | 0.1Mp－0.5Mpa |
| Refrigerant | R404a | R404a | R404a |
| Flake ice Temp | -5℃ | -5℃ | -5℃ |
| Thickness of Ice | 1.5mm-2.2mm | 1.5mm-2.2mm | 1.5mm-2.2mm |
| Standard Ambient Temp | 25℃ | 25℃ | 25℃ |
| Standard water feed temp | 20℃ | 20℃ | 20℃ |
| water Consumption (M3/h) | 0.2 | 0.34 | 0.42 |
| Feeding tube | 3/4" | 3/4" | 3/4" |
| Net weight of unit | 960KG | 1450KG | 1680KG |
| Dimensions of unit (mm) | 2030*1650*1470 | 3100*2100*1730 | 3200*2200*1870 |

| Model Specifications | IF5T-R4A | IF8T-R4A | IF10T-R4A |
| --- | --- | --- | --- |
| Name | Brand | Origin | QTY | QTY | QTY |
| Compressor | BOCK | Germany | 1 | 1 | 2 |
| Oil seperator | Emerson | USA | 1 | 1 | 1 |
| Condenser | Yiteng | Singapore | 1 | 1 | 1 |
| Condenser Fan | EBM | Germany | 2 | 3 | 3 |
| Float Ball Valve | Danfoss/Pike | Denmark/USA | 1 | 1 | 2 |
| Reservoir | Fasike | China | 1 | 1 | 1 |
| Dry filter | Emerson/Pike | USA | 1 | 1 | 1 |
| Gas return filter | Fasike | China | / | 1 | 2 |
| Solenoid valve | Danfoss/Pike | Denmark/USA | 1 | 1 | 1 |
| Expansion valve | Emerson/Danfoss | USA/Denmark | 2 | 4 | 4 |
| Pressure controller | Danfoss/Pike | Denmark/USA | 2 | 2 | 4 |
| Pressure meter | Coolmax | Taiwan | 3 | 3 | 2 |
| Vibration absorber | Hanlisi/Pike | Korea/USA | 1 | 2 | 2 |
| Reducer | Gongji | Taiwan | 1 | 1 | 1 |
| Water pump | ICESTA | China | 1 | 1 | 1 |
| Water-level switch | Fanyi | Taiwan | 1 | 1 | 1 |
| Gas-liquid separator | Fasike | China | 1 | 1 | 1 |
| PL controller | LG/Siemens | Korea/Germany | 1 | 1 | 1 |
| Air switch | Schneider | France | 1 | 1 | 1 |
| Contactor | Schneider | France | 3 | 6 | 8 |
| Thermorelay | Schneider | France | 3 | 6 | 8 |
| Touch screen | Weinwiew/Siemens | Taiwan/Germany | 1 | 1 | 1 |
| Intermediate relay | Jiale | Swiss | 2 | 2 | 4 |
| phase sequence relay | Jiale | Swiss | 1 | 1 | 1 |

3) ICESTA ICE SYSTEMS CERTIFICATION

4) ICESTA CONTROL SYSTEM (PATENT) UNIQUE INNOVATION

* Running status played live in touch-screen

* All failure record and relevant solution programmed in touch-screen for most convenience.

* Stop-time setting at will

ICESTA Control system

1). Picture one is the displaying screen of operation.

Characteristics：1. User-friendly display。

2. System failure will be indicated on screen。

2). Picture 2: Failure Display

Characteristics： The possible failures are all programmed

Into computer，operator could settle down the break-down following systems instructions very easily.

3). Failure history record

Characteristics: The computer will record all history failure in

Its system, which will give greatly convenience to the services

man, for system checking and maintenance.

4). Picture 4: Operation hours setting

Characteristics：

A. User-friendly design，operator could set working hours,

system will stop automatically at setted time.

B. User could decide the working hours by himself, to avoid

Energy waste and save cost

5). Guarantee, technical support and failure claim procedures

- All Icesta ice systems delivered to customers are carefully examined and tested, with 72 hours trouble-free trial operation.

- All ICESTA ice systems delivered are plug-in ready and well piped.

- All ICESTA ice systems enjoy 1 year guarantee ever since B/L date.

Technical support

- ICESTA provide full technical support and training courses after equipment installation and commissioning.

- 7*24 hours phone assistance on technical support.

Failure Claim procedures

- Detailed written failure description is required by fax or by mail, indicating the relevant equipment information and detailed description of failure.

- Relevant pictures are required for failure confirmation.

- ICESTA engineering and after-sales service team will check and form a diagnosis report.

- Further trouble-shooting solutions will be offered to customers within 24 hours after receiving the written description and pictures.

- Photos gallery

7). Working partners worldwide in variety industries

Seafood Industry

Construction and concrete cooling industry

Meat processing Industry

Poultry Slaughtering

Super market and Chain stores