Quotation

| Our Ref No. |  | Date: September 5th,2017 |
| --- | --- | --- |
| To: |  | ICESTA Ice Systems |
| Attn: |  | From: Ms. Sharon |
| Email: |  | Email : sharon@icesta.com |
|  | Tel:+86- 0755-29914211 Fax: +86-0755-29914210 |
| Subject: | Quotation for 5/10ton tube ice machine |

This program includes the following:

1) Quotation for the equipment

2) Technical parameter

3) Control system

4) Principles for Guarantee and technical support

5) Photos gallery for tube ice machines

6) Working partners

1). A.Quotation for 5/10Ton tube ice machine

| Item No. | Model | Capacity(T/24h) | Unit price (USD) |
| --- | --- | --- | --- |
| Tube ice machine (water cooling) | IT5T-R4W | 5t/24h | 25,285 |
| Tube ice machine (water cooling) | IT10T-R4W | 10t/24h | 44,098 |

B. Ice dispenser + automatic ice packing machine

| Name | Model / Description | Storage Capacity | Qty | Material | Unit Price(USD) |
| --- | --- | --- | --- | --- | --- |
| Ice dispenser (Semi-automatic packing) 1.3kW | Ice Storage and conveying ice by pedal | 0.5T | 1 | Stainless steel | 3,600 |
| Auto-packing machine | 6-10 bags/ minutes | / | 1 | Stainless steel | 34,816 |
| Total |  |  |  |  | 38,416 |

COMMERCIAL ITEMS

| Remarks |  |
| --- | --- |
| Trade terms | FOB SHENZHEN Port |
| Payment terms | Telegraphic Transfer. 30% deposit after PO confirmed. Balance paid before delivery. |
| Delivery | 45days after deposit |
| Package | Standard Wooden package |
| Validity | 30days |
| Warranty period | 1 year after B/L date. Any failure occurred within the period due to our responsibility, we'll supply you the spare parts for free, and permanent technical support & consultation all life long for the machines. |
| Note |  |

- . Tube Ice Machine Technical Parameter

Tube Ice Machine Technical Parameters

| Model Parameters | IT5T-R4W Bitzer | IT10T-R4W Bitzer |
| --- | --- | --- |
| Compressor | 25HP | 50HP |
| Ice output | 5t/24h | 10t/24h |
| Ice tube diameter | φ29 | φ29 |
| Cooling Capacity | 48.8 | 80.2 |
| Evaporating temperature | -15 | -15 |
| Condensing temperature | 40 | 40 |
| input power | 23.8 | 43.75 |
| Compressor input power | 18.6 | 33.8 |
| Ice cut reducer input power | 0.75 | 0.75 |
| Water pump input | 1.5 | 2.2 |
| Condenser Fan input power | 2.2 | 5.5 |
| Water pump of cooling tower | 0.75 | 1.5 |
| Power Specifications | 3P/380V/50Hz | 3P/380V/50Hz |
| Water Pressure | 0.1Mpa－0.5Mpa | 0.1Mpa－0.5Mpa |
| Refrigerant | R404A | R404A |
| Standard ambient temp. | 30 | 30 |
| Standard Water Temp. | 20 | 20 |
| Water Consumption(M3/h) | 0.21 | 0.42 |
| Water supply tube Diameter | 2" | 2" |
| Overflow pipe | 1-1/4" | 1-1/4" |
| Drain pipe | 1-1/4" | 1-1/4" |
| Ice machine Weight | 1600 | 2750 |
| Ice Machine Diameter | 1750*1400*2250 | 2300*1600*3100 |
| Dimension of cooling tower | φ1385*2150 | φ1880*2120 |
| Weight of cooling tower | 500 | 975 |

3) ICESTA CONTROL SYSTEM (PATENT) UNIQUE INNOVATION

* Running status played live in touch-screen

* All failure record and relevant solution programmed in touch-screen for most convenience.

* Stop-time setting at will

ICESTA Control system

1). Picture one is the displaying screen of operation.

Characteristics：1. User-friendly display。

2. System failure will be indicated on screen。

2). Picture 2: Failure Display

Characteristics： The possible failures are all programmed

Into computer，operator could settle down the break-down

following systems instructions very easily.

3). Failure history record

Characteristics: The computer will record all history failure in

Its system, which will give greatly convenience to the services

man, for system checking and maintenance.

4). Picture 4: Operation hours setting

Characteristics：

A. User-friendly design，operator could set working hours,

system will stop automatically at setted time.

B. User could decide the working hours by himself, to avoid

Energy waste and save cost

4). Guarantee, technical support and failure claim procedures

- All Icesta ice systems delivered to customers are carefully examined and tested, with 72 hours trouble-free trial operation.

- All ICESTA ice systems delivered are plug-in ready and well piped.

- All ICESTA ice systems enjoy 1 year guarantee ever since B/L date.

Technical support

- ICESTA provide full technical support and training courses after equipment installation and commissioning.

- 7*24 hours phone assistance on technical support.

Failure Claim procedures

- Detailed written failure description is required by fax or by mail, indicating the relevant equipment information and detailed description of failure.

- Relevant pictures are required for failure confirmation.

- ICESTA engineering and after-sales service team will check and form a diagnosis report.

- Further trouble-shooting solutions will be offered to customers within 24 hours after receiving the written description and pictures.

5) Photos gallery

6). Working partners worldwide in variety industries

Seafood Industry

Construction and concrete cooling industry

Meat processing Industry

Poultry Slaughtering

Super market and Chain stores