Quotation  Sheet

Quotation No.: SN20170927-EC-14                                     Dated: 27th September, 2017

# Submitted To: Integer SA de CV - Grupo Ecofrio

Subject: Supply Concrete Cooling System For Proposed Concrete Batch Plant.

Price List & Commercial Term

| Item | Commodity&Specification | Quantity | Unit price （USD） | Amount （USD） |
| --- | --- | --- | --- | --- |
| 1 | Containerized Flake Ice Machine - 30T/D | 1 Unit | 103,329.00 | 103,329.00 |
| 2 | Automatic Ice Storage – 125T | 1 Unit | 162,500.00 | 162,500.00 |
| 3 | Hoist Screw Delivery – 10M | 1 Unit | 8,887.00 | 8,887.00 |
| 4 | Sea Freight Charge & Insurance | -- | -- | 17,500.00 |
| 5 | Supervising Installation & Commissioning Charge | -- | -- | 5,850.00 |
| TOTAL(CIF SALVADOR): USD 298,066.00 |
| TOTAL SAY US DOLLAR TWO HUNDRED AND NINETY EIGHT THOUSAND AND SIXTY-SIX ONLY |

*The price valid for one month, Quote given is on basis of exchange rate: usd=6.60rmb. it is subject to change if the exchange rate varies.

# Terms and Conditions :

  - Packing: export worthy package suitable for container transportation.

(2) Terms of payment: 30% T/T downpayment, 70% T/T balance before delivery .

(3) Delivery time: ready for shipment within 75days after downpayment.

(4) Pre-shipment inspection :Supplier’s pre-shipment inspection is Final ;pre-shipment inspection by third Party on buyers cost.

(5) Installation and commissioning : the seller will arange engineer for supervising installation and commissioning work. And the boarding and lodging, traffic of seller’s engineers should be arranged by the buyer.

(6) Warranty: One year after commissioning or 18 months from the date of shipment,subject to the early expiry.

Technical Specification

Part-1  30T/D Container-type Flake Ice Machine (FIP30)

| 1. | 1 Set | Screw-type compressor unit |
| --- | --- | --- |
|  |  | Compressor Refrigerant capacity Evaporating temperature Power consumption Power supply Refrigerant | Refcomp (Italy) 176.4 -24 94.5 3Ph,380V,60Hz R404A | SW3L13000 kw ℃ kw |
| 2. | 1 Set | Flake ice evaporator (filtered water) | F300SF Snowkey |
|  |  | Applying couples of self-developed patents of utility and patented processing techniques to make sure the highly-efficient heat conductivity of the core part of flake ice evaporator. With dripless design for the bottom of the evaporator, light-load screw ice blade so as to make and scrap ice evenly and powderlessly. The powderless ice flakes are not easy to agglomerate so that they can be stored for longer time. Material : Low-temperature carbon steel with chrome-plated Ice blade : SUS304, patented screw ice blade, lower loade,no trash ice Bearing : Industrial-purpose bearing and seal fittings Top & bottom cover : Aluminium alloy, surface anticorrosive treatment Insulation : Polyurethane foam around the drum Exterior cover : Cladded with stainless steel sheet Gear box : Good quality, stable and reliable Motor : Wonder brand, Industrial-purpose, IP54 protection grade Water pump : Vertical-type water pump, with stainless steel blade Water tank : Stainless steel with float valve, etc. |
| 3. | 1 Set | Evaporative condenser | SLC-520 Snowkey |
|  |  | It is equipped on the top of the container with double speed fan, water pump, automatic water supplying float valve, water level protector, connecting box and so on. It fulfils the condensing heat exchange load of the complete ice making system, ice storage refrigeration system and air conditioning system. |
|  |  | Heat exhaust load Fan power Water pump power Water consumption | 520 4.5/6 2.2 830 | kw kw kw L/hr |
| 4. | 1 Set | Oil seperator | Carly (USA) |
| 5. | 1 Lot | Refrigeration valves |
|  |  | included all necessary refrigeration parts, including check valve, pressure gauge, pressure controller(high pressure, low pressure, double pressure), liquid sight glass, filter, electromagnetic valve solenoid valve and so on. |
| 6. | 1 Lot | Refrigeration pipe connecting |
|  |  | included all necessary refrigeration pipes, including gas exhaust pipe, gas return pipe, oil pipe, insulated pipe, water pipe and capillary with regulated paint. |
| 7. | 1 Lot | Compressor oil and refrigerant |
|  |  | All compressor oil and system refrigerant will be filled in the system after it is tested and accepted. |
| 8. | 1 Set | Electrical box and control system |
|  |  | Including Schneider breaker and contator,Omron intermediate relay,etc. |

Part-2  Combined-type Ice Storage Bin (AIS125)

| 1． | 1 Set | Ice storage |
| --- | --- | --- |
|  |  | The ice storage plate is high density reinforced polyurethane foam in the medium. The inner connecting of storage plate is galvanized wave plate, the exterior of which is galvanized plate. Double wall structure is used for inner cycle of cold air. Thus, a cold air buffer layer will be formed around the ice In the ice storage. |
|  |  | Outside length Outside width Outside height Inner temperature | 15000 5191 4965 -8 | mm mm mm ℃ |
| 2． | 1 Set | Ice raking device | Snowkey |
|  |  | The ice blade drove by drive device the in the ice rake system rakes the ice repeatedly to make the ice flat when the ice falls down to the ice storage. When it stores ice in the ice storage, the ice raking device run in the positive direction, while it run in negative direction when it delivery the ice from the ice storage to the horizontal screw device. |
|  |  | Ice rake motor Ice rake shelf | 3 Hot galvanized | kw |
| 3． | 1 Set | Hoist assembly | Snowkey |
|  |  | According to the ice capacity, it lifts and down automatically, keeping the ice rake device on the ice and not buried by the ice. It automatic goes down when delivering the ice and sends the ice out. |
|  |  | Hoist motor Hoist device | 0.25 Hot galvanized | kw |
| 4. | 1 Set | Ice bin door device |
|  |  | Over the ice storage width, the storage door closes when it accumulates the ice and opens when it discharges the ice. There is a plastic glass fitting to control the ice height on itself height. |
|  |  | Ice block motor Ice block plate | 0.75 Hot galvanized | kw |
| 5. | 1 Set | Air cooling system in the ice storage |
|  |  | Keep the storage temperature at -8℃ to ensure the ice is dry and easy to be conveyed. Including shell water cooled condenser, necessary refrigerating fittings and automatic defrosting system. |
| 6. | 1 Set | Horizontal screw |
|  |  | Power Delivery capacity | 2.2 16 | Kw T/hrs |
| 7. | 1set | Automatic control system |
|  |  | Integrated with ice maker, ice storage and delivery system. By using Germany SIEMENS PLC to make fully control, including setting remote ice delivery control to be convenient using. |

Part-3     Screw Ice Conveying System (TSL1610)

| 1 | Diameter | Φ323mm |
| --- | --- | --- |
| 2 | Length | 10m |
| 3 | Obliquity | 0°～+30° |
| 4 | Weight | 1.3T |
| 5 | Ice delivery capacity | 15T/H |
| 6 | Power | 9.2KW |
| 7 | Surface treatment of screw | Antifriction coating surface treatment |

Exclusions (The buyer is responsible for the following parts) :

The Buyer shall make available or supply the following 20 days prior to erection:

1. One set of complete gas welding, such as meter, welding head, valve, gas pocket and so on. supply of water, electricity to positions of equipment in the workshop according to the Seller's design. Electrical line which connect the generator with control panel.

2. Supply hoist , materials and installation of lighting, ventilation, fire-protecting system, and other common systems at the plant area and inside of the workshop.

3. Gas supply i.e. air pump/compressor pump with 0.6MPA

4. Responsible for all civil engineering construction as per the drawings provided by seller

5. Pave the drain pipe for ice storage.

6. 5-6 skilled workers which contains 2 welders and 1 electricians.

7. Refrigerant gas R404A.

8. Supply boarding and lodging, traffic for Snowkey installation teams and engineers during installation.

9. Any other item specifically not included in the above offer.