FORWOOD

PROJECT  REPORT

Reporter: ANHUI FORWOOD Drying Equipment Co., Ltd.

Project:  100，120M3 Aluminum Panel Timber Drying Kiln（steam kiln）

墨西哥客户

CONTENTS

- Project in Brief  ﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍2

2  Technical Specifications   ﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍4

3  Introduction to the Equipment   ﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍5

4  Detailed List of the Equipment ﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍7

- After-Sales Service  ﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍11

Project in Brief

This report was presented for User’s reference as a special scheme through our institute’s thorough study based on User’s individual requirements and our product’s characteristics.

# Configuration Scheme

Type of the Equipment:    FW-100,120

Timber Capacity:         100M3,120M3

Number of the Equipment:  2Unit

Method of Loading:       Forklift loading

Housing Construction:     Aluminum panel

Total Power:             18.0 KW，21kw

Heating Mode:           steam

# Civil Engineering system

Provided by FORWOOD:

- A complete set of working drawings for the foundation

- Technical guidance during the period of construction

User’s Responsibility:

- Complete all foundation construction according to working drawings

- Complete laying of all embedded parts according to working drawings

# Electric Power System

Provided by FORWOOD

- General control panel and cables connected to the panel

- Sub-panels for each kiln and cables and other facilities connected to them

Provided by User:

- Cables from the mains to the general control panel

- Earthing system for each panel

# Heating Power System

FORWOOD’s Responsibility:

piping from the boiler to the kilns and backwater piping to the boiler

Provided by USER:

All other piping and facilities will need for the boiler

# Quotation for the Equipment(FOB-SHANGHAI)

All Components for a Single Kiln:

Total price for one unit of kiln (steam heated):    100M3   29000USD/set

120M3   31000USD/set

Two  kilns total price ：                    60,000USD

The seller will send persons to install the kiln on site at the requirement of the Buyer. The freight and the boarding of the persons seller send will be afford by buyer, and $60 will paid to each person one day.

# Payment Terms

The Buyer should pay to Seller 30% of the total price as the deposit when this contract comes into effect.

The Buyer should pay to Seller 70% of the total price with in three days after shipment against BL.

# Date of Shipment

Shipment shall be effected within 40 days from the date of the Seller’s receipt of the Buyer’s deposit.

Technical Specifications

Type: FW-100

Kiln Cavity Dimensions:

Depth: 7500mm

Width: 8300mm

Height:5600mm

Stack Dimensions:

Number of Stacks:

Depth of a Single Stack: 4800mm

Width of a Single Stack: 7500mm

Height of a Single Stack: 3900mm

Theoretical Timber Capacity: 100m3 (Theoretical Timber Capacity was

calculated on the basis of 50mm thick edge-trimmed boards and with the fillet of 25mm thick)

Number of Fans: 6

Maximum Air Volume of a Single Fan: 32000m3/h

Working Air Volume of a Single Fan: 27000M3/h

Electric Power of a Single Fan: 18.0kw

Heat-Transfer Material: 150℃ steam

Type: FW-120

Kiln Cavity Dimensions:

Depth: 7500mm

Width: 10000mm

Height:5600mm

Stack Dimensions:

Number of Stacks:

Depth of a Single Stack: 4800mm

Width of a Single Stack: 9150mm

Height of a Single Stack: 3900mm

Theoretical Timber Capacity: 120m3 (Theoretical Timber Capacity was

calculated on the basis of 50mm thick edge-trimmed boards and with the fillet of 25mm thick)

Number of Fans: 7

Maximum Air Volume of a Single Fan: 32000m3/h

Working Air Volume of a Single Fan: 27000M3/h

Electric Power of a Single Fan: 21.0kw

Heat-Transfer Material: 150℃ steam

### Introduction to the Equipment

#### Control System

The controller model Delphi is a modern electronic device, made with the newest materials, which is able to do, in a totally automatic way, the complete drying cycle required by a large number of timber groups. The project of this system has been realized in order to couple the most advanced functions with the easiest simplicity of use: there is one special key for each function that can be recognized by a symbol. Furthermore, to simplify the operations, a new system based on chip-cards has been introduced, which allows the user to record on cards the most used programs, personalized according as the type of kiln dryer and the timber group, which can be set up on the machine only by inserting the card into the card reader.

Technical Specifications:

Measurement and Control Range of Temperature:   0-100℃

Measurement and Control Range of Humidity:      3-30%

Measurement Range of Moisture Content of Wood:  4-80%

Heating System

The heating system is composed of electromagnetic heating valve, bimetallic (stainless steel/aluminum) ribbed heat-exchanger coils, cut-off valve and piping.

The heating system can meet different drying requirements from medium-low temperature schedule to medium-high temperature schedule with its strong heating power.

#### Spray System

The spray system is composed of spraying valve, cut-off valve, stainless steel spray pipe.

The spray pipe is made by stainless steel so that the carbon steel pipe’s drawbacks of heavy corrosion and short service life can be effectively avoided.

#### Air Circulating System

The optimum model of kiln is adopted with circulating fans located on the upper side of the kiln. The No. 8 fan is aluminum molded with big air volume and high efficiency. The electrical power for a single fan is only 3.0Kw so that the energy consuming and the drying cost can be substantially lowered. As the symmetrical blades can ensure the same amount of the air volume and the air pressure no matter the fan is in normal direction of rotation or in contra rotation, the reversible fan guarantees the uniformity of air velocity and air temperature at the cross sections of the stack so that the uniformity of the wood moisture content at the cross section of the stack is greatly improved.

The ceiling is built using LF21 anti-corrosion corrugated aluminum panel that its strength, stiffness and corrosion resistance are substantially improved.

# Venting System

To realize the fully modulating operation, the aluminum air dampers are controlled by the vents actuator via the driving mechanism and the vents actuator in turn is controlled by the main control system.

#### Kiln Door System

The popular one-piece sliding aluminum alloy doors are furnished. The door has a welded steel framework with a double insulation using polystyrene. The door is sealed with custom-tailored special-shaped rubber tube which is heat-resisting, anti-aging and highly airtight.

Besides sliding on the top track the door carrier is also supported by a floor rail, which ensures it operate easily, smoothly and steadily.

Detailed List of the Equipment (for one unit)

#### Control System

1-1. Wood Drying Controller      1 set

Type:  DELPHI             HOLZMEISTER Delphi

Place of Production:    Italy

Technical Specifications:

Measurement and Control Range of Temperature:  0-100℃

Measurement and Control Range of Humidity:     0-100%

Measurement Range of Moisture Content of Wood:  4-60%

Power:  30W

Environmental Specifications:

Input Voltage: 220+10%AC

Working Temperature: 5-50℃

Working Humidity: 35-75%

Auxiliary Parts:

Temperature and humidity transducer and wire    1 set

Measurement probe of moisture content of wood  12 pieces

Measurement plug of moisture content of wood   12 pieces

EMC sets transducer and wire                 6 sets

1-2. Control Panel

Type:               FW-EC

###### Air Circulating System

2-1. Fan                  6sets.7sets

Type:                8#

Place of Production:    FUJIAN

Technical Specifications:

Maximum Air Volume: 32000M3/h

Working Air Volume: 27000 M3/h

Working Air Pressure: 20mmH2O

2-2. Motor                 6sets.7sets

Type:  100 Series

Technical Specifications:

Rated Voltage: 380±10%AC

Rated Current: 5A

Rated Power: 3.0Kw

Insulation Grade: H

Protection Grade: IP55

Place of Production:    FUJIAN

Environmental Specifications:

Maximum Working Temperature: 120℃

Maximum Working Humidity: 100%

The Way of Working: Continuous

2-3. Fan Rack             1 set

Place of Production:    FORWOOD

Material: Shaped aluminum alloy

2-4. Ceiling                1 set

Place of Production:    FORWOOD

Material: 1.0mm corrugated aluminum alloy plate

###### Heating System

3-1. Bimetallic Heat- Exchanger Coils   4sets

Place of Production:    FORWOOD

Technical Specifications:

Fin Type: Rolled

Fin Material: Aluminum Alloy

Tube: Stainless steel tube

Heat-Exchanging Area:    300M2,， 360M2

3-2. Internal Piping       1 set

Place of Production:    FORWOOD

Material: Seamless steel tube

3-3. Electromagnetic heating Valve

Type: 40

Place of Production:    CHINA

Technical Specifications:

Standard: 40

Working Voltage: 220V/AC

Maximum Allowed Working Temperature: 200℃

Working Pressure: 0.3-10Kg/cm2

3-4. External Piping and Valves  1 sets

Place of Production:    FORWOOD

Material: Seamless steel tube

## Spray System

4-1. Electromagnetic Spray Valve          1 piece

Type: 20

Place of Production:    CHINA

Technical Specifications:

Standard: 20

Working Voltage: 220V/AC

Maximum Allowed Working Temperature: 200℃

Working Pressure: 0.3-10Kg/cm2

4-2. Internal Piping       1 set

Place of Production:    FORWOOD

Material: Stainless steel tube

4-3. External Piping and Valves  1 set

Place of Production:    FORWOOD

Material: Seamless steel tube

## Venting System

5-1. Venting Motor         2 set

Type: SIEMENS

Place of Production:    Germany

Technical Specifications:

Input Voltage: 220V±10%/AC

Power: 4W

Output Torque: 15NW

Maximum Load Area: 4M2

5-2. Venting Duct          8 sets， 10 sets

Place of Production:    FORWOOD

Material: Aluminum Alloy

Standard:  300X300

5-3. Driving Mechanism     2 sets

Place of Production:    FORWOOD

Material: Seamless and stainless steel tube

## Door System

6-1. Door

Type: FW-

Place of Production:    FORWOOD

Standard: 8400×4450mm,10100×4450mm

Material:

Rim: Shaped aluminum

Frame: Shaped Aluminum

Insulation Material: insulation layers

Sealing Material: custom-tailored special-shaped rubber tube

Auxiliary Parts:

Door Case: Shaped aluminum alloy

6-2. Inspection Door        1 set

Place of Production:    FORWOOD

Standard: 1600×600mm

Auxiliary Parts:

Door Case: Shaped aluminum alloy

6-3. Door Carrier:          1 set

Type: Sliding and supported with floor rail

Place of Production:   FORWOOD

## Housing

7-1. Post, Beam, Truss

Material: Shaped aluminum or Shaped steel

Place of Production:        FORWOOD

7-2. Wall

Internal Wall Panel: Aluminum plate

Type: 1.2mm

Place of Production:  FORWOOD

External Wall Panel: corrugated Aluminum plate

Type:0.8mm

Place of Production:    FORWOOD

Insulating marterial: Fiber glass

Thickness: 100mm

7-3. Control Room

Material: Polystyrene panel

##### After-Sales Service

## Installation and Trial Run

Our engineers and technicians coordinating with the User’s personnel shall complete all installation and shall be responsible for the trial run until all equipment run well.

## Technical Training

We shall train the kiln drying operators for Users free of charge on site or in our company. The experts from the Institute of Drying Technology shall give lessons in drying mechanism and operating rules to make the operators have a real grasp of the wood drying technology and be skilled in wood drying.

## Maintenance and Technical Service

- We shall give prompt maintenance service to our Users by email and phone.

2.  We shall provide spare parts at the best price.

3.  We shall provide free latest wood drying technology for our Users and can provide particular technical service according to User’s individual requirements.