Questionnaire for ordering filter centrifuge

| No | Questions | Answers |
| --- | --- | --- |
| Characteristic of the product to be treated on a centrifuge |
| 1. | Water medium | Aqueous solution of sodium tungstate (Na2WO4) |
| 2. | Name, chemical composition, proportion of solid | Base - magnesium hydroxide Mg(OH)2 –70%, silicon hydroxide Si(OH)4 – 15%, tungstic acid H2WO4 – 13 %, magnesium phosphate Mg3(PO4)2 – 2%. Specific weight of wet cake (50% Н2O) – 1300 kg/м3 |
| 3. | Concentration of solid, % by weight | 20-50 |
| 4. | Particle size of solid, μm | 5-80 |
| 5. | Chemical composition, pH, proportion of liquid | С (Na2WO4)=(50-80) g/l, С (Na2SO4)=(20-50) g/l, С (NaOH)=(3-10) g/l, рН=(9-12) unit, ρ=(1,12-1,18) g/l. |
| 6. | Temperature of the suspension when entering the centrifuge, оС | 15-40 |
| 7. | Abrasive properties of sludge | No |
| 8. | Toxicity, flammability and explosiveness | No |
| Purpose and performance of centrifuge |
| 9. | The purpose of centrifuge and its place in the technological scheme of the enterprise | Filtration of thickened pulp of sodium wolframate of settling-thickening tank |
| 10. | Required productivity for slurry m3/h, dry t/h | ≈ (1-3) ≈ 0,05-0,1 (dry) |
| 11. | Required final humidity of precipitateа, % масс. | 30 |
| 12. | Sludge washing | Wash the sediment with hot water (up to 70 оС), removal of supernatant and washing water |
| Operating conditions of centrifuge |
| 13. | Mode of operation of centrifuge: continuous, periodic, duration | Intermittent 10-12 hours |
| 14. | Place of installation of the centrifuge | Industrial heated room |
| 15. | Requirements for the electric motor working (open, protect, explosion-proof), main voltage | IP54 |
| 16. | Installation place in the building, way of centrifuge feeding and residue discharge | On process area under settling-thickening tanks, pulp feeding-nature flow, residue discharge –low. The height of centrifuge- no more than 1500mm |