WEIFANG DRAGON MACHINERY TECHNOLOGY CO., LTD

DRAGON RUBBISH SALVAGE BOAT

MODEL:  DGTSB-40

Weifang. China

2018-06-03

Quotation

Description                                                               Quantity             Unit Price                     Total Price

------------------------------------------------------------------------------------------------------------------------------------------

DGTSB-40 RUBBISH SALVAGE BOAT              1 set           USD 210,000/SET         USD 210,000

------------------------------------------------------------------------------------------------------------------------------------------

Total ( FOB QINGDAO, CHINA)                                                                                        USD 210,000

SAY: US DOLLARS TWO HUNDRED AND TEN THOUSAND ONLY.

REMARKS:

- Payment Term:

30% of the total payment should be paid by T/T as deposit;

The balance should be paid before delivery by T/T or L/C at sight.

2. Delivery time: 100 days after receiving the L/C.

3. Delivery method：By bulk vessel

4. Warranty: 12 months.

5. Beneficiary Information:

BENEFICAITY NAME: WEIFANG DRAGON MACHINERY TECHNOLOGY CO., LTD.

ACOUNT NO.:4580 0000 1142 0100 0147 97

BANK NAME: CHINA ZHESHANG BANK, WEIFANG BRANCH

SWIFT CODE: ZJCBCN2N

Arrangement in whole

You can see the following arrangement from foreword to end of the boat:

------Collecting Arm

------Front Collecting Conveyor

------Hull

------Material Hopper

------Baler

------Storage Area

------Jib Crane

------Operation Cabin

------Hydraulic Engine and Hydraulic Pump

------Hydraulic Oil Tank and Fuel Tank

------Main Engine

------Gearbox

------Cooling Pump and Sealing Water Pump

------Propeller

------Toilet

Specification List

| Ser | Description | Required Specification | Remarks |
| --- | --- | --- | --- |
| A | Manufacturer | Weifang Dragon Machinery Technology Co., Ltd |  |
| B | Brand | Dragon | Registered Brand |
| C | Model | DGTSB-40 |  |
|  | 1. Principle Dimensions |  |  |
|  | (1) Length Overall | 20 m |  |
|  | (2) Width Overall | 5.0 m |  |
|  | (3) Height Overall | 4.9 m |  |
|  | (4) Draft Empty / Fully Load | 0.9m / 1.5m |  |
|  | (5) Collection Width | 4.0 m |  |
|  | (6) Collection Depth | 1.2 m |  |
|  | (7) Carrying Capacity | 10 tons |  |
|  | (8) Deigned Working Speed | 3 km/hr |  |
|  | (9) Sailing Speed | 20 km/hr |  |
|  | (10) Total Installed Power | 274 kw |  |
|  | (11) Drive Mode | Hydraulic System |  |
|  | 2. Hull |  |  |
|  | (1) Length | 18 m |  |
|  | (2) Width | 4.5 m |  |
|  | (3) Height | 2.0 m |  |
|  | (4) Type | Integrated Hull |  |
|  | (5) Plate Thickness- Deck | 6 mm | Carbon steel, CCSB Grade |
|  | (6) Plate Thickness- Sides | 5 mm | Carbon steel, CCSB Grade |
|  | (7) Plate Thickness- Bottom | 6 mm | Carbon steel, CCSB Grade |
|  | 3. Propelling Engine |  |  |
|  | (1) Manufacturer | Cummins |  |
|  | (2) Model | NT855-M |  |
|  | (3) Rated Power with RPM | 224 KW @ 1800RPM |  |
|  | (4) Amount | 1 set |  |
|  | Propeller Diameter | 800 mm | Driving through Gearbox |
|  | Propeller Material | Copper Alloy |  |
|  | 4. Hydraulic Engine |  |  |
|  | (1) Manufacturer | Weichai Deutz |  |
|  | (2) Model | TD226B |  |
|  | (3) Rated Power with RPM | 50 KW @ 1800RPM |  |
|  | (4) Amount | 1 set |  |
|  | Hydraulic Pump Type | Gear Pump |  |
|  | Hydraulic Pump Amount | 1 set Twin Pump |  |
|  | Baler Machine |  |  |
|  | Power | 15 Kw |  |
|  | (2) Bale Size | 300x300x600 mm |  |
|  | (3) Bale Weight | 25-30 kg |  |
|  | Baling Speed | 80-100 bales/hour |  |
|  | Weight | 2.6 T |  |
|  | Baling Method | Continuously baling and packed in nylon bags |  |
|  | 6. Hydraulic System |  |  |
|  | a. Hydraulic Pump |  |  |
|  | (1) Type | Twin Gear Pump |  |
|  | (2) Working Pressure | 16 Mpa |  |
|  | (3) Amount | 1 set |  |  |
|  | b. Hydraulic Tank |  |  |
|  | (1) Capacity | 1000L |  |
|  | (2) Accessories | temperature & level gauge are provided |  |
|  | c. Hydraulic System Protection | Relief valves, low oil & clogged filter sensors shall be provided for better working of the hydraulic system. |  |
|  | d. Location | In the front of the hull |  |
|  | e. Operation Panel | Switches, gauges, warning lights & alarms are provided. |  |
|  | 7. Pilot Cabin |  |  |
|  | (1) Type | 360 degree view stable cabin |  |
|  | (2) Captain Chair | Adjustable chair with Operation Sticks |  |
|  | (3) Operator Protection | All hydraulic lines / valves enclosed & shielded for better safety of operator. |  |
|  | 8. Navigation System |  |  |
|  | a. Radar | Brand: Lowrance, USA | Specification in attachment 1 |
|  | b. VHF | Brand: ICOM, Japan | Specification in attachment 2 |
|  | 9. Lighting System |  |  |
|  | (1) Lights Type | 500w spotlight: 2 pcs 65w floodlight: 6 pcs |  |
|  | (2) Signal Mast | Signal lamps required for navigation is to be provided. |  |
|  | 10. Conveyor Belting |  |  |
|  | (1) Type | Stainless Conveyor |  |
|  | (2) Conveyor Width | 1.8m |  |
|  | (3) Driven | Hydraulic Motor |  |
|  | (4) Collecting Mouth Width | 3.8 m |  |
|  | Collecting Arm Control | By hydraulic cylinders |  |
|  | 11. Frame |  |  |
|  | (1) Material | CCSB Marine Steel |  |
|  | (2) Fasteners | Stainless steel |  |
|  | (3) Anti-corrosion | 4 layers marine epoxy paint; Zinc anode protection. |  |

Designing Pictures