电话Tel: 0086-13587572818 传真Fax: 0086-577-65567266邮箱Email: Joy@sinceremachine.com

地址     Add: Songjiadai Industrial park, Feiyun Town, Ruian City, Zhejiang Province, China

浙江省瑞安市飞云镇宋家埭永定路7号

ZBJ-09 AUTOMATIC MID-SPEED PAPER CUP MACHINE

全自动中速纸杯机

简介：

ZBJ-09型中速机成型机是一种多工位高速自动机械，具有自动送纸，热封成筒，杯口润滑，冲杯底并按放杯底，杯底加热，滚压，上口卷边，成品吹送等连续工序，生产单双面淋膜冷热饮纸杯，冰淇淋杯。

ZBJ-09 MID-speed paper cup forming machine is a multi station high-speed automatic machine producing both single and double PE coated drink cups,ice cream cups through continuous process of automatic paper  feeding,sealing,oil injection,bottom cutting,heating,knurling,curling and stacking.The machine adopting hot air system,PLC control,servo motor driving,full-automatic failure warning,counting,detection,stopping,etc.

技术介绍：

1、采用凸轮和齿轮传动系统，解决了传统转动箱和链条传动带来的弊端，机器在高速运转下更加稳定。

2、采用无焰热风系统，生产效率更高。

3、采用环抱型钢架结构，机器结构紧凑、固定。

4、零部件全部采用标准化生产，通用性强，互换性能好，便于设备维修。

5、采用全自动封闭润滑系统，可保证机器长时间无间断的高速运转。

6、机型小巧，便于输送和放置

Leading technology:

1.Adopt open CAM and gear transmission system.machine run stably under high speed operation.

2.Using hot air heating system, to keep cups no leaking under high speed.

3.The parts are all made of standardized production,strong commonality,swap performance is good,easy to maintenance.

4.The automatic lubrication system,closed,can ensure the machine long time continuous high-speed operation.

5.Intelligent design,PLC automatic control,automatic fault alarm,count.testing,and stop action.

6.The machine is a compact paper cup machine helping clients to save 60% shipment cost.

主要技术参数 main technical parameter

| 纸张要求 paper request | 170-350g/m2 |
| --- | --- |
| 电源 VOLTAGE SUPPLY | 220V50HZ/380V50HZ or customized |
| 纸杯尺寸 cup size | 1.5-9oz |
| 速度SPEED | 70-80pcs/min |
| 总功率 general power | 8.5KW |
| 重量 weight | 2000KGS |
| 外形尺寸 measurement | 2.2*1.15*1.7M |
| FOB Ningbo price | 17000USD |

机器图片 machine picture

售后 after sale service：

A guide book is included to assist with the installation and machine adjustment process and help solve any problems that may be encountered.

1. The machine is adjusted one week prior to delivery to make sure our Lifeng machine is in perfect condition.

2. Technicians are available to guide the installation and adjust the machine at the buyer’s factory. This service would be at the buyers expense and include the technician’s salary, transportation, accommodations, consultation, etc.

3. Free training is available and ongoing for the buyer until he fully understands the operation of our Lifeng machine .the buyer would be responsible for airfare and accommodations expenses.

操作手册应该包括专辑，调试，以及如何解决有可能会发生的问题

- 机器需发货一周前进行调试，确保机器完善

- 技师可以去工厂调试（国外客户需支付旅费，食宿费,出国手续费，一天补贴100美金，国内保修内不用）

- 技师会提供调试，培训服务，直到买方理解，能操作

- 易损件一年内免费更换

质保Warranty:

1.Lifeng  machine offers a one year warranty from the shipment date.

2.The Lifeng warranty is not applicable to parts requiring normal replacement.

3.Lifeng is not responsible for any damage caused by misuse, improper handling, negligent maintenance, intentional injury or other damages.

- 保修期一年（从发货开始算起）

- 保修不包括调换的配件

- 对因人为造成的损坏，公司将不负责