Thanks for your inquiry, here is the machines quote, look forward to hearing your feedback suggestion.

Product name/specification:CR-3280Double shaft shredder

Unite price:285000.00(RMB)

QTY:1set

Technical parameters:

Power: 3-phase, 380V  50HZ

Motor: 40HP*2

Gearbox: two set heavy ZQ650 gearbox

Crushing room size: 800*600mm

Feeding size:960*760mm

Knife quantity: fixed one is 19 pieces, rotated one 19 piece

Rotated knife size:Ø320*40mm

Knife material:SKD-11

Rotated speed:15/20RPM

Machine overall size:L3350*W1600*H2800MM

Equipped with overheat protector, avoid motor get broken when motor overload.

Equipped with reverse rotation function, extend knife and motor’s service life.

Structural characters:

Double-blade shaft structure: adopt multi-chip and multi-claw cutting tool, can change the angle when cooperated with cutter shaft, which saves cutting energy with strong cutting force and crushing capacity.

Cutting tool is made of special steel and has long shelf life after being hardened through heat treatment. Single blade is replaceable and can be recycled for use after welding.

With drive gear transmission system, the motor is in transmission structure, can operate strongly with low-speed revolution and high torque, and high in crushing efficiency.

Large transmission gear is made of special steel, have long shelf life after being hardened with heat treatment.

By adopting oil lubrication, the gearbox is easy to operate, low in noise, strong in torsion and long and durable to work.

The design of low-speed revolution and high torque allows low noise and low dust emission and can greatly better working conditions.