FORWOOD

PROJECT  REPORT

Reporter:   FORWOOD Drying Equipment Co., Ltd.

Project:   2×120M3 Aluminum Panel Timber Drying Kiln

（Forklift loading steam kiln）

Date:     2021/10/13

To ：   Jario

CONTENTS

- Project in Brief  ﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍2

2  Technical Specifications   ﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍4

3  Introduction to the Equipment   ﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍5

4  Detailed List of the Equipment ﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍7

- After-Sales Service  ﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍﹍11

Project in Brief

This report was presented for User’s reference as a special scheme through our institute’s thorough study based on User’s individual requirements and our product’s characteristics.

# Configuration Scheme

Type of the Equipment:    FW-120

Timber Capacity:          120M3

Number of the Equipment:  2sets

Method of Loading:       Forklift loading

Housing Construction:     Aluminum panel

Total Power:             18 KW/unit

Heating Mode:           150℃ steam

Quantity of heat needed:   25-300000Kcal/h.kiln

# Civil Engineering system

Provided by FORWOOD:

- A complete set of working drawings for the foundation

- Technical guidance during the period of construction

User’s Responsibility:

- Complete all foundation construction according to working drawings

- Complete laying of all embedded parts according to working drawings

# Electric Power System

Provided by FORWOOD

- General control panel and cables connected to the panel

- Sub-panels for each kiln and cables and other facilities connected to them

Provided by User:

- Cables from the mains to the general control panel

- Earthing system for each panel

# Heating Power System

FORWOOD’s Responsibility:

piping from the boiler to the kilns and backwater piping in the kiln

# Quotation for the Equipment(FOB SHANGHAI)

All Components for a Single Kiln:

Total price for one unit of kiln (steam heated):

USD 33,000/set     Price period is 20 days

2kilns total price      USD66,000

Container 1×40HP

Select:

1，Due to the COVID-19 impact, suggest the Buyer's installation,The Seller shall provide drawings.

2，The seller will send persons to install the kiln on site at the requirement of the Buyer. The freight and the boarding of the persons seller send will be afford by buyer, and $70 will paid to each person one day.

# Payment Terms

The Buyer should pay to Seller 30% of the total price as the deposit when this contract comes into effect.

The Buyer should pay to Seller 70% of the total price with in before shipment against BL.

# Date of Shipment

Shipment shall be effected within 40days from the date of the Seller’s receipt of the Buyer’s deposit.

Technical Specifications

Type: FW-120

Kiln Cavity Dimensions:

Width : 11500mm

Depth : 7500mm

Height: 5600mm（ceiling height 4400mm)

Stack Dimensions:

Number of Stacks:

Width of a Single Stack:  11000mm（5×2100mm，or 2×5500mm）

Depth of a Single Stack:  4800mm（4×1200mm）

Height of a Single Stack:  3900mm（3×1300mm）

Theoretical Timber Capacity: 130m3 (Theoretical Timber Capacity was

calculated on the basis of 50mm thick edge-trimmed boards and with the fillet of 25mm thick)

Number of Fans: 6

Working Air Volume of a Single Fan: 30000M3/h

Electric Power of a Single Fan: 3kw

Heat-Transfer Material:150℃ steam