Bale cutter model：80T

Inner cutting length：1200mm

Blade thickness：50mm

Machine weight：3200MM

Cylinder size)：D220mm×d180mm×1350mmdouble cylinder）

Piston rod size)：￠140mmX1480mm

Power380V  50HZ

Motor：15KW-4

Oil pump)：25V 19A  68pm

Manual valve,pressure regulating valve,one-way valve brand is Taiwan HSUTIEN

Price：52000.00元/台(RMB)

This bale cutting machine is suitable for cutting raw rubber or plastic rubber heads and other similar large rubber and plastic products.  It is equipped with a gantry structure frame.  The hydraulic power is a high-pressure and low-speed hydraulic system, which can be adjusted arbitrarily and the working pressure is safe and reliable.  Each type has a variety of models with different pressure levels, manual hydraulic manual liquid level reversing valve, automatic electromagnetic reversing valve and limit safety travel switch.  The  cutting blade is heat-treated and hardened, it can be used for repeated sharpening.