Parameters of 300 dehydrator:

Model：CR-300#

Overall size: L2200*W1000*H2800

Standard size: Ø300*L2000

Motor power: 7.5kw

gearshift method：Pulley proportional speed change

Rotary speed: 约1000RPM

handling capacity：600KG/H

Material：Inner parts and screen are stainless steel

unit price：5800.00（USD)

Suitable for plastic crushing materials, raw materials, sheet dehydration and air drying reuse.

The machine is made of stainless steel, including screen mesh, blade and spindle side plate.

The transmission part adopts triangular belt transmission, and the centrifugal starting wheel is directly driven by the motor, which can make the machine start slowly and gradually reach the design speed to ensure the smooth operation of the machine.

The spindle is made of stainless steel after heat treatment.

Spindle dynamic balance check to ensure the smooth operation of the equipment.