SL-1080    Eight-head color changer

Руководство по эксплуатации

A. Упаковка

※ SL-1080 Eight-head color changer x 1pcs

※ Cable x 1pcs

※ Manual x 1pcs

B. Установка

※Please hang this light into the suitable place with suitable angle (if operate this light in external place, please remember to get some water-proof cover to protect them)

※ To connect the cable and put into power, then the light stay in the status to receive the operating signal like: music, Automatic, DMX512 etc. Take note: Please cut off the power line if you will not operate it for a certain time.

※ To connect the signal cable, plug one side into “ IN” socket in the back of light and plug another side into “ OUT” signal connector in the DMX512 board, (signal input: 1=>Ground,  2=>data-,  3=>data+ )

C．Функция：

1．Automatic model(stand alone):7 color change/7 color strobe/7 color Automatic changing /7 color automatic fade in and fade out/ 7 color chase/ sound color changing

2．Synchronization model (master and slave)

3．Special manual controller ( please read SL-1080-C operation manual)

4．DMX-512 Model

D．Техническое обслуживание  。

- Use the soft cloth to clean the light and check if the screw is loose or not during certain period, if loose, please fix them tightly

E．Рабочее место

※Indoor, temperature:：-20—45℃  ※humidity：0％－90％

F．Подробная функция, как показано ниже:

※ Auto：（Dip switch as below） ● means “on” status。◎ means “OFF”status

| function |  | №1 | №2 | №3 | №4 | №5 | №6 | №7 | №8 | №9 | №10 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | red | ● | ◎ | ◎ | ◎ | ◎ | ◎ | ◎ | ◎ | ◎ | ◎ |
| 2 | green | ◎ | ● | ◎ | ◎ | ◎ | ◎ | ◎ | ◎ | ◎ | ◎ |
| 3 | blue | ◎ | ◎ | ● | ◎ | ◎ | ◎ | ◎ | ◎ | ◎ | ◎ |
| 4 | strobe | Speed 1 | Speed 2 | Speed 3 | Speed 4 | ● | Red:off/on | Green: off/on | Blue: off/on | ◎ | ◎ |
| 5 | fade in and fade out | Speed 1 | Speed 2 | Speed 3 | Speed 4 | ◎ | ● | ◎ | ◎ | ◎ | ◎ |
| 6 | Auto. | Speed 1 | Speed 2 | Speed 3 | Speed 4 | ◎ | ◎ | ● | ◎ | ◎ | ◎ |
| 7 | Chase light | Speed 1 | Speed 2 | Speed 3 | Speed 4 | ◎ | ◎ | ◎ | ● | ◎ | ◎ |
| 8 | Sound activated strobe | ◎ | ◎ | ◎ | ◎ | ◎ | ◎ | ◎ | ◎ | ● | ◎ |
| 9 | Sound activated color change | ● | ◎ | ◎ | ◎ | ◎ | ◎ | ◎ | ◎ | ● | ◎ |

Remarks: function 1. 2. 3 will be fold to run 7 color, function 8, 9 will adjust the music sensitivity via potentiometer knob.

Speed 1 mean slowest ,  Speed 4 mean fastest

※Synchronization /master and slave (dip switch as below):

Master light: dip switch same as auto model way, all slave lights: press NO.1 and no10to”ON”, other NO2-NO9 stay on “ OFF” status

※ Special manual controller:

Please connect the controller with the light through a XLR3 pin cable, dip NO1 and No10 switch to “ ON” status for all units, other NO2-NO9 switches are stay “ off” status”。

※DMX-512 Model

Press “10” to “ ON” status to receiving DMX signal, 1-9 are selectable code, refer below:

● means “ on” status

| №1 | №2 | №3 | №4 | №5 | №6 | №7 | №8 | №9 | №10 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | ● |

This light have 29 DMX512 channels, please reference the below function channels:

CH 1: function selecting:

| digital | 0~40 | 41~80 | 81~120 | 121~160 | 161~255 |
| --- | --- | --- | --- | --- | --- |
| function | dimmer | strobe | light in and light out | auto. Color change | chase light |

CH2:

| Stay in dimmer function | Stay other function |
| --- | --- |
| 0~255 adjustable luminance | 0~255 adjustable speed |

CH 3:

|  | Stay in dimmer and strobe function | Stay in chase light function |
| --- | --- | --- |
| digital | 11~255 | 0~10 | 0~30 | 31~255 |
| effect | Red color dimmer | Off red color dimmer | Auto running all functions | Have one effect per 30 |

CH 4:

|  | Stay in dimmer and strobe function |
| --- | --- |
| digital | 11~255 | 0~10 |
| effect | Green color dimmer | Off green color dimmer |

CH5

|  | Stay in dimmer and strobe function |
| --- | --- |
| DIGITAL | 11~255 | 0~10 |
| effect | blue color dimmer | Off blue color dimmer |

CH6-CH29 are the adjustable brightness from head 1 to head 8 in red, green and blue color,

distributing digital: 0-255

G．Технические характеристики:

- Input power:AC100～240V/50-60Hz

- Total power: 50W

- LEDs: red / 320pcs, blue / 144pcs, green / 144pcs

- House size：110×14×12cm

- Net/weight：7.3Kg

- 1pcs/carton: 118 x 20 x 20 cm

- Gross/weight：8.4Kg

- Shipping size( 4pcs/master carton): 120×42×44cm

- Gross/weight：35Kg