1]  EXTRUDER   SJ-A75         SPECIFICATION 
FEATURE--material to be used  HDPE LDPE 
              max film width  500-1500MM 
              Firm thickness - 0.008-0.08mm 
             max extrusion  output  30-120kg/h 
             screw  diameter - 75mm 
EXTRUDER--- screw  L/D ratio 28:1 
                  main motor 37kw From Siemens , with Delta inverter 
                 heating motor  27kw 
                blown  firm  dies :200mm,350mm with rotary die head 
CONTROL PANEL--TYPE- independent or attached type switch board 
                            temperature control --5 points 
COOLING UNIT-  TYPE- external air cooling by dual air ring 
                                 
TAKE UP UNIT-  TYPE -height  adjustable type 
                               roller width 1600mm 
                             take up speed- max 70M/min 
                             bubble guide 
                             take up motor 1.5kw  with frequency inverters 
                           steady  plate -with gusset board 
                          winding station – double winders 
                          effective   width   1500mm